## Slide 1
Proposed Type Differentiation Criteria for the Cyber Security and Software Update Interpretation Documents
TFCS-xx-xx

## Slide 2: Example of changes in the E/E Architecture
Development of an E/E Architecture requires a new type.
Change of outcome of risk assessment by introducing new technologies
No change of outcome of risk assessment
Requires a new type, since security in existing subsystem is being influenced.
Replacing an existing subsystem, and this does not change the cybersecurity of the resulting E/E architecture, and thus does not require a type extension. This is the usual situation.
Development of a new E/E Architecture
Possible changes in the E/E Architecture
Replacing an existing subsystem or adding a new subsystem, and this introduces some minor changes to the cybersecurity of the resulting E/E architecture, and thus requires an type extension.
New type
Extension of existing type
No impact
New Type or Type Extension
Changes of outcome of risk assessment by adding or replacing subsystems
Development of an E/E Architecture requires a new type.
Adding new external interfaces (NFC Near Field Communication) for new services such as personalization
Change of network topology by adding a new gateway
Replacing an ECU:
new state of the art processor, more memory, no new functionality,
different supplier
.
Examples
Replacing a UMTS communication unit by a 5G communicaiton unit -> additional communication possible
Replacing a ECU by a new one with a HSM (hardware security module)

## Slide 3: Suggested addition to the interpretation document Cyber Security
New Type
Type Extension
Development of a new E/E architecture or fundamental change(s), that influences security in the existing E/E architecture.
Changes that can occur with the introduction of an additional subsystem or the replacement of an existing subsystem that have minor impact to the cybersecurity of the existing E/E architecture.

## Slide 4: Vehicle type, new type and type extension for software update processes regulation
Vehicle type:
The vehicle type for the system approval for software updates comprises of the technical means used to provide a software update via cable, remotely or by any other means; independent of the update purpose e.g. due to a recall, a bug fix or providing a new feature to the customer.
New Type
Type Extension
A new technical way of providing software updates.
Changes in the means to protect integrity and authenticity of the update.
Changes in the way of reading and protecting the RXSWIN.
Changes in way of ensuring safe state of the vehicle in case of remote updates.
Changes in ways of informing the vehicle user about a software update.