## Slide 1: PEV low temp family concept, Low temp concept application for all EVs Status: 14.05.2020 (after discussion within SG EV)
EV Low temp family concept

## Slide 2: Proposal PEV Low Temperature Family concept
Parameter | Example | Boundary conditions when merging
Capacity of battery (same type of REESS, overtake IP family but strike out some criteria like capacity; range between capacities need to be limited due to thermal effects) | x kWh | Higher capacities can be covered lower capacities Note: in case of merging vehicles with different capacities, the selected vehicle for Type 6 testing shall have lowest capacity of the merged capacities
Battery preheating | Available/not available | Vehicles with preheating can be covered by vehicles w/o preheating Note: in case of merging vehicles with and w/o preheating, the selected vehicle for Type 6 testing shall be w/o preheating
Battery insulation (thermal) | Type of insulation | Batteries with more insulation can be covered by a batteries with less insulation Note: in case of merging vehicles more and less insulation, the selected vehicle for Type 6 testing shall the less insulation of the merged insulations
UBE (ratio) family  Family from which the vehicle for the UBE determination shall be selected from:
Current discussed proposal: Highest cycle energy demand Vehicle H of the UBE family
To be discussed
Note: Positive effect on range, negative impact on energy consumption as EAC is required for calc.  can it be really merged?  What is the worst case?
EC/Range (ratio) family  Family from which the vehicle for the range/EC ratio calculation shall be selected from:
Current discussed proposal: Most energy consuming vehicle of the UBE family
Proposal: Most energy consuming vehicle of the EC/range (ratio) family
Parameter | Example | Boundary conditions when merging
Energy consumption: Most energy consuming heater configuration and the worst case powertrain in terms of EC (combination of motor(s), transmission, no. of powered axles, energy converters, operation strategy and n/v) | Wh/km | Less energy consuming can be covered by more energy consuming vehicles
Note: description quite vague, clearer definition and guidance is required for most electric energy consuming config. E.g. use IP family criteria + additional low temp criteria as basis for definition Furthermore: can the vehicle this vehicle be used for the UBE determination as well?  Would reduce the mandatory testing for manufacturer in case the highest cycle energy demand vehicle H is not the most energy consuming config. Not only heater is influencing energy consumption but also vehicle config.

## Slide 3: Proposal PEV Low Temperature Family concept application (parent and member vehicle concept)
Sufficient to measure only the parent1 vehicle
if parent1 vehicle is the highest cycle energy demand vehicle H of the UBE family
if parent1 vehicle is the most energy consuming vehicle configuration of the EC/Range family
Parent1 vehicle covers all remaining vehicles in the UBE and EC/range family.
Parent1 vehicle: for EC/range-ratio determination PERparent1,-7°C = ECparent1,-7°C =
Calculation of Ratioparent1_PER =
Calculation of Ratioparent1_EC =
Ratioparent1_PER, Ratioparent1_EC
Remaining vehicles in UBE (ratio) vehicle:
PERmember,-7°C = PERmember,23°C * Ratioparent1_PER ECmember,-7°C = ECmember,23°C * Ratioparent1_EC
Both parent1 and parent2 vehicle are required to be measured mandatory
if parent vehicle is the highest cycle energy demand vehicle H of the UBE family
if parent vehicle is not the most energy consuming vehicle configuration of the EC/Range family
Measurement of parent1 vehicle  UBE ratio determination
Measurement of parent2 vehicle  EC/range ratio determination (with most cons. veh. config.)
Parent1 and Parent2 vehicle cover complete all remaining vehicles in UBE and EC/range family.
UBEparent1,-7°C
Ratioparent1_UBE
Only measurement of parent1 vehicle:
Measurement of parent1 vehicle and parent2 vehicle:
Parent1 vehicle for UBE determination: Determination of UBEparent1,-7°C
Parent2 vehicle for EC/range-ratio determination:
PERparent2,-7°C = ECparent2,-7°C =
Calculation of Ratioparent2_PER =
Calculation of Ratioparent2_EC =
Parent1 vehicle for UBE-ratio determination: Calculation of Ratioparent1_UBE =
Remaining vehicles in UBE (ratio) family
PERmember,-7°C = PERmember,23°C * Ratioparent2_PER ECmember,-7°C = ECmember,23°C * Ratioparent2_EC
Ratioparent2_PER Ratioparent2_EC
Parent2 vehicle for EC/range-ratio determination:
PERparent2,-7°C = ECparent2,-7°C =
Calculation of Ratioparent2_PER =
Calculation of Ratioparent2_EC =
>>> Manufacturer shall be allowed to declare the ratios  need to be worse than the measured ones

## Slide 4: Proposal PEV Low Temperature Family concept application (parent and member vehicle concept): Example
Option 1:
Option 2:
20 kWh
30 kWh
40 kWh
23°C UBE
18.8 kWh
18.8 kWh
18.8 kWh
-7°C UBE
UBEparent = 18.8 kWh
Parent vehicle with a low capacity battery can cover a higher capacity battery
Hence a 20kWh battery can cover 30kWh and 40kWh battery
If UBE from parent vehicle will be carry over directly then the range for child vehicle will not reflect the reality and range will be low
Parent vehicle with a low capacity battery can cover a higher capacity battery
Determine UBE ratio (which determine the loss of battery capacity from 23°C to -7°C)
Then this worst case loss can be applied to other high capacity batteries
This UBE child at -7°C reflect the worst case UBE but close to the real life
20 kWh
30 kWh
40 kWh
23°C UBE
18.8 kWh
30 x 0.94=28.2 kWh
-7°C UBE
UBEratio =18.8/20= 0.94
40 x 0.94=37.6 kWh
UBEparent1,-7°C
Parent1 vehicle for UBE determination: Determination of UBEparent1,-7°C
Parent2 vehicle for EC/range-ratio determination:
PERparent2,-7°C = ECparent2,-7°C =
Calculation of Ratioparent2_PER =
Calculation of Ratioparent2_EC =
Ratioparent1_UBE
Parent1 vehicle for UBE-ratio determination: Calculation of Ratioparent1_UBE =
Parent2 vehicle for EC/range-ratio determination:
PERparent2,-7°C = ECparent2,-7°C =
Calculation of Ratioparent2_PER =
Calculation of Ratioparent2_EC =
Remaining vehicles in UBE (ratio) family
PERmember,-7°C = PERmember,23°C * Ratioparent2_PER ECmember,-7°C = ECmember,23°C * Ratioparent2_EC
Ratioparent2_PER Ratioparent2_EC
Remaining vehicles in UBE (ratio) family
PERmember,-7°C = PERmember,23°C * Ratioparent2_PER ECmember,-7°C = ECmember,23°C * Ratioparent2_EC
Ratioparent2_PER Ratioparent2_EC

## Slide 5: Proposal (N)OVC-HEV Low Temperature Family concept application (vehicle concept and its application)
OVC-HEVs:
Measurement according to PEV concept (following UBE (ratio) family and EC/range family concept)
Criteria emissions treated in the same way than for pure ICE
Range and energy consumption treated in a similar way than for pure ICE
NOVC-HEVs:
Measurement of one or more representative vehicles within Type 6 family (selection of vehicle as defined for Type 6 for vehicles with a combustion engine).
Application of the values of the measured vehicle (or vehicles) to all represented vehicles.
Criteria emissions and CO2 treated in the same way than for pure ICE
23°C/-7°C ratio application:
MCO2,CS, MCO2,CD, MCO2,weighted
EC, ECp
AER, EAER
MCO2,CS
Criteria Emissions
Vehicle concept and selection:
Similar/in line with PEVs (as focus on range and electric consumption)
Criteria emissions
Vehicle concept and selection:
Same as pure ICE vehicles (as focus on emissions)
Proposal when OVC-HEVs base on PEV family concept

## Slide 6: Proposal (N)OVC-HEV Low Temperature Family concept application (vehicle concept and its application)
OVC-HEVs:
Measurement of one or more representative vehicles within Type 6 family (selection of vehicle as defined for Type 6 for vehicles with a combustion engine).
Application of the values of the measured vehicle (or vehicles) to all represented vehicles.
Criteria emissions and CO2 treated in the same way than for pure ICE
Range and energy consumption treated in the same way than criteria emissions and CO2
NOVC-HEVs:
Measurement of one or more representative vehicles within Type 6 family (selection of vehicle as defined for Type 6 for vehicles with a combustion engine).
Application of the values of the measured vehicle (or vehicles) to all represented vehicles.
Criteria emissions and CO2 treated in the same way than for pure ICE
Vehicle concept and selection:
Same as pure ICE vehicles (as focus on emissions)
MCO2,CS, MCO2,CD, MCO2,weighted
Criteria emissions
EC, ECp
AER, EAER
Proposal when OVC-HEVs base on pure ICE family concept
MCO2,CS
Criteria Emissions