## Slide 1: IWG Measurement Uncertainties
6th session
6/7 October 2020

## Slide 2
Justification by different approaches:
by measurement (or simulation) results from specific experiments, e.g. investigations on power train noise at indoor test bench
by classic statistical methods e.g. parameter studies and correlation analysis (ACEA Tyre study)
by theoretical derivations based on physical relations e.g. distance law (deviation from centered driving)
Justification of the main impact quantities.

## Slide 3
Justification of the main impact quantities.
Situation | Input Quantity | estimated deviations of the meas. result (peak-peak) |  | Impact on Lurb | Status | Justification by |  | 
 |  |  |  |  |  | measurement | statistical methods | theoretical derivations
 |  | Lwot | Lcrs |  |  |  |  | 
Run to Run | Micro climate wind effect | 0,40 | 0,77 | 0,53 | done | X |  | 
 | DRIVER #1: Deviation from centered driving | 0,50 | 0,50 | 0,50 | done |  |  | X
 | DRIVER #2: Start of acceleration | 0,50 | 0,00 | 0,33 | done | X |  | 
 | DRIVER #3: Speed variations of +/- 1km/h | 0,30 | 0,30 | 0,30 | done |  | X | 
 | DRIVER #4: Load variations during cruising | 0,00 | 0,50 | 0,17 | done |  | X | 
 | Varying background noise | 0,10 | 0,10 | 0,10 | done | X |  | 
 | Variation on operating temperature of engine (WOT) and tyres (WOT&CRS) ==> See ISO 362-1 NOTE | 1,20 | 0,50 | 0,96 | done | X |  | 
Day to Day | Barometric pressure (Weather +/- 30 hPa) | 0,60 | 0,00 | 0,40 | done |  |  | X
 | Air temperature effect on tyre noise (5-10°C) | 1,00 | 2,00 | 1,34 | done | X |  | 
 | Air temperature effect on tyre noise (10-40°C) | 1,00 | 2,00 | 1,34 | done | X |  | 
 | Varying background noise during measurement | 0,60 | 1,00 | 0,74 | done | X |  | 
 | Air intake temperature variation | 1,50 | 0,00 | 0,99 | done | X |  | 
 | Residual humidity on test track surface | 0,70 | 1,00 | 0,80 | done | X |  | 
Site to Site | Altitude (Location of Test Track) -100 hPa/1000m (from 1015 to 915 hPa) | 1,00 | 0,00 | 0,66 | done |  |  | X
 | Test Track Surface | 3,50 | 5,00 | 4,01 | done | X |  | 
 | Microphone Class 1 IEC 61672 | 1,00 | 1,00 | 1,00 | done | X |  | 
 | Sound calibrator IEC 60942 | 0,80 | 0,80 | 0,80 | done | X |  | 
 | Speed measuring equipment continuous at PP | 0,07 | 0,13 | 0,09 | done |  | X | 
 | Acceleration calculation from vehicle speed measurement | 0,50 | 0,00 | 0,33 | done |  |  | X
Vehicle to Vehicle | Production Variation on Tyres; Aging of Tyres until delivery to customer (1dB after one year) | 0,75 | 1,50 | 1,00 | done | X |  | 
 | Variation on Tyre Size and Brand (non-OEM) | 0,00 | 0,00 | 0,00 |  |  |  | 
 | Production Variation in Power | 0,40 | 0,00 | 0,26 | done |  |  | X
 | Battery state of charge for HEVs (3 dB(A)) | 0,00 | 0,00 | 0,00 |  |  |  | 
 | Production Variability of Sound Reduction Components | 1,00 | 0,50 | 0,83 | done | X |  | 
 | Impact of variation of vehicle mass | 1,40 | 0,60 | 1,13 | done | X |  | 
Status of completeness: 100%

## Slide 4
Justification of the main impact quantities.
A car with low PMR and large frontal projected area such as tall body shape is affected in acceleration during pass-by noise test by wind speed but sound pressure levels in cruise and acceleration are less changed by wind speed.
The impact for the final result of Lurban is 1.6dB.
„wind effect“ – justification by measurement
Wind speed within 5m/sec tolerance may affect acceleration performance.
Normally its influence is not so significant, but we should know some vehicles have large impact.
The example shows 1.6 dB(A) difference for Lurban in the conditions of following and against wind.
Acceleration [m/s2]
Sound Pressure level [dB(A)]
Against wind 5m/s
Following wind 5m/s
2nd gear
3rd gear
Influence of k- factor
ΔSPLurban:
1,6 dB

## Slide 5
Justification of the main impact quantities.
„ DRIVER#1: deviation from centered driving“ – justification by theoretical derivation
Assumption for the calculation: 5dB/distance doubling (monopole source under semi-free field conditions) and 0,5m for the deviation from center.
center
deviation from center Δx
Invers square law:
with:
ɑ coefficient for dB/distance doubling
Δx deviation from center
= 0,5dB
ΔSPLurban:
0,5 dB

## Slide 6
Justification of the main impact quantities.
„ DRIVER#2: start of acceleration“ – justification by measurement
The variation of the point of push down gas pedal causes different accelerations and a different sound emission in the wot measurement.
ΔSPLurban:
0,3 dB
ΔSPLwot
=0,6 dB
preacceleration [meter bevor line AA]: -5m/-3m

## Slide 7
Justification of the main impact quantities.
„DRIVER#3: speed variations of +/- 1km/h“ – justification by theoretical derivation
SPLtyre road noise vs. vehicle speed (derived from R117)
with:
ɑ SPLTRN@50km/h
b coefficient for speed dependency
= 0,5dB
Assumption for calculation: mean coefficient of the speed dependency is 30 (usually varies between 27 -33 for C1 tyres). Depending on the source distribution this effect influences the test result of crs and wot measurement.
ΔSPLurban:
0,5 dB

## Slide 8
Justification of the main impact quantities.
„ DRIVER#4: Load variations during cruising“ – justification by statistical methods
A constant speed test is considered valid, if the vehicle speed does not change by more than 1 km/h around the vehicle target speed of 50 km/h. The tables above provide a calculation scheme for the 3rd (left table) and the 4th gear (right table). Per gear three columns are shown. Column 1 is a run, with 50 km/h throughout the test area. Column 2 is an acceleration from the lower border vehicle speed to the upper border vehicle speed. Column 3 is almost a free rolling from the upper border speed to the lower border speed. The calculations of the sound source tyre/rolling sound (Ltr,50) and the mechanics/dynamic sources (Ldyn) are done according to the RD-ASEP model with a split of 90% tyre rolling sound and 10% for the remaining sources. The impact on Lurban is estimated by a 1/3rd share of the cruise test to the overall result.
ΔSPLurban: 0,3dB
(ΔSPLcrs:1.0dB)

## Slide 9
Justification of the main impact quantities.
„Varying background noise“ – justification by measurement
Background shall be measured before and after a serious of measurements. During a measurement it is not possible to determine the background noise.
While the background noise might be low during its measurement, transient broadband events with up to 60 dB(A) may occur.
Such events are typical for test centers with multiple tracks and events, but hardly noticeable during pass-by measurements.
These transient noises will be counted as vehicle signal and can especially affect cruise measurement up to 1.0 dB to 1.2 dB higher values. In a 1/3rd share of the cruise test to Lurban, the impact on Lurban is estimated up to 0.4 dB.
14 dB(A)
16 dB(A)
ΔSPLurban:
0.0 – 0.4 dB

## Slide 10
Justification of the main impact quantities.
„variation on operating temperature of engine and tyres “ – justification by measurement
Variation of approx. 100 °C on exhaust system (KAT Temp.)
+
Variation of 10°C test track temp (derived from R117)
High-performance vehicles in particular can have a large dependency on component temperatures of the power train. Here, too, the source distribution decides how large the influence on the end result is.
ΔSPLurban:
0,8 dB

## Slide 11
 | Barometric Pressure |  | Power variation | Acceleration variation | Lurban [dB(A)]
Day to day | Weather +/- 30 hPa | 60hPa | 7.7% | 7.7% | 0.4dB
Site to site | Altitude -1000m Location of Test Track | 100hPa | 13.5% | 13.5% | 0.7dB
Justification of the main impact quantities.
„barometric pressure“ – justification by theoretical derivation
The influence of barometric pressure can be calculated by using ISO 1585 “Engine test code – Net Power”(or R85)
ISO1585 paragraph 6.3.1
Correction of engine power;
P
Correction factor for spark-ignition engines;
Chart: Acceleration m/s2
| 1.17 | 1.17
aurban | 0 | 100
awot ref | 0 | 100
αwot ref±5% | 0 | 100
awot ref-5% | 0 | 100
awot 2.0 | 0 | 100
Lwot | 0 | 0
Lcrs | 0 | 0
a_wot
a_urban
ΔSPLurban:
up to 0,7 dB

## Slide 12
Justification of the main impact quantities.
„Air temperature effect on tyre noise (5-10°C)“ – justification by measurement
The influence of the air temperature on the tire/ road noise can be up to 5dB within the total temperature range from 5 up to 40°C. For Lcrs 100% contribution of tire noise is considered and for LWOT 50% contribution of tire noise is considered.
„Air temperature effect on tyre noise (10-40°C)“ – justification by measurement/ calculation
Extrapolation (upper temp. range) of the measured SPL
by a logarithmical fitting function (derived from temperature
correction of the R117 for C1 tires) with using the air
temperature.
-1,7dB
3,3dB
extrapolation
ΔSPLCRS: 5 dB ΔSPLWOT: 3.2 dB
ΔSPLurban:
3.8 dB

## Slide 13
Justification of the main impact quantities.
„ Varying background noise during measurement“ – justification by …
…
redundant– see slide „ Varying background noise“ (no. 5)

## Slide 14
Temperature effect for Lcrs and Lwot for tyre noise are covered in “Air temperature effect on tyre noise“. Therefore temperature effect for Lwot for power train noise is considered here.
The temperature effect for intake noise is used measured data. Same impact of air (gas) flow excitation to exhaust etc. are considered.
The contribution of sound level provided by such excitation is assumed by 50% for calculation of Lwot.
„Intake temperature“ – justification by measurement
Justification of the main impact quantities.
Relation between air- and intake temperature (at least increasing by 10℃ at higher temp.))
10℃
35℃
Air temperature range
(The regulation allow tem-perature condition at 5 to 40℃.)
1 ~ 1.5dB /20℃
45℃
Ave. 2.8dB
Impact to Lwot
Total range of intake temperature (5 to 50 ℃)
Impact to intake noise
1.6dB
2.25~3.38dB
Estimation of the impact on Lwot
+2.8dB
Impact of Intake noise against intake temperature
(Decreasing by 20℃ provides increasing of intake noise by 1 to 1.5dB based on measured data.)
ΔSPLurban:
1 dB
E.g. Staying idle for 5 minutes provides intake temperature increases by 10℃.
Intake temp.
[℃]
time [min.]

## Slide 15
Justification of the main impact quantities.
„Residual humidity on test track surface“ – justification by measurement
2,1
1,7
0,9
0,7
3 Measurements in each operating condition, Runs with residual humidity: test track surface between AA‘ and BB‘ almost 100% dry
All measurements performed on the same day according to R51.03, Annex 3 (Tyre dimensions: 285/40 ZR21; 315/35 ZR21)
Residual humidity on one side of the line CC‘ only can lead to Run-to-Run deviations
ΔSPLurban:
1 – 1,3 dB

## Slide 16
Justification of the main impact quantities.
„Altitude (Location of Test Track) -100 hPa/1000m (from 1015 to 915 hPa) “ – justification by …
…
redundant– see slide „Barometric pressure“ (no. 7)

## Slide 17
Justification of the main impact quantities.
„Test track surface“ – justification by measurement (VDA RR)
Maximum deviation track: 5,5 dB
 max. deviation vehicle measurement: 4dB
Different test tracks surfaces lead to different tyre road noises. Depending on the source distribution these differents influence the test result of crs and wot measurement.
ΔSPLurban:
4 dB
Chart: acc. [m/s^2]
| 0 | 1.7700000000000002 | 1.17
Test track min | 61.6389 | 64.3415 | 63.4254
Test track max | 66.6898 | 67.7271 | 67.3755
Lroll min | 61
Lroll max | 66.5

## Slide 18
Justification of the main impact quantities.
„Microphone Class 1 IEC 61672“ – justification by measurement (calibration)
The deviation from reference of today used microphones is normally in a range of +/- 0.5 dB. The maximum error during measurement by using two different sound level meters can be up to 1 dB. The frequency range of interest of pass by test is up to 5000 Hz (example in the left diagram, 99% of the OAL @5000Hz)
5000 Hz
ΔSPLurban:
1 dB

## Slide 19
Justification of the main impact quantities.
„Sound calibrator IEC 60942“ – justification by measurement (calibration)
The maximum allowed deviation determined by DIN EN 60942:2018 “Electroacoustics. Sound calibrators“ is +/- 0.25 dB. The maximum error during measurement by using two different sound calibrators can be up to 0.5 dB.
Excerpt from a calibration report
ΔSPLurban:
0,5 dB

## Slide 20
Justification of the main impact quantities.
„speed measuring equipment at PP“ – justification by theoretical derivation
Same approach as „DRIVER#3: speed variations of +/- 1km/h“
Precision of todays speed measuring systems: approx.:
+/-0,2 km/h
= 0,1dB
See „DRIVER#3: speed variations of +/- 1km/h“
ΔSPLurban:
0,1 dB

## Slide 21
Justification of the main impact quantities.
„Acceleration calculation from vehicle speed measurement“ – justification by theoretical derivation
The acceleration is derived by calculation from the speed measurement. The speed measurement shall be determined with devices according to is subject to uncertainty and given by the regulation according to paragraph 1.4 of Annex 3 of UN R51.03. The tables and the figure show the impact of the allowed speed uncertainty on the final test result.
ΔSPLurban:
0,5 dB
0,5 dB

## Slide 22
Justification of the main impact quantities.
„Production variation on tyres; Aging of tyres until delivery to customer“ – justification by measurement
aging: ≈ 1 dB/ year
+
prod. variation: ≈ 0,5 dB
= 1,5 dB (CRS)
production variation
aging
The variation of 0,75 dB in WOT measurement assumes a source distribution of 50% between tyre road and power train noise.
ΔSPLurban:
up to 1dB

## Slide 23
Justification of the main impact quantities.
„Production variation in power“ – justification by theoretical derivation
Based on a allowed production variation in power of +/- 5% and a total variation in acceleration of 10% the impact on Lurban is up to 0,4 dB.
Power variation | Power variation absolut | Acceleration variation | Lurban [dB(A)]
+/- 5% | 10% | 10% | 0.4dB
ΔSPLurban:
up to 0,4 dB
0,2 m/s2
0,4 dB
approach similar to
„barometric pressure“

## Slide 24
Justification of the main impact quantities.
„Production Variability of Sound Reduction Components“ – justification by measurement
The impact on Lurban of 0.7 dB assumes a contribution of the effect of 50% on Lwot (1.1dB). The effect in the Lcrs is neglectible.
SPL [dB(A)]
rpm [1/min]
tailpipe noise
Measurement of 7 exhaust
systems from the same type
rpm [1/min]
deviation [dB]
Variation up to 2dB
ΔSPLurban:
up to 0,7 dB

## Slide 25
Justification of the main impact quantities.
„variation vehicle mass “ – justification by measurement (simulation)
argumentation chain:
„test gear change“
ΔmFZG
Δa
Δtest gear
Δengine speed
ΔSPL
ΔSPL
=1,6dB
gear i becomes valid
The main impact of the variation of the vehicle mass is on acceleration behavior and can causes a test gear change. The test gear change leads to an other test engine speeds and an other sound emission.
normal vehicle mass
vehicle mass + 200kg (appr. + 11%)
gear i+1