## Slide 1
Related vehicle
Test vehicle
Scenario 1 :
Left turn or Right turn at the intersection
Not less than
16km/h
TTC
not more than
2.8sec.
Stationary
30km/h
1)Beginning to steer for right turn
2)Wrap ratio 0%
TTC
not more than
1.7sec.
Stationary
Not less than
10km/h
 | Speed （Average） | TTC （Average） | Brake pedal operation
1) | 16km/h | 2.8 sec. | Observed (all of data)
2) | 10km/h | 1.7 sec. | Not observed (73% of data)
Research result: Driving behavior of normal drivers
The subject vehicle drives at a speed of 30 km/h (with a tolerance of +0/-2 km/h) toward the intersection, and decelerates by braking to a speed of not less than 16 km/h at a point where the subject vehicle begins to steer left / right, and the TTC to the oncoming vehicle is not more than 2.8 seconds. When the subject vehicle turns left or right in the intersection, the speed is reduced to not less than 10 km/h, and then drives at a constant speed. The TTC to the oncoming vehicle is not more than 1.7 seconds at when the wrap ratio between the subject vehicle and the oncoming vehicle becomes 0%.
An example of the detail scenario
Relation between the Draft Scenario and the research result
AEBS-13-xx

## Slide 2
Related vehicle
Test vehicle
1)Beginning of left turn (related vehicle)
2)Wrap ratio 0%
Research result: Driving behavior of normal drivers
Both the forward vehicle and the subject vehicle drive at a speed of 40 km/h (with a tolerance of +0/-2 km/h) on the straight road. The forward vehicle decelerates by braking to a speed of 10 km/h (with a tolerance of +0/-2 km/h) in order to turn right or left at the corner, and the subject vehicle also decelerates by braking to keep appropriate distance with the forward vehicle. At when the forward vehicle begins to turn right or left, the speed of the subject vehicle is not less than 26 km/h and the TTC to the frontal vehicle is not more than 4.7 seconds. After that, the subject vehicle decelerates to a speed of not less than 20 km/h, and then drives at a constant speed. The TTC to the forward vehicle is not more than 2.5 seconds at when the wrap ratio between the subject vehicle and the oncoming vehicle becomes 0%.
Relation between the Draft Scenario and the research result
 | Speed （Average） | TTC （Average） | Brake pedal operation
1) | 26km/h | 4.7 sec. | Observed (97% of data)
2) | 20km/h | 2.5 sec. | Not observed (all of data)
10km/h
Not less than
26km/h
TTC
not more than
4.7sec.
10km/h
Not less than
20km/h
TTC
not more than
2.5sec.
AEBS-13-xx
Scenario 2 :
Right turn or Left turn of a forward vehicle
An example of the detail scenario

## Slide 3
1)Beginning to steer to turn right
2)Offset ratio -100%
Research result: Driving behavior of normal drivers
The subject vehicle drives at a speed of 30 (with a tolerance of +0/-2 km/h) km/h toward the curve of which the radius is not more than 25 m at the outer side of the road, and decelerates by braking to a speed of not less than 22 km/h at a point where the subject vehicle enters the curve. The TTC to the stationary object is not more than 1.6 seconds at when the subject vehicle begins to turn in the curve. In the curve, the subject vehicle drives outer lane than the centre of the road. After that, the subject vehicle continue to turn in the curve at a constant speed of not less than 21 km/h. The TTC to the stationary object is not more than 1.1 second at when the wrap ratio between the subject vehicle and the stationary vehicle becomes 0%, or at when the offset ratio* between the subject vehicle and the centre of the stationary pedestrian target or the stationary bicycle target becomes -100%.
Relation between the Draft Scenario and the research result
Stationary
30km/h
Guard pipe
Curve radius:
not more than
25m
Not less than
22km/h
TTC
not more than
1.6sec.
Stationary
Not less than
21km/h
TTC
not more than
1.1sec.
 | Speed （Average） | TTC （Average） | Brake pedal operation
1) | 22km/h (Pedestrian target) | 1.6 sec. (Pedestrian target) | Observed (87% of data)
2) | 21km/h (Pedestrian target) | 1.1 sec. (Pedestrian target) | Observed (57% of data)
Scenario 3 :
Curved road with guard pipes and a stationary object
An example of the detail scenario
AEBS-13-xx

## Slide 4
Test vehicle
1)Beginning to steer for lane change
2)Offset ratio -100%
Research result: Driving behavior of normal drivers
The subject vehicle drives a straight road at a speed of 40 km/h (with a tolerance of +0/-2 km/h), and begins to steer in order to change the lane in front of the signboard which notifies reducing the lane. No other vehicles approach the subject vehicle. The TTC to the signboard is not more than 4.2 seconds at when the subject vehicle begins to steer. During changing the lane, the speed of the subject vehicle is constant, and the TTC to the signboard is not more than 3.3 seconds at when the offset ratio between the subject vehicle and the centre of the signboard becomes -100%.
Relation between the Draft Scenario and the research result
 | Speed （Average） | TTC （Average） | Brake pedal operation
1) | 39km/h | 4.2 sec. | Not observed (79% of data)
2) | 38km/h | 3.3 sec. | Not observed (75% of data)
車
線
減
少
TTC
not more than
4.2sec.
40km/h
(constant)
車
線
減
少
40km/h
(constant)
TTC
not more than
3.3sec.
Scenario 4 :
Lane change due to road construction
An example of the detail scenario
AEBS-13-xx