## Slide 2
Accidentology study & efficiency calculation for solutions evaluation to decrease fatal injuries in bus and coach evacuation after accident

## Slide 3: Introduction
  This accidentology study is done to highlight the fact that current manual hammers are not used as it’s recommended.
  Today, despite the passenger advertisement, the system is not 100% efficient and fatalities cases are directly due to the wrong uses or no-use of this manual system.
  In order to be constructive, an accidentology study was done from real facts and from these facts, rates were determinate. The final objective is to have concrete values to evaluate the system benefit.
  In this study we will compare manual hammer to a “system easier to operate”, i.e. with an optimization of identification, location and operation for passengers.

## Slide 4: Study path explanation
STEP 1
Presentation of the ratio of manual hammers present in buses regarding the requirement issued from regulation
STEP 2
Presentation of the accidentology analysis results from real cases
STEP 3
Technical comparison between the manual hammer and a local “system easier to operate”
Determination of the technical efficiency ratio between the both systems
Conclusion
Conclusion on this analysis
Determination of the real manual hammer efficiency in comparison of a 100% theorical efficiency
Questions

## Slide 5: STEP #1 : Manual hammer presence in bus
Manual hammer:
  Removable from its support
  Movable in all the bus … and outside
  Location mandatory close to the emergency exits (EE) BUT
  Unconscious & unscrupulous people picks up hammer for playing with or robbing
Because of the last point, hammer locations are changed:
  behind the driver (authorized in France only for buses, not coaches)
  OR close to the driver
  … OR not present inside bus
A French road control demonstrates that on 27 controlled buses, 25 were in accordance with the regulation. 2 / 27 didn’t respect the hammer prescription : all hammers were not accessible in one case and all were missing in the second case.
So a ratio of 92,5% of well-equipped buses.

## Slide 6: STEP #2 : Accidentology study:
Accidentology study:
  All the BEATT reports was analyzed and only reports referencing the hammer mandatory use are raised in this presentation.
  Other official reports from minister departments for road accident like NSTB are included in this study.
  Videos are part too of the study to determine times and internal conditions inside the vehicles during evacuation or evacuation attempt.
  Each case defines how the manual hammer was used, IF USED, and evaluates the difficulty to break an EE with it.
  Each case is compared to a “system easier to operate” with gain evaluation based on the capacity to open all the EE in one time and in 10ms.
  Each case mention the benefit to open all the EE asap: gain of time, gain to limit an explosion risk, gain to escape a dangerous zone, etc.

## Slide 7: STEP #2 : Accidentology study:
Analysis | Reference document | Vehicle type | Accident type | Execution | Visibility | Accessibility | Comparison to “system easier to operate” | Efficiency of the “system easier to operate”
@0,16s: student ready to use the hammer @0,20s:studient start to punch with the hammer Student broke the emergency windows in two times: - @0,23: first layer after 4 tries , - @0,25: second layer in 2 tries Non possible estimation of the time to found and take the hammer; total time to break the windows: 9-10s |  | travel coach | Fire | DIFFICULT | POOR | POOR | 10ms in one time easier to identify and to use (Light flash on system) | duration: 50000% attempts:600% action/layer: 100% x time of identification and use
no use of hammer / only one exit opened all passengers panic pushing them and walking on them: @0,3s: one door opened / no visible fire @0,6s: fire on left side visible and under the bus @0,10: fire on the right of the bus @0,18: front door opened @0,36: 60 passengers out the bus; one on the floor because of the smoke toxicity | https://www.youtube.com/watch?v=-5aNdqZWphY | urban bus | Fire | DIFFICULT | POOR | POOR | 10ms in one time Able to multiply the exit number and avoid severe toxicity injuries | IMPOSSIBLE to compare with manual hammer due to the lack of data on the presence or not of hammer inside the bus and if passengers try to use one of them without break a windows. In theory: INFINITE
No use of the hammer. Passengers wait firemen for exit. safety team on area 10min after accident. No fire / No smoke | EQ-BEAT--06-6--FR | coach (TCP) | rollover | NA | NA | NA | No gain if activated on back window view the accident damages. Gain if front window intact. | No measurable efficiency
NGPV bus (natural gas-powered vehicle, not gasoline)Doubles accidents on two different sites. Multiple incidents identical >30 (in France and Europe like Saarbruck in Germany on 4 bus). Explosion <10min in one case du to fire inside GNV tank. - Conclusion from the BEATT to use new materials to limit the fire propagation. - second conclusion: improve the thermal protection to the bus's roof to avoid the explosion risk of the gas tank. --> opening all the emergency exit ASAP (Windows, hatches and doors) delay the tank's thermal heating. | EQ-BEATT--06-3--FR | >30 NGPV bus over Europe | FIRE | EASY | HIGH | EASY | Windows, Hatches and door opening in only one action by driver and at safety distance to the fire. Delay the tank explosion --> safer evacuation. Windows & Hatches opening in 10ms in one safety action. More time for passenger evacuation with Driver help. Environmental damage (external to the bus) more mastered due to the delay to decrease the fire propagation | - Delay before explosion: no value but High based on BEATT conclusions - Manual action: 500% - Trig time efficiency: 50000%
Passengers out of the bus via back windows broken by passenger and helped by external persons. | EQ--BEA-TT-08-11-FR | travel coach | rollover | not valuable | High | EASY | No urgency of fire, smoke or over accident | identical on result. The difference is about the accessibility of the easily, readily hammer already presents on the window and easy to use.
Front shock at low speed with fire 10s after the collision. Despite of the panic, all passengers and the second driver were able to go outside the bus by the windows after hammer use on several EE | EQ-BEAT--15-2--FR | travel coach | front collision & Fire | EASY | HIGH | EASY | Good use of the manual hammer by all the passengers --> all the passengers were evacuated by the windows | identical on result. The difference is about the accessibility of the easily, readily hammer already presents on the window and easy to use.

## Slide 8: STEP #2 : Accidentology study:
Passengers: - persons with special needs - assisted living facility persons 23 deads /45 passengers Passengers dead because of the smoke toxicity (first), fire and the incapacity to move to the door without assistance. Nurses and officers had to push and pull passengers to the door. "Of the 14 passengers who evacuated, many had to be pulled, pushed, or dragged out the front loading door by nurses or rescuers." Lack off time for evacuation and no use of windows braking system (hammer) report extract: " • The nursing staff had not been instructed on the availability of the window exits and how to use them, and they were unaware of their potential as a means of exit during the evacuation. • Most of the passengers who required assistance during the evacuation had special needs, and negotiating the movements necessary to escape through the emergency windows and the front door was all but impossible during the limited time available." | ACCIDENT REPORT NTSB/HAR-07/01 PB2007-916202 | travel coach | Fire | NONE | NA | POOR | - Triggered by driver = Smoke evacuation in one action (10ms) - Triggered by nursing staff = 5 trigs but better visibility due to lighting flashes. - Staff nursing and officers able to pull and push passengers by the windows: reducing the physical effort to pull and push passengers to the doors and reducing evacuation time of each passenger. - Increase evacuation time - decrease smoke toxicity concentration - with passengers pulled by windows, the central aisne should be clear for beds evacuation (100% died in the accident). | on the 23 dead passengers, on the base of 25 rescued passenger in 3min with effort, it could be clearly supposed that a electronic hammer system provide a minimum of 3min more time for evacuation, decreasing the effort by 3; in term of efficiency, the 23 dead passengers could theoretically be evacuated out of the bus in fire. efficiency via classic hammer in this configuration: infinite. in comparison if manual hammers should be used = 500%
Accident in night and all internal lights of because of the shock. First door opened by the driver with difficulty. Second door blocked by the central railing. One passenger attempted to break a windows with success, fallen and fainted due to a gas intoxication. Flames few seconds after the crash. big opacity because of the smoke between the collision and the use of the hammer (<30s) The 41 passengers dead in the bus was discovered in the bus's corridor trying to go outside the bus. the smoke toxicity is responsible of this result. | EQ-BEAT--17-6--FR GRSG-113-05 | travel coach | front collision & Fire | DIFFICULT | POOR | POOR | - Triggered by driver = Smoke evacuation in one action (10ms) - Triggered by nursing staff = 5 trigs but better visibility due to lighting flashes. - Increase evacuation time - decrease smoke toxicity concentration and nobody faints - without passengers pulled by windows, the central corridor should be clear for classic evacuation | it could be clearly supposed that a “system easier to operate” provide a minimum of 3min more time for evacuation, decreasing the risk of faint, the 41 dead passengers could theoretically be evacuated out of the bus in fire by the central door. efficiency via classic hammer in this configuration: infinite if triggered in one action by the driver. in comparison if all manual hammers had been used in the same time, visible and accessible = 500%
Analysis | Reference document | Vehicle type | Accident type | Execution | Visibility | Accessibility | Comparison to “system easier to operate” | Comparison to “system easier to operate”

## Slide 9: STEP #2 : Accidentology study:
No use of the EE; one attempt on a hatch without success by one child. No help from the driver for evacuation. Evacuation time > 30 minutes helped by external persons and via the front window using makeshift tools (> 20minutes only to break the front window) Manual hammer placed at the good place inside the bus. | EQ-BEAT--16-13--FR | autobus | rollover | EASY | HIGH | EASY | Visibility and accessibility of a structural fixed system should draw attention of the passengers. Moreover, with a dashboard trigger button, the driver should open all the EE in one action and allow passengers to exit the bus and the external persons to help easily the passengers (essentially by the rear of the bus via back window) | Compared to the unique attempt without success, the opening of all the EE should decrease the window braking action from 20 minutes to 10 milliseconds.
Analysis | Reference document | Vehicle type | Accident type | Execution | Visibility | Accessibility | Comparison to “system easier to operate” | Comparison to “system easier to operate”

## Slide 10: STEP #2 : Accidentology study:
Theory :
Supposing the 100 % presence of manual hammer in all buses at the right place
Supposing the manual hammer is used in each 100 % needed situation
Supposing the EE breaking/opening in one action in 100% of the cases (including breaking the two layers in one action)
THEN The manual hammer’s efficiency could be considered as 100%
BUT the reality is :
92,5 % measured presence of the hammer
Accidentology analysis shows an effective good use of the hammer of 5/9 cases so less than 60%; it’s assumed to use 70% for the following calculation.
Accidentology analysis shows a breaking window action in two times (2 layers) so an assumed efficiency of 85%.
The facts shows that the real efficiency of the manual hammer is not 100%. With the actual values, the real efficiency is 55%.

## Slide 11: STEP #2 : Accidentology study:
The use of the hammer (current device) is not a priority for evacuation and it is not very effective, as confirmed by this UK study (SDWEE-03-08) :

## Slide 12: STEP #3 : Technical efficiency comparison
Comparison Matrix |  |  |  |  |  |  | 
 |  | Classic manual Hammer |  | “system easier to operate” (driver's trigger) |  | “system easier to operate” (Passenger trigger) | 
Criteria | Weight | ranking | score | ranking | score | Ranking | score
Functional features |  |  |  |  |  |  | 
Windows Breaking duration | 1 | 1 | 1 | 5 | 5 | 5 | 5
Easy to use | 2 | 3 | 6 | 5 | 10 | 5 | 10
Visibility | 3 | 1 | 3 | 5 | 15 | 5 | 15
accessibility | 3 | 2 | 6 | 4 | 12 | 4 | 12
Time to trig/break the windows | 3 | 1 | 3 | 5 | 15 | 5 | 15
number of devices inside the bus | 1 | 5 | 5 | 4 | 4 | 5 | 5
 |  |  | 0 |  | 0 |  | 0
Safety actions |  |  |  |  |  |  | 
Vehicle speed > 3km/h | 3 | 1 | 3 | 1 | 3 | 1 | 3
Vehicle speed <= 3km/h | 3 | 5 | 15 | 5 | 15 | 5 | 15
Exit regarding traffic jam | 3 | 1 | 3 | 1 | 3 | 1 | 3
Glass particule damage | 2 | 3 | 6 | 3 | 6 | 3 | 6
Windows fall down | 1 | 3 | 3 | 3 | 3 | 3 | 3
Financial & contractual |  |  |  |  |  |  | 
System Cost | 3 | 5 | 15 | 1 | 3 | 1 | 3
 |  |  | 54 |  | 91 |  | 92
Efficiency only |  |  | 59% | 54% | 99% |  | 100%
Total Score |  |  | 69 |  | 94 |  | 95
= MAX of all systems eval (SUM (functional features + Safety action)) / SUM(functional features + Safety action) * 100
Chart: Technical efficiency reported to the max value
| Proposal
Classic manual Hammer | 0.58696
Electronic exit opening system (driver's trigger) | 0.98913
Electronic exit opening system (passenger's trigger) | 1

## Slide 13: STEP #3 : Global efficiency comparison
Hypothesis :
Supposing the 100 % presence of “system easier to operate” in all buses at the right place by structural assembly
Supposing the lighting mandatory system on “system easier to operate” rising the visibility and the accessibility, the “system easier to operate” is used in each 100 % needed situation like the manual hammer
Supposing the EE breaking/opening in one action in 100% of the cases (including breaking the two layers in one action)
THEN The “system easier to operate”’s efficiency could be considered as 100%
According to the previous table :
The score comparisons between manual and “system easier to operate” are 40% and 41% (depending of the use case) more efficient for the “system easier to operate” IF 100% of the system are present and well placed inside vehicles.
The real manual system efficiency is measured at 55% because of the 92,5% of real presence; and the calculated comparison provides 59%; by extrapolation, 59% of theorical efficiency x 92,5% of real presence = 54,75% of real efficiency.
 so the “system easier to operate” confirms 100% of efficiency in real case compared to manual system.

## Slide 14: Bibliography:
EQ-BEATT--05-4--FR
EQ-BEATT--05-6--FR
EQ-BEATT--05-1--FR
EQ-BEAT--06-6--FR
EQ-BEATT--06-3--FR
EQ-BEA-TT—07-2--FR
EQ-BEA--07-9--FR
EQ-BEATT--8-4--FR
EQ-BEAT--09-02--FR
EQ-BEATT--09-4--FR
EQ-BEATT--08-9--FR
EQ-BEATT--08-7--FR
EQ--BEA-TT-08-11-FR
EQ-BEATT--09-08--FR
ACCIDENT REPORT - NTSB/HAR-07/01PB2007-916202
EQ-BEATT—09-9--FR
EQ-BEATT—14-10--FR
EQ-BEATT—14-11--FR
EQ-BEAT--17-6--FR / GRSG-113-05
EQ-BEAT--15-2--FR
EQ-BEAT--16-14--FR
EQ-BEAT--16-13--FR
EQ-BEAT--13-12--FR
EQ-BEAT--13-2--FR
EQ-BEAT--12-17--FR
EQ-BEAT--11-16--FR
EQ-BEAT—09-12--FR
EQ-BEAT--16-9--FR
EQ-BEAT--19-1--FR
EQ-BEAT--18-7--FR
EQ-BEAT--19-7--FR
EQ-BEAT--20-3--FR
BEATT: Affaire n°2003-0141-01
EQ-BEAT--10-9--FR
https://www.youtube.com/watch?v=81k7AOqa7wE
https://www.youtube.com/watch?v=-5aNdqZWphY
https://www.ledauphine.com/faits-divers-justice/2020/02/19/annonay-les-gendarmes-ont-mene-une-operation-de-controle-des-bus-scolaires?utm_source=kwanko&utm_medium=contextual%20targeting&utm_campaign=GENERIQUE&utm_content=355569