## Slide 1
UI
1234567
Proposal for extension of the DETA to improve the use of the
UNIQUE IDENTIFIER for the lighting UN Regulations
SLR-42-12-Rev.2
(Rev. of SLR-37-01)
GRE
IWG
SLR

## Slide 2
UNIQUE IDENTIFIER / DETA Database
Alternative marking options in UN Regulations Nos. 148, 149 and 150
UI
270650
With UI essential information becomes invisible, unless you are part of one of the existing user groups in DETA
R1 S1 2a F1 AR
E1
148R00
3170
MAY BE REPLACED BY
GRE
IWG
SLR
The (traditional) Approval Marking specifies (Example R148):
The number of the type approval
The contracting party (country) who is responsible for the type approval
The Regulation Number the device was type approved to
The status of the Regulation at the time of type approval
The different functions that are included in the device
Any possible restrictions in mounting height
Any possible restrictions in mounting position
Any possible restriction to the number of devices necessary (D or Y)
IMPORTANT:
ALL these markings must be visible after the installation of the device on the vehicle
3170
E1
148R
(series) 00
R1 S1 2a F1 AR
-
The (new) Unique Identifier Marking specifies:
The unique number of the type approval
IMPORTANT:
ALL these markings must be visible after the installation of the device on the vehicle
270650

## Slide 3
UNIQUE IDENTIFIER / DETA Database
SLR requests for improvement – Update usage and management of DETA
Part A: Document management
Create a new PDF document in DETA
(e.g. „Summary“) showing for example, depending on GRs decisions:
  Description / Picture / Drawing / Sketch of the device
  Markings following the alternative option / Explaining text
  If they exist, limitations to the installation and/or use
Proposal - Make the relevant information available to those dependent on the content
GRE
IWG
SLR
Part B: Usergroup management
Create a new usergroup in DETA
  Usergroup level: Public
  Usergroup rights: Read only the „Summary“ document

## Slide 4
UNIQUE IDENTIFIER / DETA Database
SLR requests for improvement – New document “Summary” (example)
“Summary”
UI
270650
Headline
The Unique Identifier marking as on the device
One or more picture(s) / drawing(s) of the device
The alternative marking as in the Regulation /
Explaining text for the device
R1 S1 2a F1 AR
E1
148R00
3170
If necessary this document may have more pages
The above information, except for the alternative marking, is available somewhere in the existing documents in DETA. This information could be found by authorised experts only, but impossible for all others. The existing documents also contain a lot of information that is not for public view in any case!
GRE
IWG
SLR
Proposal Part A: Document management

## Slide 5
 | CERT (communication on type approval) | TR (test report) | IF (information document) | OTHER (other document)
Approval granting TAA (for granted approval) | W | W | W | W
CP applying the UN Reg. for which approval was granted | R | R | R | R
CP applying UN Reg. 0 (access to the approvals of R0 and the annexed Regulations | R | R | R | R
CPs not applying that Reg. | R | - | - | -
Manufacturer (only for own approvals) | R | R | R | R
UNIQUE IDENTIFIER / DETA Database
SLR requests for improvement – New usergroup(s) and access rights for DETA
USERGROUPS DETA
DOCUMENTS AVAILABLE IN DETA
Proposal Part B: Usergroup management
GRE
IWG
SLR
“Summary” (PDF)
W
R
R
R
R
Periodical technical inspection, Law enforcement bodies, Repair shops, Vehicle owners, End-users / Public | - | - | - | -
Additional summary document
+
Existing access rights
And documents (177th WP.29)
Additional usergroup
+
R
The new usergroup has only read access right of the new document „Summary“

## Slide 6
BACKUP
GRE
IWG
SLR

## Slide 7
Information included in the approval marking:
The number of the type approval (3169 and 3170)
The contracting party who is responsible for the type approval (E1)
The Regulation Number the device was type approved to (148)
The status of the Regulation at the time of type approval (00)
The functions that are included in the device (R1, S1, 2a, F1, AR)
Any possible restrictions in mounting height on the vehicle
Any possible restrictions in mounting position on the vehicle
Any necessary other devices that should be present (D or Y lamps)
UI
1234567
DETA
Information
+
In the database (internet)
Information included in the Unique Identifier:
The UI number under which the device information is available in the electronic database.
On the device
(approval markings + additional markings)
texttexttexttexttexttexttexttext
texttexttexttexttexttexttexttext
texttexttexttexttexttexttexttext
texttexttexttexttexttexttexttext
texttexttexttexttexttexttexttext
texttexttexttexttexttexttexttext
UNIQUE IDENTIFIER
The original idea behind
If necessary available via the internet
Paragraph 3.3.3. (148) „The approval marking may be replaced by the Unique Identifier (UI), if available.“
On the device
(UI number + additional markings)
R1 S1 2a F1 AR
E1
148R00
3169
3170
GRE
IWG
SLR