## Slide 2
Conclusions about accidentology study & efficiency of current device for breaking emergency windows in case of evacuation after accident

## Slide 3: Difficulties with current device
Based on previous group discussions and accident analysis, we all seem to agree on the suboptimal effectiveness of current devices :
Not used as it’s recommended.
Current device like manual hammer :
  Removable from its support
  Movable in all the bus … and outside
  Location mandatory close to the emergency exits (EE) BUT unconscious & unscrupulous people picks up hammer for playing with or robbing
Several actions needed to break window
 It is therefore necessary to define how to improve this situation and improve the efficiency of the system through its localisation, its visibility and ease of use

## Slide 4: Report from BEATT (Land transport accident investigation department)
This conclusion is confirmed by the recent report from BEATT about an accident on mars 2019.
A fire broke out on board a coach. The driver parks his vehicle in a paved area bordering the emergency lane of the motorway. The 50 passengers, young students, as well as the two drivers managed to evacuate the coach.
One of the passengers injured his hand while trying to smash a window on the coach before the stop. Despite repeated actions, this passenger did not succeed in breaking the window with the hammer.

## Slide 5: Principle #1 : Better localisation
Placed permanently on the emergency window (unique positioning)
Accessible for all passengers (adapted positioning)
Not easy removable from its support (theft risk avoidance)

## Slide 6: Principle #2 : Better visibility
A means of alert (flash, light) to help locate the device in case of emergency, using a more intrusive way for passenger in case of event.
The alert and operability of the device conditioned on activation of an alarm system (with possible driver deactivation) or action by the driver under the same conditions as defined by the group for power operated doors.

## Slide 7: Principle #3 : Easier to use
Can be operated by a simple action (misuse avoidance)
A single action to break the window (operation time decreased)
Easy to operated by all type of passenger, without the need for physical force