## Slide 1: Comments on UNECE R No.141.01
3 Options regarding proposal for driver-display of “Trailer TPMS not Equipped” in addition to Trailer TPMS Malfunction
elaborated by a small group of TF TPMSTI experts
(TPMSTI-10-05)
27 Nov 2020
TPMSTI-11-03a

## Slide 2: Option 1
5.4.4. In case a vehicles of category N2 or N3 is towing a vehicle of category O3 and O4 which is not equipped with a TPMS, a notification shall be displayed to the driver that a towed vehicle without equipped TPMS is connected. This notification shall be displayed after the following conditions are fulfilled:
  - The ignition switches in the "on" (run) position or a change of a towed vehicle is detected
  - Cumulative drive time defined in Annex 5 2.5

## Slide 3: Option 1
Option 1 requires an addition extension of the Annex 6 by adding:
2.2.1.2.4 Simulate a towed vehicle without installed TPMS signalled by the towed vehicle TPMS and check that the towed vehicle TPMS driver notification signal specified in paragraph 5.4.4 of this Regulation is displayed after the cumulative time specified in Annex 5, 2.5
The parameters defined in EBS 23 bytes 1 and 2 of ISO 11992-2:2014 shall be transmitted as follows:

## Slide 4: Option 1
Function / Parameter | ISO 11992-2:2014 Reference | Driver Notification Required
Tyre Pressure Status (TPMS data continously) | EBS23 Byte 1 Bit 1-2 (112 — not available) | Reference to paragraph 5.4.4. in this UN Regulation
Tyre/wheel identification (corresponding to Tyre Pressure Status) | EBS23 Byte 2 (00000000b — Tyre/Wheel ID not defined or wheel not defined and axle > 1510 ) OR (11111111b — Tyre/Wheel ID not available or Tyre 1510/Wheel 1510, no other Tyre/Wheel IDs with this Status are present) | Reference to paragraph 5.4.4. in this UN Regulation
Note: This test covers the scenario when a towing vehicle is combined with a towed vehicle released before TPMS was mandatory.

## Slide 5: Option 1
Pros:
Driver is always aware about the status of the Trailer TPMS
Cons:
Driver might get annoyed with the notification
In some cases (no ISO 11992 and ISO 11992) the notification might be superfluous
Additional implementation requirement for truck manufacturers (might not be part of the scope of the legislation)
Notification only possible 10 minutes after cumulative driving
Behaviour for TPRS is unclear

## Slide 6: Option 1

## Slide 7: Option 2
5.4.4. In case a vehicles of category N2 or N3 is towing a vehicle of category O3 and O4 which is not equipped with a TPMS, a notification may be displayed to the driver that a towed vehicle without equipped TPMS is connected.
Pros:
No annoying notifications to the driver
No additional requirements for truck manufacturers
Truck manufactures get aware of the issue and try to find proprietary solution
Cons:
Driver will not be notified in case there is no TPMS on the trailer (old trailer)
Regulation is changed without really adding a new requirement
Behaviour for TPRS is unclear

## Slide 8: Option 3
Kept Regulation and Annex unchanged
Pros:
No annoying notifications to the driver
No additional requirements for truck manufacturers
Behaviour for TPRS is not affected
Cons:
Driver will not be notified in case there is no TPMS on the trailer (old trailer)