## Slide 1: LED replacement light sources
Basics
TFSR-15-02rev1

## Slide 2: TERMINOLOGY ― OVERVIEW
LED substitute light sources
  Intended as alternative to incandescent filament light sources in new applications
  Almost equivalent to the incandescent filament light sources
LED replacement light sources
  Intended to replace incandescent filament light sources in existing applications
  Fully equivalent to incandescent filament light sources
LED retrofit
  No longer used for regulated and approved light sources
  Used in the market for “other” light sources
    Not standardised
    Not approved

## Slide 3: SITUATION need for LED replacements
general lighting
  energy saving
  life time
  consumer have accepted led light sources as replacement
  sales of incandescent light sources is often forbidden
  (incandescent) filament technology will be scarcely available
automotive
  fewer failure, less exchanges on the vehicle
  more robust
  energy saving
  diverse performance
  not always permitted
continued availability of (incandescent) filament technology is driven by general lighting
need for
automotive LED replacement light sources
capable to replace filament light sources
approved, permitted for use
consumers are asking for it
future availability of spare parts

## Slide 4: SOLUTION replacement parts ― insert into R37
Light source regulations are about
  approved light sources for
    new vehicles/lamps to be put on the market
    vehicles-in-use, replacement parts
Solution is to develop LED light sources
  for corresponding filament light sources
  as replacement part
    equivalent performance in an approved lamp technical equivalence
    same name
    approved according to the same regulation legal equivalence
Amend Regulation 37
(incandescent) filament technology
  new
  replacement
New: LED technology
  Replacement
Equivalent counterpart light sources
Technical
  Equivalent performance
Legal (administrative)
  Same name
  Approved according to R37

## Slide 5: CATEGORIES standardized basic design ― different technologies
Category definition by parameters on
  photometric
  colorimetric
  geometric
  electrical
  thermal (LED)
Types: variation within a category
  manufacturer
  voltage
  design of supports (bulb, cap) if changing optical output
New LED replacement categories
  compared to the corresponding category in incandescent filament technology:
    equivalent technical performance in the lamp
    with the same name

## Slide 6: EQUIVALENCE GRADE SUBSTITUTES ↔ REPLACEMENTS
LED substitutes
  GRE 82-03, Guide supporting the definition of LED substitute categories
  GRE informal documents: equivalence reports for new categories
  R128, requirements
  R.E.5, Annex 3, Group 4, Sheets for LED light sources
    For additional lamp (luminaire) approval if approved with filament light source
    Additional keying (interlock)
    Example H11/LED
  Lamp and installation regulations
LED replacements
  GRE 83-15, Guide supporting the definition of LED replacement categories
  GRE informal documents: equivalence reports for new categories
  R37, requirements
  R.E.5, Annex 3, Group 5, Sheets for LED light sources
    Not for additional lamp (luminaire) approval
    Standard keying
    Example H11 (mark: LEDr)

## Slide 7: OTHER REQUIREMENTS
To all LED light sources
Correlated colour temperature
UV radiation
EMC/EMI as for an electronic sub assembly (ESA) in R10
No light from ≤2 ms. flashes

## Slide 8: EQUIVALENCE CRITERIA GRE-82-03 vs. GRE 83-15
Parameters, main changes | LED subst. | LED repl.
Photometry |  | 
Objective luminous flux | = | =
Light centre length | = | =
Distortion free zone (if any) | = | =
Normalized luminous intensity distribution | ≈ | ≈
Size and position of the light-emitting-area | ≈ | ≈
Homogeneity of the light-emitting-area | ≈ | ≈
Contrast of the light-emitting area | ≈ | ≈
Colorimetry |  | 
Colour of emitted light | = | =
The spectral content | ≠ | ≠
Geometry |  | 
Maximum lamp outline dimensions | = | =
Cap/holder | = holder | = cap
Functional interlock between light source and application | ≠ | 
Electrical connector | = | =
Parameters, main changes | LED subst. | LED repl.
Electrical |  | 
Test voltage | = | =
Electrical power consumption | ≠ max | ≠
The minimum voltage range | ≠ | ≠
Dependency of the luminous flux on the applied voltage |  | ≠
Dependency of the luminous flux on elevated ambient temperatures |  | ≠
PWM operation to stabilize the applied voltage |  | +
PWM operation to dim light sources |  | +
Voltage polarity |  | +
Failure detection | + | +
Failure behaviour | + | +
Thermal |  | 
Cap temperature |  | ≠
Thermal behaviour | + | + run-up
=, ≠, + are compared to filament light sources
All coloured cells for LED replacement are additional to the LED substitutes

## Slide 9: EQUIVALENCE CRITERIA
Equivalent in all aspects: default LED replacement light source
- all cells right column above
Equivalent, practical in production : options at the request of the applicant
- yellow cells right column above
- due to outer dimensions of the cap too small
Parameters, main changes | LED subst. | LED repl.
Photometry |  | 
Objective luminous flux | = | =
Light centre length | = | =
Distortion free zone (if any) | = | =
Normalized luminous intensity distribution | ≈ | ≈
Size and position of the light-emitting-area | ≈ | ≈
Homogeneity of the light-emitting-area | ≈ | ≈
Contrast of the light-emitting area | ≈ | ≈
Colorimetry |  | 
Colour of emitted light | = | =
The spectral content | ≠ | ≠
Geometry |  | 
Maximum lamp outline dimensions | = | =
Cap/holder | = holder | = cap
Functional interlock between light source and application | ≠ | 
Electrical connector | = | =
Parameters, main changes | LED subst. | LED repl.
Electrical |  | 
Test voltage | = | =
Electrical power consumption | ≠ max | ≠
The minimum voltage range | ≠ | ≠
Dependency of the luminous flux on the applied voltage |  | ≠
Dependency of the luminous flux on elevated ambient temperatures |  | ≠
PWM operation to stabilize the applied voltage |  | +
PWM operation to dim light sources |  | +
Voltage polarity |  | +
Failure detection | + | +
Failure behaviour | + | +
Thermal |  | 
Cap temperature |  | ≠
Thermal behaviour | + | + run-up

## Slide 10: OPTIONS practical in production ― at request
1: electrical current and monitoring
LED requires lower electrical current
Failure detection and monitoring use calculated electrical current from the corresponding incandescent filament lamp
LED replacement light sources
  Default: same electrical current
  High-efficiency: lower current
  AE device to increase the electrical current where needed for failure detection and monitoring
2: voltage polarity and insertion
Some incandescent filament light sources can be inserted in more than one way
LED replacement too, but voltage polarity matters
Cap size too small:
  +/- marks on the light source
  Light source category data sheet (if adopted by GRE) specifies which terminal shall be marked plus or minus
3: cap dimensions and insertion
Geometric dimensions relevant for interchangeability shall be the same
When more space in the cap is needed:
  Light source category data sheet (if adopted by GRE) specifies maximum deviations to the IEC cap sheet
  Only for part of the cap, irrelevant for interchangeability

## Slide 11: OPTIONS summary
Package
Trade name/mark, rated voltage, approval code, category name and LEDr mark
Additional to A.:
  Information symbol on the package
  Instructions
    In the package
    Display at the point of sales
  Reference to web site
    Listed applications
    Info for installation and proper functioning
Light source
Default – universally applicable
Non-default – limited applicable (2.2.2.2.2.)
  Information symbol on the light source
  Depending on the option:
  High-efficiency light source
    ͰE mark
  AE device included
    Æ mark
  Voltage polarity matters
    +/- mark
  Larger dimensions
    Actual dimensions mark, followed by an exclamation mark !

## Slide 12: MORE INFORMATION
GRE inf. 83
GRE-83-15e (TF SR) - Equivalence criteria
GRE-83-16e (TF SR) - Equivalence report for H11 LEDr
GRE-83-14e (TF SR) - Supporting information for GRE_2020_15, GRE-83-11, GRE-83-12 and GRE-83-13
TF SR
TFSR-13-08 - SAE J575 Humidity Test-with-LEDr
TFSR-11-02rev1 Technical_Requirements_open topics 2020-05-25

## Slide 13: END