## Slide 1: Round Table Discussion on Thermal Propagation Requirements
Transport Canada: Kyle Hendershot
NRC: Dean MacNeil, Steven Recoskie

## Slide 2: Introduction
Recent incidents with major OEM using automotive quality Li-ion battery cells from a Tier 1 supplier have highlighted our previous concern about thermal events in EV.
Recommendations for this incident include charging to lower SOC, software upgrade, parking outside and replacing battery pack.
Perhaps an induced thermal failure evaluation is required, how should we proceed?
In attempting to create a proposal to incorporate a physical test as alternative to existing documentation method, several important questions were raised.
Please think of each subsequent question for a round table discussion on how to proceed with developing a test and pass/fail criteria. You will be requested to share your thoughts on each topic.

## Slide 3: 1. Test Mode - Vehicle Mode
“D. Principle for developing the global technical regulation
…
  (b) To identify and assess the potential safety risks, depending on the relevant vehicle conditions such as:
  (i) in normal use, in active driving possible mode and parking;
  (ii) in normal use, during external charging/feeding;
  (iii) in an accident (during and post-crash).”
A. Does “parking” imply that the vehicle is off?
Section 5.4.12. Thermal propagation, does not specify the vehicle mode at which tests need to be conducted.
B. Should testing be conducted in both “active driving possible mode and parking”?

## Slide 4: 2. Pass/Fail Criteria - External Warning
“5.4.12. Thermal propagation.
For the vehicles equipped with a REESS containing flammable electrolyte, the vehicle occupants and those in close proximity to the vehicle shall not be exposed to any hazardous environment caused by thermal propagation…”
Current requirements only target a “situation inside the passenger compartment”
C. Should an external warning be a requirement?

## Slide 5: 3. Vehicle vs Component Level Equivalency
“5.4.12.1. The vehicle shall provide an advance warning indication to allow egress or 5 minutes prior to the presence of a hazardous situation inside the passenger compartment caused by thermal propagation …”
D. How can a warning and egress time be demonstrated at a component level?

## Slide 6: 4. Early Detection
“5.4.12. Thermal propagation.
For the vehicles equipped with a REESS containing flammable electrolyte, the vehicle occupants and those in close proximity to the vehicle shall not be exposed to any hazardous environment caused by thermal propagation which is triggered by an internal short circuit leading to a single cell thermal runaway.”
As written in GTR 20, current requirements do not allow for early detection.
E. Do we have sufficient information to regulate this technology within our existing mandate?
F. How can early detection be verified in a regulation?

## Slide 7: 5. Method
G. Is the documentation method in GTR 20 enforceable and how would it be enforced under self certification and type approval?

## Slide 8: Canadian Thoughts
A. Does “parking” imply that the vehicle is off?
We have seen recommendations in the field that suggest parking outside in open space to minimize damage from potential TR event. This would be a vehicle off situation, we think this could be a very stringent test that will require an advanced monitoring system that will benefit bystanders, infrastructure and vehicle owner. It could be more important than a vehicle “on” test.
B. Should testing be conducted in both “active driving possible mode and parking”?
Need to specify whether drive mode engaged or not. We think testing under active mode is a different test than non-active mode and the key parameters are different. Most can be confirmed by testing in non-active mode (e-gress time, internal warnings to occupants) except whether drive mode is disengaged (is this required?)
C. Should an external warning be a requirement?
We feel that an audible external warning is a minimum response to a serious thermal event when in non-active mode. Ideally, there is an early warning detection or safety system design that does not permit serious event, in this case the vehicle must be disabled and notification to driver provided. If a serious thermal event does occur could existing warning systems such as those required in UN R. 116/ FMVSS 114/CMVSS 114 be utilized?
D. How can a warning and egress time be demonstrated at a component level?
In our experience there is no substitute for a vehicle level test for TR testing. It is the most representative of in-situ conditions and does not need replication of any system to predict full system response. A component level test helps in the design process, but is not a substitute for a vehicle level test. In fact, many of these component level tests could very well be design restrictive when the system level response at the vehicle level is not considered.

## Slide 9: Canadian Thoughts
E. Do we have sufficient information to regulate this technology within our existing mandate? / F. How can early detection be verified in a regulation?
The main issue for us is validation of these technologies. Current TR tests are designed to initiate TR rapidly to minimize interferences with other system level parameters not related to safety. Validation of any early warning system is not trivial and would require significant effort in understanding every OEMs BMS system, which is not practical.
OICA proposed text in EVS20-E1TP-0100 to amend section 5.4.12.2.1 to include text that would allow for early detection. This proposal would be insufficient as the requirements under 5.4.12. are targeted at safety measures to mitigate thermal runaway after a single cell thermal runaway has already occurred.
In principle we fully support the idea of early detection however without a sufficient method of evaluating them at a regulatory level the existing mandate of the Phase 2 may be insufficient to have it included.
G. Is the documentation method in GTR 20 enforceable and how would it be enforced under self certification and type approval?
A documented approach is dependent on tests, modelling and expert opinions on the designed safety strategies. It still needs validation. Depending on the burden of proof an enforcement body intends to apply this could pose a significant burden on manufacturers. If a sufficiently robust test can be validated by an OEM that satisfies the enforcement body, why can’t we just use this validated test as a regulatory requirement?
To date, we have been unable to assess the documentation method from a legal/enforability standpoint as we have not seen examples of what information would actually be provided to enforcement bodies.