## Slide 1: Alternative assessment of ALKS performance
Response to OICA’s comments Assessment of additional scenarios Criticality-based scenario classification
K. Mattas, B. Ciuffo, S. Vass, C. Galassi
UNR157-05-12

## Slide 2: OICA’s comments (UNR157-04-10) to EC proposed text (UNR157-03-06)
1. Possible adverse affect on the surrounding vehicles' traffic flow
  The proposed conditions don’t take false reaction avoidance sufficiently into account
  When braking earlier, it is natural, that more collisions could be avoided, but this could be detrimental to many other aspects of road safety, (e.g. rear end collision by a following vehicle)
  When ALKS vehicles are forced to brake too strongly too early, this will likely disrupt traffic flow
EC reply
  The proposed approach is a performance model used only to define whether a certain scenario would be preventable or not for an attentive human driver. It does not introduce any operational requirement to the ALKS. It is based on tactical safety approach adopted by experienced drivers
  The model assumes that driver is able to anticipate the risk by mild decelerations before reaching a safety critical situation. The comment on braking too strong too soon does not seem to hold.
  Is industry suggesting that ALKS vehicles will not be able to be at least as safe as a competent human driver?

## Slide 3: OICA’s comments (UNR157-04-10) to EC proposed text (UNR157-03-06)
2. Design constraints (not technology neutral)
  In order to meet the required performance, the underlying approach would likely need to be implemented into the system software when assessing the criticality of a situation
  So instead of setting a performance expectation, the approach is so detailed, that it would likely be a technical requirement on implementation
EC reply
  Is industry suggesting that ALKS vehicles will not be able to be as safe as a competent human driver without using an approximation of her/his driving logic?
  Is it possible that a shorter reaction time and a continuous monitoring by the ALKS would not be sufficient to have in place something better than the driver model proposed by the EC?
  The model is set to be a performance model and there is no requirement to implement such a high-level control logic. For this reason also this comment does not seem to hold
Notes: Her/his

## Slide 4: OICA’s comments (UNR157-04-10) to EC proposed text (UNR157-03-06)
3. Possible Intel patent conflicts
  The proposed approach could require the use (see 2.) of certain potentially protected IP, as some aspects of the RSS are protected by international patents (WO2018115963, WO2019180506, WO2020035728, WO2020245654)
EC reply
  Even in the case that the comment would hold true for the RSS, since the EC is not suggesting to use the RSS as performance model and the proposed approach is included in the legislation as a set of equations on which there cannot be protected IP, even in the case that an OEM would use the equation as part of the high-level vehicle controller there would be no issue. For this reason also this comment does not seem to hold
Notes: Her/his

## Slide 5: OICA’s comments (UNR157-04-10) to EC proposed text (UNR157-03-06)
Industry considers the proposed concept not mature enough to replace the recently introduced provisions for ALKS.
The discussion should first be finalized within FRAV/VMAD, then a comparison between the new approach and what is established for ALKS shall be made and if necessary the new approach can be used to provide guidance within ALKS on how to assess the performance of the system.
EC reply
  Since the model in the amendment proposal has the same scope as that used in the current R157 (define the performance of an attentive and competent human driver) we don’t believe that the discussion should be necessarily finalized in FRAV
  A thorough assessment of the model has been performed including comparison with the performance models used in R157 and other models (i.e. RSS).
Notes: Her/his

## Slide 6: Insights to the EC performance model proposal (FSM)
Given the questions raised by Industry the following slides will:
  Compare the results of the EC performance model with RSS and the two performance models currently in R157 for the cut-in scenario
  Make the same comparison for cut-out and car-following scenarios
  Show that by using the «membership» of the Fuzzy model it is possible to classify scenarios on the basis of their criticality
At the end of the presentation additional background slides are provided with more information about the model
Notes: Her/his

## Slide 7: Unpreventable cut-in scenarios
Simulation framework proposed by Japan for the CC model
Same values for the common parameters of FSM, RSS and CC.
The Reg157 model uses its own parameters

## Slide 8: Unpreventable cut-in scenarios

## Slide 9: Cut in scenario classification
The FSM is a satisfactory compromise among the different approaches proposed so far to identify unpreventable cut-in scenarios.
What about the preventable ones?
  Is it possible to classify them on the basis of their criticality to allow their fair random selection?
Two possible approaches:
  TTC
  FSM

## Slide 10: Cut in scenario, minimum TTC
CC human driver model
Reg 157 model

## Slide 11: Cut in scenario, using Fuzzy SSMs examples
Green: Easy Not a big challenge for the ADS
Yellow: Medium More interesting than easy cases
Red: Hard Most of the scenarios in test track should be hard cases, as they represent the most important challenge to the control

## Slide 12: Car-following scenarios
CC -> no collisions
RSS -> collisions at high speed
FSM -> no collisions

## Slide 13: Classification of car-following scenarios
In this case the criticality of the scenario is affected by the steady state distance used for the driver
The initial distance is set to have PFS = 0 in the model.

## Slide 14: Cut-out scenarios results
At higher speeds a few collisions for all models.
Pictures for ego vehicle speed of 110 km/h

## Slide 15: Classification for cut out scenarios

## Slide 16: Conclusions
Criticisms to the performance model proposed by the EC raised by industry do not seem to hold
The proposed approach shows better performances than what included in current text and a good compromise wr other SoA models like the RSS
The proposed model allows a simple classification of the criticality of a prevetable scenario that can help in the parameter selection for track-tests
The proposed model shows similar results to the current models regarding car-following (no unpreventable cases) and cut-out (a few unpreventable cases for high-speed scenarios)

## Slide 17: Background information
Section 1. The Fuzzy surrogate Model

## Slide 18: What is Fuzzy Logic? Crisp sets
Classical set is a collection of distinct objects. Any element is either in a set or not.
We can describe a set by its characteristic function. It takes the value 1 for elements that are in the set and the value 0 for elements that are not in the set
The sets are ‘Crisp’

## Slide 19: What is Fuzzy Logic? Fuzzy sets
Characteristic functions of Fuzzy sets can take all values from 0 to 1
This can be helpful in many cases to better describe a situation
Based on those we can create fuzzy rules

## Slide 20: Why Fuzzy logic
Two vehicles with known speeds. What is a safe distance?
Safe
Unsafe

## Slide 21: Why Fuzzy logic
Two vehicles with known speeds. What is a safe distance?
Safe
Do nothing
Unsafe
Decelerate hard

## Slide 22: Why Fuzzy logic
Two vehicles with known speeds. What is a safe distance?
Safe
Do nothing
Unsafe
Decelerate hard

## Slide 23: Why Fuzzy logic
Two vehicles with known speeds. What is a safe distance?
Safe
Unsafe
Safe
Unsafe
Fuzzy

## Slide 24: Why Fuzzy logic
Two vehicles with known speeds. What is a safe distance?
Safe
Unsafe
Safe
Unsafe
Fuzzy
The more unsafe, the harder the vehicle must decelerate

## Slide 25: Car following scenarios
Three models are compared
Regulation Appendix 3 model
RSS model
Fuzzy logic model

## Slide 26: Longitudinal safe distance according to Fuzzy SSMs
Two different definitions of unsafe:
If the leader vehicle decelerates, the follower vehicle cannot avoid an accident (Vienna Convention on Road Traffic)
If nothing changes, there will be a collision in x sec (TTC)
We calculated the Proactive Fuzzy SSM (PFS) and the Critical Fuzzy SSM (CFS)

## Slide 27: Longitudinal safe distance according to Fuzzy SSMs
Maximum
Unsafe distance
Minimum
Safe distance

## Slide 28: Longitudinal safe distance according to Fuzzy SSMs
PFS: If the leader vehicle decelerates, the follower vehicle cannot avoid an accident

## Slide 29: Longitudinal safe distance according to Fuzzy SSMs
CFS: If nothing changes, there will be a collision
If :
=
Else if :

## Slide 30: Capacity for calm proactive reaction
The deceleration is relative to the values of PFS and CFS
PFS value of 1 induces full comfortable deceleration (e.g. 3 m/s2)
CFS value of 1 induces full deceleration (e.g. 6 m/s2)
PFS value of 0.2 induces 20% of comfortable deceleration (e.g. 0.6 m/s2)
The suggested model has the ability to apply a calm deceleration proactively, to avoid getting into a more serious (and possibly unavoidable) conflict

## Slide 31: Background information
Section 2. Cut-in scenario: additional results

## Slide 32: Range of concrete scenario assessed
Ego vehicle longitudinal speed 10 – 130 kph
Cutting-in vehicle longitudinal speed 10 – 120 kph
Cutting-in vehicle lateral speed 10 – 120 kph
Initial longitudinal distance 1 – 60 m (1 – 120 for high speeds)

## Slide 33: Parameters used in the simulations
Reaction time:
  Reg157 -> 0.35 sec
  CC human driver, FSM, RSS -> 0.75 sec
Maximum deceleration (ego-vehicle)
  CC human driver, RSS -> 0.774 G
  Reg157, FSM -> 6 m/s2
Maximum jerk (ego-vehicle, absolute)
  CC human driver, RSS, FSM -> 12.65 m/s3

## Slide 34: Cut in Unpreventable

## Slide 35: Background information
Section 3. Criticality based classification of preventable scenarios

## Slide 36: Criticality-based classification using Fuzzy SMs
In each simulation, PFS and CFS (see background information) are calculated for each simulation step. They take values for 0 to 1, with:
PFS = 1, the situation is “proactively unsafe”, the ego vehicle would not avoid an accident in case of a hard deceleration of the preceding vehicle
CFS = 1, the situation is “critically unsafe”, there is a severe conflict, and a very hard deceleration is required
By the maximum value of each scenario we classify in:
Easy: PFS <=0.85, Medium: PFS>0.85 and CFS <0.9, Hard: CFS=>0.9

## Slide 37: Classification for cut out scenarios

## Slide 38: Classification for cut out scenarios

## Slide 39: Background information
Section 4. Car-following and cut-out

## Slide 40: Car following scenarios
Steady state speed 2 – 130 kph
Leader’s deceleration rate 0.05 – 1 G
Initial distance:
CC human driver model  2 sec THW
RSS model  For time equal to , do not enter in dunsafe if the leader vehicle decelerates
Fuzzy logic model  PFS and CFS = 0

## Slide 41: Car following scenarios simulated
Reaction time starts when:
CC human driver model  Leader vehicles deceleration harder than 5 m/s2
RSS model  Ego vehicle enters dunsafe (could be avoided with calm deceleration)
Fuzzy logic model  PFS or CFS > 0

## Slide 42: Parameters used in the simulations
Reaction time:
  CC human driver, FSM, RSS -> 0.75 sec
Maximum deceleration (ego-vehicle)
  CC human driver, RSS -> 0.774 G
  FSM -> 6 m/s2
Maximum jerk (ego-vehicle, absolute)
  CC human driver, RSS, FSM -> 12.65 m/s3

## Slide 43: Cut out scenarios
Three models are compared
CC human driver model
RSS model
Fuzzy logic model

## Slide 44: Cut out scenarios simulated
Steady state speed 10 – 130 kph
Distance in front 5 – 130 m
Initial distance:
CC human driver model  2 sec THW
RSS model  For time equal to , do not enter in dunsafe if the leader vehicle decelerates
Fuzzy logic model  PFS and CFS = 0

## Slide 45: Cut out scenarios simulated
Reaction time starts when:
Leader vehicle has moved more than 0.375 m (wondering zone) or has crashed and
RSS model  Ego vehicle enters dunsafe (could be avoided with calm deceleration)
Fuzzy logic model  PFS or CFS > 0

## Slide 46: Parameters used in the simulations
Reaction time:
  CC human driver, FSM, RSS -> 0.75 sec
Maximum deceleration (ego-vehicle)
  CC human driver, RSS -> 0.774 G
  FSM -> 6 m/s2
Maximum jerk (ego-vehicle, absolute)
  CC human driver, RSS, FSM -> 12.65 m/s3

## Slide 47: Cut-out scenarios results
For low speeds the ego vehicle avoids the collision with the stopped vehicle for any model
Pictures for ego vehicle speed of 60 km/h

## Slide 48: Thank you
© European Union 2020
Unless otherwise noted the reuse of this presentation is authorised under the CC BY 4.0 license. For any use or reproduction of elements that are not owned by the EU, permission may need to be sought directly from the respective right holders.
Slide xx: element concerned, source: e.g. Fotolia.com; Slide xx: element concerned, source: e.g. iStock.com
Notes: Update/add/delete parts of the copy right notice where appropriate.
More information: https://myintracomm.ec.europa.eu/corp/intellectual-property/Documents/2019_Reuse-guidelines%28CC-BY%29.pdf