## Slide 1
Minimum Following Distance for ALKS
UN R157 5th SIG on 10&11 May 2021
MYUNGSU LEE
Korea Automobile Testing & Research Institute
Submitted by the Republic of Korea
UNR157-05-13

## Slide 2
Present speed of the ALKS vehicle |  | ACSF-22-09r1(KOREA) (UNR157-05-03) |  | ACSF-23-07(KOREA) |  | GRVA-2020-32(Germany) | 
 |  | Minimum time gap | Minimum following distance | Minimum time gap | Minimum following distance | Minimum time gap | Minimum following distance
(km/h) | (m/s) | (s) | (m) | (s) | (m) | (s) | (m)
7.2 | 2.0 | - | 2.0 | - | 2.0 | 1.0 | 2.0
10 | 2.78 | - | 3.2 | - | 2.0 | 1.1 | 3.1
20 | 5.56 | - | 5.6 | - | 3.6 | 1.2 | 6.7
30 | 8.33 | - | 9.2 | - | 7.2 | 1.3 | 10.8
40 | 11.11 | - | 14.1 | - | 12.1 | 1.4 | 15.6
50 | 13.89 | - | 20.3 | - | 18.3 | 1.5 | 20.8
60 | 16.67 | - | 27.6 | - | 25.6 | 1.6 | 26.7
70 | 19.44 | 1.9 | 36.3 | 1.8 | 34.3 | 1.7 | 33.1
80 | 22.22 | 2.1 | 46.1 | 2.0 | 44.1 | 1.8 | 40.0
90 | 25.00 | 2.3 | 57.2 | 2.0 | 50.0 | 1.9 | 47.5
100 | 27.78 | 2.5 | 69.5 | 2.0 | 55.6 | 2.0 | 55.6
110 | 30.56 | 2.7 | 83.1 | 2.0 | 61.1 | 2.0 | 61.1
120 | 33.33 | 2.9 | 97.9 | 2.0 | 66.7 | 2.0 | 66.7
130 | 36.11 | 3.2 | 113.9 | 2.0 | 72.2 | 2.0 | 72.2
The Korean Comment to Minimum Following Distance discussion
In 22nd ACSF IWG(ACSF-22-09r1, April 2019), a formula that considered the margin distance based on the braking distance of the state of art vehicles acquired on the wet road was proposed, but there was an comment from ACSF member that the Minimum Following Distance proposed was too long in the middle and high speed range
Therefore, in 23rd ACSF IWG(ACSF-23-07, July 2019), a renew formula that combines and the general time gap of European road traffic law with the braking distance was proposed
In conclusion, the proposal that the time gap gradually increase to 2.0 s seems to be reasonable
MFD from current regulation
(0~60km/h → 2.0~26.7m)

## Slide 3
Distance[m]
speed[km/h]
The comparison of 3 doc. plots
Chart: 
| 0 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130
GRVA-2020-32(Germany) | 2 | 3.1 | 6.7 | 10.8 | 15.6 | 20.8 | 26.7 | 33.1 | 40 | 47.5 | 55.6 | 61.1 | 66.7 | 72.2
ACSF-23-07( ROK) | 2 | 2 | 3.5905 | 7.2453 | 12.1398 | 18.274 | 25.6479 | 34.2615 | 44.1148 | 50 | 55.5556 | 61.1111 | 66.6667 | 72.2222
ACSF-22-09r1(UNR157-05-03) | 2 | 3.2 | 5.6 | 9.2 | 14.1 | 20.3 | 27.6 | 36.3 | 46.1 | 57.2 | 69.5 | 83.1 | 97.9 | 113.9
MFD from current regulation
(0~60km/h → 2.0~26.7m)

## Slide 4
Appendix

## Slide 5
Minimum Following Distance to the front
ACSF IWG 23rd session on July 2019, Brussels
Korea Automobile Testing & Research Institute
Submitted by the Republic of Korea
Informal Document - ACSF-23-07

## Slide 6: Comment Histroy
The history and comments on previous session
19th session proposal(ACSF-19-06) : , = 2.3sec
- comment : concern for frequent occurrence of cutting-in in low
speed range
20th session proposal(ACSF-20-08) : , =sec
- comment : concern for too high deceleration()
22nd session proposal(ACSF-22-09r1) : , = sec
- comment : concern for too long distance at mid and high speed

## Slide 7: Plot for the respective formula

## Slide 8: Safe distance between vehicles April 2010
Source : Conference of European Directors of Roads

## Slide 9: Consideration of full range speed for next step (ALKS for high speed)
Road speed limits are used in most countries to set the max./min. speed at which road vehicles can legally travel on particular stretches of road. But, the speed range under min. speed is depending on particular situation(e.g. traffic Jam) and can be allowed
Road max. limit speed (e.g. 130km/h)
Road min. limit speed (e.g. 60km/h)
ALKS for low speed
ALKS for high speed
ALKS for low speed
Time gap = 1.8~2 sec
General driving range
particular driving range
Time gap < 1.8 sec
(e.g. traffic jam)

## Slide 10: New Formula for Minimum Following Distance
Where :
: the actual speed of the ALKS vehicle in m/s;
: minimum time gap in second between the ALKS vehicle
and a leading vehicle in front =
: minimum time gap of 2 seconds between the ALKS vehicle
and a leading vehicle in front
☞ the result of the formula above for actual speeds below 4 m/s
the minimum following distance shall never be less than 2 m.
Low speed application
High speed application

## Slide 11: Plot for G/OICA vs. ROK
Chart: 
| 0 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130
German/OICA proposal | 2 | 3.0556 | 6.6667 | 10.8333 | 15.5556 | 20.8333 | 26.6667 | 33.0556 | 40 | 47.5 | 55.5556
ROK New proposal | 2 | 2 | 3.5905 | 7.2453 | 12.1398 | 18.274 | 25.6479 | 34.2615 | 44.1148 | 50 | 55.5556 | 61.1111 | 66.6667 | 72.2222

## Slide 12
Appendix-1

## Slide 16: Plot for G/OICA vs. ROK vs. braking dist.
Chart: 
| 0 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130
German/OICA proposal | 2 | 3.0556 | 6.6667 | 10.8333 | 15.5556 | 20.8333 | 26.6667 | 33.0556 | 40 | 47.5 | 55.5556
ROK New proposal | 2 | 2 | 3.5905 | 7.2453 | 12.1398 | 18.274 | 25.6479 | 34.2615 | 44.1148 | 50 | 55.5556 | 61.1111 | 66.6667 | 72.2222
S-braking dis. | 0 | 1.2 | 3.4 | 6.4 | 10.4 | 15.4 | 21.6 | 28.9 | 37.6 | 47.6 | 59.1 | 72.2 | 87.1 | 103.8