## Slide 1: Has an audible reverse warning device always to be type approved according to Part 1, when the device will be type approved as part of the vehicle according to Part 2?
Proposal prepared by the Secretary and the Expert from Germany
2021-04-16
Working Paper TFRWS-19-05
19th TFRWS, 19 April 2021

## Slide 2: Background information
According to TFRWS-16-05 paragraph 14.5.1.1. the audible reverse warning device(s) fitted on the vehicle has to be type approved according to Part I:
14.5.1.1.
  The audible reverse warning device(s) fitted on the vehicle has been of a type approved under this Regulation (Part I);
This request is mandatory! But should it be mandatory?

## Slide 3: Solution: new text proposed
14.5.1.1. Either
  The audible reverse warning device(s) fitted on the vehicle has been of a type approved under this Regulation (Part I);
  or
  The audible reverse warning device(s) fitted on the vehicle, which has (have) not been of a type approved under this Regulation (Part I), this device (s) has (have) to fulfil the “Endurance test” of paragraph 6.5. (Part 1).
14.5.1.2. The test voltage shall be as specified in paragraph 6.3.4. to 6.3.6 of this Regulation;