## Slide 1: Fuzzy-logic based performance model for motorway traffic scenarios
Description and first results
K. Mattas, B. Ciuffo
08 April 2021
FRAV-12-06, submitted by the European Commission
12th FRAV session, 8 April 2021

## Slide 2: Assessment of ADS safety in GRVA/VMAD*
* VMAD-16-06 NATM MASTER DOCUMENT
FRAV-12-06, submitted by the European Commission
12th FRAV session, 8 April 2021

## Slide 3: What type of Requirements?
Behavioural/Operational Requirements affect parameters of ADSs operations (e.g. target speed, acceleration, deceleration, headway, etc.)
  Pros. -> clear and easily verifiable
  Cons. -> limit OEMs’ freedom, may hinder innovation, side effects possible, difficult to be linked with overall safety/efficiency targets
Performance Requirements define situations that the ADS shall be able to handle (e.g. should be able to avoid collision, have a collision probability of X etc.) without saying how to handle them
  Pros. -> give freedom to OEMs and foster innovation, focus on safety/efficiency targets
  Cons. -> not always easy to be verified
FRAV-12-06, submitted by the European Commission
12th FRAV session, 8 April 2021

## Slide 4: Use of performance requirements
Performance Requirements can be used to:
  Identify those scenarios that the vehicle shall be able to handle (deterministic use)
    Pros -> no need to take into account severity and likelihood of the scenario
    Cons -> too much related to the correctness of the performance criteria
  Define the probability of an accident occurrence among the scenarios considered in the assessment (probabilistic use)
    Pros -> uncertainty in performance requirements better handled
    Cons -> need to complement the probability with other risk-related measures like severity and likelihood
FRAV-12-06, submitted by the European Commission
12th FRAV session, 8 April 2021

## Slide 5: Example. Cut-in scenarios in Reg 157
Paragraph 5.2.5 introduces two performance requiremet models for car-following, cut-in and cut-out. In particular:
  5.2.5.2. defines the performance model for cut-in,
  5.2.5. refers to Appendix 3 to Annex 4 for the performance model for cut-in, car-following and cut-out
Cut-in
Cut-in, car-following and cut-out
FRAV-12-06, submitted by the European Commission
12th FRAV session, 8 April 2021

## Slide 6: Example. Cut-in scenarios in Reg 157 Appendix 3 model
FRAV-12-06, submitted by the European Commission
12th FRAV session, 8 April 2021

## Slide 7: Example. Cut-in scenarios in Reg 157
The two proposed performance models are equally valid approaches to determine “unpreventable” cut-ins
Their only limitation is to always treat the cut-in as an “emergency” situation in which the vehicle has either to do nothing or to apply maximum deceleration capabilities
In reality humans (as well as the future ADSs) apply proportionate reactions and count very much on anticipation (tactical safety)
FRAV-12-06, submitted by the European Commission
12th FRAV session, 8 April 2021

## Slide 8: Assessment of current performance requirements
In order to understand whether the two approaches are ambitious enough we have compared them with other two approaches recently being presented
  The Intel’s Mobileye Responsibility-Sensitive Safety (RSS)*
  The JRC Fuzzy-logic based Model**
Parameters used in the two models for the comparison (system reaction time, acceleration, deceleration, jerk) are the same proposed by the Reg157 Appendix 3 model
* Shalev-Shwartz, S., S. Shammah, and A. Shashua (2017) On a Formal Model of Safe and Scalable Self-Driving Cars. arXiv:1708.06374 [cs, stat]
** Mattas et al. (2020) Fuzzy Surrogate Safety Metrics for real-time assessment of rear-end collision risk. A study based on empirical observations. Accident Analysis and Prevention 148
FRAV-12-06, submitted by the European Commission
12th FRAV session, 8 April 2021

## Slide 9: New model based on fuzzy SSMs
The new model has 3 main differences with the previous ones
Different calculation of lateral safe distance
Longitudinal safe distance according to Fuzzy SSMs
Capacity for calm proactive reaction
FRAV-12-06, submitted by the European Commission
12th FRAV session, 8 April 2021

## Slide 10: What is Fuzzy Logic? Crisp sets
Classical set is a collection of distinct objects. Any element is either in a set or not.
We can describe a set by its characteristic function. It takes the value 1 for elements that are in the set and the value 0 for elements that are not in the set
The sets are ‘Crisp’
FRAV-12-06, submitted by the European Commission
12th FRAV session, 8 April 2021

## Slide 11: What is Fuzzy Logic? Fuzzy sets
Characteristic functions of Fuzzy sets can take all values from 0 to 1
This can be helpful in many cases to better describe a situation
Based on those we can create fuzzy rules
FRAV-12-06, submitted by the European Commission
12th FRAV session, 8 April 2021

## Slide 12: Why Fuzzy logic
Two vehicles with known speeds. What is a safe distance?
Safe
Unsafe
FRAV-12-06, submitted by the European Commission
12th FRAV session, 8 April 2021

## Slide 13: Why Fuzzy logic
Two vehicles with known speeds. What is a safe distance?
Safe
Do nothing
Unsafe
Decelerate hard
FRAV-12-06, submitted by the European Commission
12th FRAV session, 8 April 2021

## Slide 14: Why Fuzzy logic
Two vehicles with known speeds. What is a safe distance?
Safe
Do nothing
Unsafe
Decelerate hard
FRAV-12-06, submitted by the European Commission
12th FRAV session, 8 April 2021

## Slide 15: Why Fuzzy logic
Two vehicles with known speeds. What is a safe distance?
Safe
Unsafe
Safe
Unsafe
Fuzzy
FRAV-12-06, submitted by the European Commission
12th FRAV session, 8 April 2021

## Slide 16: Why Fuzzy logic
Two vehicles with known speeds. What is a safe distance?
Safe
Unsafe
Safe
Unsafe
Fuzzy
The more unsafe, the harder the vehicle must decelerate
FRAV-12-06, submitted by the European Commission
12th FRAV session, 8 April 2021

## Slide 17: New model based on fuzzy SSMs
The new model has a number of differences with the previous ones
Different calculation of lateral safe distance
Longitudinal safe distance according to Fuzzy SSMs
Capacity for calm proactive reaction
FRAV-12-06, submitted by the European Commission
12th FRAV session, 8 April 2021

## Slide 18: Different calculation of lateral safe distance
The cutting in vehicle has to be in front of the ego vehicle
The cutting in vehicle has lateral speed towards the ego vehicle
The lateral net time headway < The longitudinal gross TTC + 0.1 sec
If all three restrictions apply, then we have to check the situation for the longitudinal safe distance
FRAV-12-06, submitted by the European Commission
12th FRAV session, 8 April 2021

## Slide 19: Different calculation of lateral safe distance
Longitudinal gross distance
Lateral net distance
The lateral net distance the space between the vehicles laterally
The longitudinal gross distance is the longitudinal space from the rear of the ego vehicle to the front of the cutting in vehicle
To calculate headway, they have to be divided to the cutting in vehicle lateral speed and the approaching speed respectively
FRAV-12-06, submitted by the European Commission
12th FRAV session, 8 April 2021

## Slide 20: Different calculation of lateral safe distance
Longitudinal gross distance
Lateral net distance
If the lateral net time headway > The longitudinal gross TTC+ 0.1 sec, the cut-in is very slow and the ego vehicle will not have to decelerate
FRAV-12-06, submitted by the European Commission
12th FRAV session, 8 April 2021

## Slide 21: Different calculation of lateral safe distance
Longitudinal gross distance
Lateral net distance
Else, if the longitudinal distance is long and the cut-in speed is slow, it goes to the longitudinal safety part and may be considered safe at the end
FRAV-12-06, submitted by the European Commission
12th FRAV session, 8 April 2021

## Slide 22: Different calculation of lateral safe distance
Advantages
Less parameters needed
Less information that may induce errors (lane markings)
Cases when the vehicles deceleration causes an accident are avoided
Slow lane changes for vehicles in a distance are also considered
FRAV-12-06, submitted by the European Commission
12th FRAV session, 8 April 2021

## Slide 23: Longitudinal safe distance according to Fuzzy SSMs
Two different definitions of unsafe:
If the leader vehicle decelerates, the follower vehicle cannot avoid an accident (Vienna Convention on Road Traffic)
If nothing changes, there will be a collision in x sec (TTC)
We calculated the Proactive Fuzzy SSM (PFS) and the Critical Fuzzy SSM (CFS)
FRAV-12-06, submitted by the European Commission
12th FRAV session, 8 April 2021

## Slide 24: Longitudinal safe distance according to Fuzzy SSMs
Maximum
Unsafe distance
Minimum
Safe distance
FRAV-12-06, submitted by the European Commission
12th FRAV session, 8 April 2021

## Slide 25: Longitudinal safe distance according to Fuzzy SSMs
PFS: If the leader vehicle decelerates, the follower vehicle cannot avoid an accident
FRAV-12-06, submitted by the European Commission
12th FRAV session, 8 April 2021

## Slide 26: Longitudinal safe distance according to Fuzzy SSMs
CFS: If nothing changes, there will be a collision
If :
=
Else if :
FRAV-12-06, submitted by the European Commission
12th FRAV session, 8 April 2021

## Slide 27: Capacity for calm proactive reaction
The deceleration is relative to the values of PFS and CFS
PFS value of 1 induces full comfortable deceleration (e.g. 3 m/s2)
CFS value of 1 induces full deceleration (e.g. 6 m/s2)
PFS value of 0.2 induces 20% of comfortable deceleration (e.g. 0.6 m/s2)
The suggested model has the ability to apply a calm deceleration proactively, to avoid getting into a more serious (and possibly unavoidable) conflict
FRAV-12-06, submitted by the European Commission
12th FRAV session, 8 April 2021

## Slide 28: Results
The parameters are to be discussed, and they may change the picture
We see the new Fuzzy model being close to the intersection between the others
FRAV-12-06, submitted by the European Commission
12th FRAV session, 8 April 2021

## Slide 29: Results
Two areas of interest
The first is about cases when the deceleration of RSS vehicles causes an accident
Other models do not decelerate and avoid the accident
FRAV-12-06, submitted by the European Commission
12th FRAV session, 8 April 2021

## Slide 30: Results
RSS
Reg157
FRAV-12-06, submitted by the European Commission
12th FRAV session, 8 April 2021

## Slide 31: Results
Two areas of interest
The second is for vehicles in large distance and small lateral speed
Those cases are avoidable by decelerating in a proactive manner
FRAV-12-06, submitted by the European Commission
12th FRAV session, 8 April 2021

## Slide 32: Results
RSS
Reg157
FRAV-12-06, submitted by the European Commission
12th FRAV session, 8 April 2021

## Slide 33: Results
The model is tested for a number of cases of different ego vehicle and cutting-in speeds.
There are no obvious problems for those cases.
FRAV-12-06, submitted by the European Commission
12th FRAV session, 8 April 2021

## Slide 34: Conclusions
Performance models for setting the safety requirements of future ADSs seem more appropriate than operational requirements
Current approaches suggested by first Regulation on ADSs base accident avoidance on the capability to handle emergency situations
  Anticipation capability by humans (and also by AVs) have also an important role in defining driving safety (tactical safety)
  A model based on fuzzy-logic is proposed and compared with existing models available in the literature. It shows its capability to address limitations of existing approaches
The use of performance models in deterministic rather than probabilistic settings is to be further explored
FRAV-12-06, submitted by the European Commission
12th FRAV session, 8 April 2021

## Slide 35: Thank you
© European Union 2020
Unless otherwise noted the reuse of this presentation is authorised under the CC BY 4.0 license. For any use or reproduction of elements that are not owned by the EU, permission may need to be sought directly from the respective right holders.
Slide xx: element concerned, source: e.g. Fotolia.com; Slide xx: element concerned, source: e.g. iStock.com
FRAV-12-06, submitted by the European Commission
12th FRAV session, 8 April 2021
Notes: Update/add/delete parts of the copy right notice where appropriate.
More information: https://myintracomm.ec.europa.eu/corp/intellectual-property/Documents/2019_Reuse-guidelines%28CC-BY%29.pdf