## Slide 1: Assessment of target lane ACSF C: Concept of defining “critical situation”
scritical
Parameter |  | Values for ACSF C (UNR79 para. 5.6.4.7.)
vRear | actual speed of rear vehicle | variable (≤130 km/h)
tReaction | reaction time (of driver) in rear vehicle = time after the start of the LCM at which the deceleration of the rear vehicle starts | 0.4 s*
aRear | deceleration of rear vehicle | 3 m/s²
vACSF | actual speed of the ACSF vehicle | variable
tG | time of safety gap of ACSFvehicle | 1 s
»
Example:
vRear = 130 km/h
vACSF = 80 km/h
→ scritical = 59.9 m
UNR157-06-09
* +continuous lateral movement of the vehicle before crossing the lane marking.
Submitted by the experts of Germany

## Slide 2: Assessment of target lane Proposal for ALKS lane change (GRVA/2020/33)
scritical
Parameter | Values for ALKS (2020/33 para. 5.2.6.6.1.)
vRear | variable (≤130 km/h)
tReaction | 0.4 s or 1.4 s
aRear | 3 m/s²
vACSF | variable
tG | 1 s
A
B
C
»

## Slide 3: Assessment of target lane Proposal for ALKS lane change (GRVA/2020/33)
Parameter | Values for ALKS (2020/33 para. 5.2.6.6.2.)
vRear | e.g. 130 km/h
tReaction | 0.4 s or 1.4 s
aRear | 3 m/s²
vACSF | variable
tG | 1 s
In case no approaching vehicle in target lane (same concept to ACSF C):
scritical
»