## Slide 1: GRBP-IWGMU-11-03 (11th session of the GRBP Informal Working Group Measurement Uncertainties, (25 May 2021)
2021-05-04 Flowchart Tem Cor V04
prepared by OICA

## Slide 2
Correction of pass-by measurements according to Annex 3
for temperature and if applicable for test track differences
Tyre rolling sound has already been
determined independently and the normalized parameters are available:
tyre rolling sound LTR,DB,REF,
the reference speed vTR,DB,REF , and the tyre sound level slope slpDB,REF
Per gear and run, extract the power train component LPT,CRS,j
from the constant speed test result
Per gear and run, adjust the tyre rolling sound to the vehicle speed condition of the individual acceleration test run
Per gear and run, extract the power train component LPT,ACC,j
from the acceleration test result
Perform pass-by sound measurements according to Annex 3
Perform tyre rolling sound measurements
In combination with the tests above according to Appendix 2 to Annex 3
CASE 2
Correction for temperature and test track
CASE 1
Correction for temperature only
Recalculate LCRS,j and LACC,j
with power train components
and normalized tyre
rolling sound components
Calculate Lurban with the corrected constant speed and acceleration test results according the the procedure in Annex 3
Follow the procedure of CASE 1 to determine the power train components

## Slide 3
Temperature Correction for Tyre Rolling Sound Components CASE 1
Case 1:
Tyre rolling sound LTR,TEST is determined during a set of pass-by measurements according to Annex 3 and used to normalize the tyre rolling sound component of each individual measurement run to the reference air temperature REF = 20 °C
The rolling sound of the tyre LTR,TR shall be determined for a reference speed according to Appendix 3 to Annex [3].
The reported values are the tyre rolling sound LTR,TR, the tyre sound level slope slpREF
and the temperature TR at which these tests have been performed.
For the per gear and run reported constant speed test result LCRS,j, extract the power train component LPT,CRS,j by calculation.
Adjust the tyre rolling sound LTR,TEST to the speed condition of the acceleration test
For the per gear and run reported acceleration test LACC,j, extract the power train component LPT,ACC,j by calculation.
Adjust the tyre rolling sound component of the acceleration test LTR,ACC,j,TEST to the reference temperature REF
Proceed to calculate LURBAN using the temperature normalized sound pressure levels LCRS,j,REF and LACC,j,REF
according to the procedure of Annex 3
Calculate per gear and run the temperature adjusted constant speed test result LCRS,j,REF
Calculate per gear the acceleration test result LACC,REP,REF
For each individual pass-by measurement run j under constant speed the following values per gear are available: the reported sound levels LCRS,j, the vehicle speed vCRS,PP’,j and the air temperature CRS,j
For each individual pass-by measurement under acceleration the following values per gear are available: the reported sound levels LACC,j, the vehicle speeds vACC,PP’,j and vACC,BB’,j and the air temperature ACC,j
If the temperature TR of the tyre rolling sound reference differs by more than 3 °C from the reported temperature of an individual run, adjust at first the tyre rolling sound to the applicable temperature CRS,j or ACC,j of the individual run. For simplicity these temperatures are named TEST in all further formula below.

## Slide 4
Temperature Correction for Tyre Rolling Sound Components CASE 2
Case 2:
Tyre rolling sound has already been determined independently from the type approval and the air temperature normalized parameters LTR,DB,REF, reference speed vTR,DB,REF and the tyre sound level slope slpDB,REF are available
Adjust tyre rolling sound to vTEST (if needed)
Proceed to calculate LURBAN using the air temperature and test track adjusted sound pressure levels LCRS,j,REF and LACC,j,REF according to the procedure of Annex 3
Calculate per gear the temperature and test track adjusted constant speed test result LCRS,REP,REF
For each gear and run, determine the tyre rolling sound for the vehicle according to CASE 1 and extract the power train relevant components LPT,CRS,j and LPT,ACC,j
For each gear and run, adjust the tyre rolling sound LTR,DB,TEST to the speed condition of the acceleration test.
Calculate per gear the temperature and test track adjusted acceleration test result LACC,REP,REF

## Slide 5
Test Track Correction for Tyre Rolling Sound Components CASE 3
Case 3:
Case 3 is applicable for C2 tyres only and provides a correction for different test tracks without temperature correction. Parameters LTR,DB, reference speed vTR,DB,REF and the tyre sound level slope slpDB,REF are available
Adjust tyre rolling sound to vTEST (if needed)
Proceed to calculate LURBAN using the air temperature and test track adjusted sound pressure levels LCRS,j and LACC,j according to the procedure of Annex 3
Calculate per gear test track adjusted constant speed test result LCRS,j
For each gear and run, determine the tyre rolling sound for the vehicle according to CASE 1 and extract the power train relevant components LPT,CRS,j and LPT,ACC,j
For each gear and run, adjust the tyre rolling sound LTR,DB to the speed condition of the acceleration test.
Calculate per gear the test track adjusted acceleration test result LACC,j