## Slide 1
▶ R48 (GRE-84-05)
5.10.4.3. In case of doubt, the requirement above shall be deemed fulfilled if the luminous intensity of the red light emitted to the front and/or the white light emitted to the rear, as verified during type
approval of the lamps, is less than 0.25 cd per lamp taking into account the influence of the vehicle body if applicable.”
▶ R148 Series 01 (SLR-47-12)
4.8.3.1.1. In addition, in order to verify the visibility of red light towards the front and/or white light towards the rear of a vehicle required in UN Regulation No.48, the applicant may request
an additional test, to show that in the angular field from 165° to 180° outboard in horizontal direction and -2.5° to +5° in vertical direction, the maximum intensity is not more than 0.25 cd.
This additional test may be conducted taking into account the influence of the vehicle body.
▶ R149 Series 01 (SLR-47-13)
4.19. For any road illumination devices listed in paragraph 1, in order to verify the visibility of white light towards the rear of a vehicle required in UN Regulation No. 48, the applicant may request
a test, to show that in the angular field from 165° to 180° outboard in horizontal direction and -2.5° to +5° in vertical direction, the maximum luminous intensity is not more than 0.25 cd.
This additional test may be conducted taking into account the influence of the vehicle body.
Q. As far as I understand the additional test, the reference point for the test should be the farthest point from the
longitudinal plane in illuminating surface or light-emitting surface of the lamp.
However, I think there is no specific information about the reference point for the test in existing draft documents.
I’d like to ask if there is any possibility of misunderstanding or misuse such as testing it with axis of reference of the lamp.
SLR-48-09

## Slide 2
Answers (Dr. Kooss)
The measurement distance has to be chosen so that the inverse square law is valid.
A lateral distance from the reference axis to the outer edge of the light emitting surface can therefore only have an effect within the measurement uncertainty.
This is valid for the measurement within the grid as for all other measurement directions – even to the opposite side (180°).
Chassis parts may be simulated by shading with a tape or other means if necessary.