## Slide 1: ACSF Cat. C for Truck & Trailer
Concept of proposed amendments to UN R79 as proposed by GRVA/2021/11:
Amend Chapter 2: New definitions for the interface and data communication
Amend Chapter 5: New requirements specifying the interface and the detection area
Amend Annex 1: Add the types of possible combinations
New Annex 9*
„Compatibility between towing vehicles and
trailers with regard to data transmission
according to ISO 11992 for environmental
monitoring“
New Annex10*
„Test method for evaluating the functional
compatibility of vehicles with electrical control
cables“
* similar to UN-R13/11
Amend Annex 8: Add new tests for towing vehicle and trailer

## Slide 2: Motivation of the proposal for ACSF-C Truck & Trailer
Current R79 with passenger cars, rigid trucks and buses
* truck/trailer combination and tractor/semi-trailer combination
Additional Requirements in R79 for truck & trailer (N2/N3 with O3/O4)*
No change in the current approach in UN ECE R79.
Extension of the current regulation for N2/N3 power-driven vehicle and O3/O4 trailer w or w/o sensor capabilities. Introducing additional requirements to reflect these use-cases.
min. 55m
min. 55m

## Slide 3: Types of possible combinations
Possible with current regulation R79
Amendments for R79 for N2/N3 with O3/O4 trailer
Amend Annex 1 (Communication Sheet) to clearly show the possible combinations:
Power-driven vehicle with sensors
Power-driven vehicle with sensors
Power-driven vehicle with sensors
O3/O4 trailer without sensors (7.x.2)
No O3/O4 Trailer (7.x.1)
O3/O4 trailer with sensors (7.x.3. and 8.x.)

## Slide 4: Types of possible combinations
Power-driven vehicle
O3/O4 Trailer without sensors* (7.x.2)
Power-driven vehicle
No O3/O4 Trailer (7.x.1)
truck sensor
trailer sensor
min. 55m
min. 55m
* Includes trailer without sensor and trailer with sensor not used by the truck
Power-driven vehicle
O3/O4 Trailer with sensors (7.x.3. and 8.x.)
min. 55m
Copy approach as currently in R79

## Slide 5: Backup

## Slide 6: Summary of technical requirements
7.x.1 |  | yes | yes | No | yes | yes
7.x.2 |  | no | yes | No | No | yes
7.x.3 |  | no | no | yes | yes | yes
Requirements applicable to the power-driven |  |  |  |  |  | 
Possible combinations | Solo |  |  |  |  | 
 | With trailer |  |  |  |  | 
55m
55m
55m
8.x
55m
8.x
8.x
(*)
(*) the truck may not use the trailer sensors but rely on its own

## Slide 7: Types of possible combinations
Tests | Truck
3.5.1. Lane change functional test | x
3.5.2. Minimum activation speed test Vsmin. | x
3.5.3. Overriding test | x
3.5.4. Lane Change Procedure suppression test | x
3.5.5. Sensor performance test | x
3.5.6. Sensor blindness test | x
3.5.7. Engine start/run cycle test | x
3.5.8.1. Lane change suppression test* | 
3.5.8.2. Lane change suppression test* | 
3.5.9. Trailer Object detection test* | 
Truck | Trailer
x | 
x | 
x | 
x | 
x | 
x | 
x | 
x | 
Truck | Trailer
x | 
x | 
x | 
x | 
x | 
x | x
x | 
x | 
 | x
*New tests in red
truck sensor
trailer sensor
truck sensor
truck sensor
min. 55m

## Slide 8: Tests ACSF Cat. C for Truck & Trailer
Current tests in the regulation R79/03 suppl. 03:
3.5.1. Lane change functional test
System must be active to follow the test
Test for Truck only with a Trailer with or without sensors, depending on version of the towing vehicle
3.5.2. Minimum activation speed test Vsmin.
System must be active to follow the test
Test for Truck only with a Trailer with or without sensors, depending on version of the towing vehicle
3.5.3. Overriding test
System must be active to follow the test
Test for Truck only with a Trailer with or without sensors, depending on version of the towing vehicle
3.5.4. Lane Change Procedure suppression test
System must be active to follow the test
Test for Truck only with a Trailer with or without sensors, depending on version of the towing vehicle
3.5.5. Sensor performance test
System must be activ to follow the test
Test for Truck only with a Trailer with or without sensors, depending on version of the towing vehicle
3.5.6. Sensor blindness test
System must be active to follow the test
Test for Truck only with a Trailer with or without sensors, depending on version of the towing vehicle
Test for Trailer in a non dynamic situation
3.5.7. Engine start/run cycle test
System must be active to follow the test
Test for Truck only with a Trailer with or without sensors, depending on version of the towing vehicle

## Slide 9: Tests ACSF Cat. C for Truck & Trailer
New tests in the regulation R79 for CVs:
3.5.8. Lane change suppression test
System must be active to follow the test
Test for Truck only with a Trailer with or without sensors, depending on version of the towing vehicle
3.5.9. Trailer object detection test for trailers supporting lane change function(s) according to paragraph 8.x
System must be active to follow the test
Test for Trailer only with sensors