## Slide 1: Particle Measurement Programme (PMP)
Questionnaire: summary of replies
30 April, 2021

## Slide 2: Input
Number of replies: 12
OEMs and associations: 1+1+1+1+1+1+1 (=58%)
Instrument manufacturers: 1+1+1+1 (=33%)
Institutes: 1

## Slide 3: Q4: Definition of particles
PM number:
PN: 1+1+1+1 = 4 (33%)
SPN: 1+1+1+1+1+1 = 6 (50%)
No reply: 1 (but harmonization) + 1 (both PN and SPN)
Proposal: SPN for the resolution,
Attention in future R49, GTR15 to check

## Slide 4: VPR: Q1 (temperature), Q2 (catalytic stripper)
 | 23 nm (old in grey) | 10 nm
Requirements VPR evaporation tube | Include an initial heated dilution stage which outputs a sample at a temperature of ≥150 °C and ≤ 400°C 350 °C ±10 °C, and dilutes by a factor of at least 10. | Include an initial heated dilution stage which outputs a sample at a temperature of ≥ 150 °C and ≤ 350 °C ±10 °C, and dilutes by a factor of at least 10. Include a catalytically active part at a fixed (±10°C) wall temperature greater than or equal to that of the initial dilution stage. (only resolution)
Recommended system VPR evaporation tube | T=350°C (±10°C) from 300-400°C May be catalytically active | T=350°C (±10°C) Catalytically active

## Slide 5: Replies
Q1: Temperature between 150 and 350°C should change?
No (150-350°C): 1+1+1+1+1+1+1 = 7 (58%)
Yes (300-350°C): 1+1+1+1 = 4 (33%)
Q2: Catalytic stripper should be requirement?
No (remain at recommended system only): 1+1+1+1+1 = 5 (42%)
Yes (obligatory, C40 requirement not sufficient): 1+1+1+1+1 = 5 (42%)
Not clear answer: 1+1

## Slide 6: Proposal
Leave the text as it is:
(since 2007, only recommended systems are used, low risk to change it)
Requirements:
Temperature 150-350°C
No mention of catalytic stripper
Recommended system
Temperature 350°C
Catalytic stripper obligatory for SPN10, allowed for SPN23

## Slide 7: Tailpipe sampling with fixed dilution (HD)
Pre-diluter | A cold or hot pre-diluter may be located at the end of the particle sampling probe and in front of the PTT. A fixed dilution ratio >5:1 shall be applied to the cold or hot dilution stage. Cold dilution is defined as a dilution with (unheated) dilution air and/or diluter temperature ≥20°C.
Losses | The penetration for each model of pre-diluter shall be determined as described in A.8.2.2.4 The final system penetration (pre-diluter, PTT and VPR) shall not decrease 20% the requirements of A.8.1.3.3.6. The particle concentration reduction factors of each pre-diluter shall be determined as described in A.8.2.2.2. The complete system (pre-diluter, PTT and VPR) shall not exceed 10% for 50 nm, 20% for 30 nm, and 30% for 15 nm (if applicable) the requirements of A.8.1.3.3.4.
Sampling line | When sampling directly from the tailpipe the residence time until the pre-diluter or the VPR shall be ≤ 1 seconds. The tubing shall be heated at ≥150°C if >10 cm, otherwise only insulated. Any unheated parts shall be <10 cm
* in red not agreed

## Slide 8: Pre-diluter
Additional losses should be included in VPR: 1+1+1+1+1+1? = 6 (50%)
Not clear if current specs should increase.
Additional losses should not be considered: 1
More data needed: 1+1+1+1 = 4 (33%)
No reply: 1
Proposal: More data is needed. Penetration and PCRF ratio requirements open. Check if sampling line always heated (for all lengths) (unify)

## Slide 9: Tailpipe minor issues (HD)
Emission analyzers with automatic or manual range switching are permitted. During the test cycle, the range of the emission analyzers shall not be switched. (refers to gas analyzers)
Not PMP task: 1+1(but ok)+1+1(but ok)+1(probably ok)+1+1(probably ok) = 7 (58%)
Yes: 1
No reply: 1+1
Note: change of dilution should not allowed for PN systems: 1+1+1
Proposal: Leave the text as it is (auto range not allowed for gas analysers)

## Slide 10: Tailpipe minor issues (HD)
Sampling close to the engine (position representative to retention time in typical application) as to ensure an exhaust gas temperature of at least 343 K (70 °C) to avoid condensation at the probe.
Representative to retention time in typical application: 1+1+1
- Close to the engine seems inappropriate, as it should be close to the “end of the after-treatment system (e.g. after SCR, DPF, etc.). That is where “emissions” are defined.
- Is there a requirement to measure the exhaust temperature at the sampling position?
- Maybe a wording similar to LD RDE regulation “after a straight piece of exhaust pipe of at least x(5?)*diameter”.

## Slide 11: Proposal
Sampling from the exit of the exhaust manifold, turbocharger outlet, last aftertreatment device, or the in-use exhaust system, whichever is furthest downstream”. I would add the “to avoid (or minimize) condensation” to make clear why this statement is here
Sampling position representative to retention time in original exhaust system (End of exhaust system and point at which mixing with ambient air takes place). Good engineering practice should be encouraged to minimize condensation.
Proposal: Sampling downstream of the aftertreatment devices at a position representative to retention time in original exhaust system. Good engineering practice is encouraged to minimize condensation.

## Slide 12: Common calibration procedures
No replies: 1+1+1 = 3 (25%)
Neutral: 1+1 = 2 (17%)
Approach towards PMP procedures (1?+1+1+1) = 4 (33%):
PEMS with a CPC may yield results better comparable to the PMP results
PEMS calibration should be aligned with the PMP calibration. (x3)
Is it feasible?
Even if it would be possible, probably more difficult for calibration institutes ?

## Slide 13
Approach towards PEMS procedures (1+1+1) = 3 (25%)
Procedure according to ISO 27891:2015 with a soot-based aerosol (CAST) for both CPC and PEMS but with different acceptance criteria System efficiency determination (e.g. coefficient of variation (CV) < 25 %; η ± 0,07; zero criteria according to (EU) 2017/1151
Use of a uniform calibration aerosol: cast-soot aerosol pre-treated (dried)
Flexibility to allow both full-device or separate calibration, as the approach with the lowest experimental uncertainty may depend on the dilution concept.
Having a common set of criteria (i.e. overall device efficiency) that can be either directly or indirectly determined should be sufficient. This would also help reduce efforts/costs in re-establishing ISO certifications in accredited calibration lines.
The validation test of the PN-PEMS devices on the roller dynamometer against the particle counter installed should be mandatory
Narrow down the allowed limits of the system efficiency requirement for PEMS devices

## Slide 14
Regularly compare major calibration laboratories against each other
Establish a “standard aerosol” with very detailed definition (e.g. based on the work of NMIs)
Calibrate PMP system as a whole unit against traceable reference (e.g. CPC, electrometer); find out differences to established PMP procedure with separate CPC/VPR calibration
Make multiple calibrations and establish “repeatability” of the calibration for each instrument model (PMP system, PEMS)
Establish DMA error at 10, 15, 23 nm and influence of DMA error. Establish improved size standard for DMA size calibration
Every instrument may use whatever “calibration factor” (like the K-factor), but a requirement for overall penetration must remain, also a way to check flows for drifting away (similar to PEMS approach)
Include measurement uncertainty to final measurement result to improve transparency

## Slide 15: Common calibration procedures
Proposal:
Thermally stable soot-like calibration material
Common efficiencies (PMP and PEMS) (PEMS / black box approach)
Full device or parts calibration to derive efficiencies (ISO 27891 like)
Determine and include uncertainty for various sizes (depending on reference instrument, DMA, zero levels, repeatability)
Experimental campaigns
Input from NMIs and MetroPEMS project: https://www.metropems.ptb.de/home/

## Slide 16: Next steps (to be updated based on the discussion)
Accepted points will be included in the resolution (track changes or comments for PMP group to further comment)
The changes are based on the replies from the questionnaires (attached the presentation with the results)
Open points will be further evaluated experimentally (pre-diluter etc)
Common calibration procedures: A first proposal from JRC to be discussed in a small PMP group, then input from NMIs and then presentation to PMP group

## Slide 17: Keep in touch
EU Science Hub: ec.europa.eu/jrc
@EU_ScienceHub
EU Science Hub – Joint Research Centre
EU Science, Research and Innovation
EU Science Hub
Notes: Delete/update as appropriate

## Slide 18: Thank you
This presentation has been prepared for internal purposes. The information and views expressed in it do not necessarily reflect an official position of the European Commission or of the European Union.
Except otherwise noted, © European Union (year). All Rights Reserved
Slide xx: element concerned, source: e.g. Fotolia.com; Slide xx: element concerned, source: e.g. iStock.com