## Slide 1: Start timing of MRMLC
Time (second)
0
10
15
Warning to driver
by transition demand.
If an event happens, transition demand starts.
If the driver dose not respond
transition demand, MRM starts.
Warning to ORU
by hazard warning lights.
5s
Other road user should be warned that ALKS is in emergent situation because MRM LC dose not have enough capability of doing LC safely unless other road users specially take care of the ALKS movement.
Without this “5s”, other road user has no chance to be warned before the ALKS starts MRM LC.
the hazard warning lights : ON
the direction indicator : OFF
the hazard warning lights : OFF
the direction indicator : ON
the hazard warning lights : OFF
the direction indicator : OFF
Call attention, but Not warning to ORU by direction indicator
UNR157-11-06
11h SIG on R157
09,10 December 2021