## Slide 1
Proposal 1
We would like to delete the dimension of “a/3 “
that defines the distance between the circle and letters on Annex 2. Ⅰ, Ⅱ, Ⅲ, Ⅳ, and would like to define the letters position close to the circle for visibility.
e.g.
“The approval number must be placed close to the circle and must be in a position either above or below the letter "E" or to left or right of that letter.”
(The same as UNR#28 Audible warning device)
Justification
To provide the flexibility of marking design and its arrangements in the small space on audible reverse warning devices.
1/6
Japan proposes to change the following items
Annex 2. Ⅰ Page.37 on TFRWS-28-02 Rev1
Regarding Annex 2
Close

## Slide 2
Annex 2. Ⅲ Page.39 on TFRWS-28-02 Rev1
Annex 2 Ⅱ. Page.38 on TFRWS-28-02 Rev1
Please delete “a/3”
2/6
Please change “at a distance of a/3” to “Close”.
close
Japan proposes to change the following items

## Slide 3
3/6
Annex 2 Ⅳ. Page.41 on TFRWS-28-02 Rev1
Please delete “a/3”
Japan proposes to change the following items

## Slide 4
Correction 1
“Multiple audible reverse warning device”
shall be added to Annex 2 table 1.
Justification
“Multiple audible reverse warning device”
also have Class Ⅰ, Ⅱ, Ⅲ.
Refer to §2.6. Page 5 on TFRWS-28-02 Rev1
Regarding Annex 2
The excerption of Annex 2. Page.37 on TFRWS-28-02 Rev1
The excerption of Annex 2. Page.40 on TFRWS-28-02 Rev1
4/6
Japan proposes to change the following items

## Slide 5
Proposal 2
We would like to change the frequency range
of qualification criteria for anechoic chamber.
From 250Hz to 10kHz  From 500Hz to 4,000Hz
Justification
Audible reverse warning sound frequencies
are defined from 500 Hz to 4,000 Hz based on §2.7.
250Hz to 10kHz is over spec for anechoic chamber.
Over spec can be a capital investment burden for parts suppliers.
Regarding Annex 3
The excerption of Annex 3. Page.42 on TFRWS-28-02 Rev1
§ 2.7, Page.5 on TFRWS-28-02 Rev1
Qualification criteria for Anechoic chamber
5/6
Japan proposes to change the following items

## Slide 6
Correction 2
Measurement points shall be “A minimum of 4 points ”
Justification
Measurement point start at 0.5m with 0.15m of spacing to 1m, physically 10 points are not possible to measure…
Regarding Annex 3
Figure. 1
: Measurement
points
0.15m
The excerption of Annex 3. Page.42 on TFRWS-28-02 Rev1
Qualification criteria for Anechoic chamber
6/6
Japan proposes to change the following items