## Slide 1: A Follow-up to the Interpretation Question Raised by AEBS-HDV IWG to the 11th GRVA Session
Reference: GRVA-11-27-Rev.1
ADAS-10-05
Submitted by the TF on ADAS Co-Chairs
Informal document GRVA-12-XX
12th GRVA session 24-28 Jan. 2022
Provisional agenda item 7

## Slide 2: Background
GRVA noted the interpretation question raised in GRVA-11-27-Rev.1. GRVA invited the Special Interest Group (SIG) on Regulation No. 157 and the Task Force on ADAS to check it at a future occasion and agreed to discuss it back at the next GRVA session.
The next three slides (6-8 from GRVA-11-27-Rev.1) explain the issue.

## Slide 3: Open issues
Deactivation of AEBS
An agreement on the deactivation procedure is not yet reached
Specifically:
  Deactivation possible only below 10 km/h  from R152
  Request for guidance from GRVA-11
Definition of performance requirements
As in R152, performance requirements are given together with boundary requirements
Different interpretations of the text (copied from R152) possible
See next two slides for an introduction
After clarifying, the text in R152 might need to be aligned as well.

## Slide 4: Performance Req‘s (comparable to R152)
5.2.1.4. Speed reduction by braking demand
  In absence of driver’s input which would lead to interruption according to paragraph 5.3.2., the AEBS shall be able to achieve a relative impact speed that is less or equal to the maximum relative impact speed as shown in the following table:
  (a) For collisions with unobstructed and constantly travelling or stationary targets;
  (b) On flat, horizontal and dry roads affording good adhesion;
  (c) No trailer is coupled to the motor vehicle and the mass of the motor vehicle is between maximum mass and mass in running order conditions;
  (d) …
  It is recognised that the performances required in this table may not be fully achieved in other conditions than those listed above. However, the system shall not deactivate or unreasonably switch the control strategy in these other conditions. This shall be demonstrated in accordance with Annex 3 of this Regulation.
  [… Performance requirements table …]
Condition list in which the requirements have to be fulfilled
How to treat situations when conditions above are not met
Performance requirements in conditions above

## Slide 5: Problem Description
Clear:
  Not all conditions (a) – (…) are fulfilled
  Performance targets not required, but changing strategy not allowed
Unclear
  All conditions (a) – (…) are fulfilled
  An additional parameter (e.g. lane markings, lamp posts, fog, anything else) is introduced
How to deal with parameters not explicitly listed in the requirements, but obviously influencing the performance?
Request for Guidance from GRVA: What is GRVA’s interpretation?
Notes: […]
The group had divergent views on this item. While the contracting parties supported the position that the list of conditions from R152 should simply be adjusted for truck-specific additional constraints and otherwise the wording should be kept, while Industry was asking for additional conditions to be included which are not necesarily truck-specific, such as difficulties of the sensor system to interpret situations in the real world.
There was also a debate about how to interpret the wording „It is recognised that the performances required in this table may not be fully achieved in other conditions than those listed above.”. Industry shared the interpretation that adding other parameters would break the performance requirements. Another interpretation could be that the list of conditions is exhaustive, so including other parameters would be irrelevant to the performance requirements, those would still have to be fulfilled. Note that if changes and clarifications would need to be made, this is relevant for at least R152, probably also R157 as well.
The question is now, how do the parties present in GRVA interpret this concept.

## Slide 6: Consideration (1)
The raised question relates to the description of system boundaries.
The manufacturers establish boundaries for AEBS operation:
  Where AEBS meets the performance requirements of UN R 131/152;
  Where AEBS is operational and can mitigate the consequences of the collision;
  These boundaries include parameters influencing AEBS operation and had been taken into account by the manufacturers at the design stage;
  The manufacturers should describe all such boundaries in the type-approval documentation.
The intent is to have the manufacturers proactively outline some conditions, which may impact system performance, and which the type-approval authorities can take into account at the compliance assessment process.

## Slide 7: Consideration (2)
UN R 131/152 also can establish mandatory boundaries, within which AEBS shall be operational.
The manufacturers’ documentation should specify the conditions, where AEBS is operational:
  Those mandated by UN R 131/152;
  Additional boundaries that had been taken into account by the manufacturers at the design stage.
The AEBS performance can be verified under UN R 131/152:
  At mandatory conditions of UN R 131/152;
  At additional conditions according to the manufacturer’s documentation, if so is stipulated in UN R 131/152.

## Slide 8: Relevance to the ADAS TF Activity
The description of system boundaries is also relevant for DCAS and the declaration of such should be reflected in the draft UN Regulation.
  This proposal does not suggest an exhaustive list to be declared by the manufacturer, but rather would request the manufacturer to declare the conditions which were used as part in the manufacturer’s system design stage.

## Slide 9: Thank you for your attention!