| Transmitted by the experts from CLEPA and the Netherlands | Informal Document IWVTA-SG58-08-07 (8th IWVTA-SG58, 7-8 November 2013, agenda ite3.3) |
| --- | --- |

Harmonised numbering system for UN type approvals

A. Introduction:

At the 7th meeting of SG58 the working group agreed on schedule 6 of appendix 2 of the draft revised 1958 Agreement according the proposal as given in section II of document IWVTA-SGR0-04-04-Rev.3 on a harmonised numbering system.

However it is noted that the proposed text describing section 3 of the harmonised number contains a text between square brackets on which no decision has been taken and which is related to the fact that some regulations require a code  to be reflected in the approval markings. 

CLEPA and the Netherlands came to the conclusion that a code has only relevance for the approval markings, but that the proposed transitional provision (2) on approval markings at the end of section II of document IWVTA-SGR0-04-04-Rev.3 should take account of the existing application of approval codes or identification codes. Therefor CLEPA and the Netherlands suggest to delete “[or codes]“ in section 3 of the proposed approval number and to clarify the proposed transitional provision (2).

B. Proposals:

1.	In document IWVTA-SGR0-04-04-rev.3, section II, the wording for section 3 of the approval number should read:

“Section 3: 	A four-digit sequential number [or code] (with leading zeros as applicable). The sequence shall start from 0001.”

2.	In document IWVTA-SGR0-04-04-rev.3, section II, the wording for the transitional provision (2) should read:

“As from the entry into force of the [revised] 1958 Agreement and notwithstanding that the provisions on approval markings in any version of UN regulations may have stipulated otherwise, the manufacturer shall affix an approval mark, if requested, according the provisions of the relevant regulations however utilizing in that marking the first two digits of section 2 and the digits of section 3 of the approval number as mentioned in Annex 1 to appendix 2, Chapter 3 this schedule as approval number to each vehicle, system, component or part for which a new approval has been granted or for which such approvals have been extended; however this provision does not apply where a UN regulation requires an approval code or an identification code to be used in the approval mark in stead of an approval number. The leading zeros to section 3 may be omitted.”

______________________