## Slide 1: Particle emissions from Tyre and brake wear OPEN QUESTIONS
Sustainable Transport Unit
Institute for Energy and Transport
Joint Research Centre
8 January 2014

## Slide 2
Difficult to reconcile the many studies on the subject due to:
  Many different sampling methodologies/locations and measurement techniques
  Important differences between LD and HD vehicles
  Influence of driving conditions
  Lack of a clear definition of non-exhaust emissions especially for tyre and road wear and resuspended material
Nevertheless, in general, there is consensus on the emission factors
Literature study : Main issues

## Slide 3: TYRE AND BRAKE WEAR – EMISSION FACTORS
 | PM2.5 (mg km-1 veh-1) | PM10 (mg km-1 veh-1)
Brakes LDV | 2.1-5.5 | 2.0-8.0
Tyres* LDV | - | 3.5-9.0
EFs derived from road simulation studies
EFs derived from receptor modeling
 | PM2.5 (mg km-1 veh-1) | PM10 (mg km-1 veh-1)
Brakes LDV | 0.0-5.0 | 1.0-8.8
Tyres* LDV | 0.3-5.0 | 6.0-13
* Friction tyres
Brake and tyre wear PM10 EFs of HDVs are estimated to be approximately one order of magnitude higher compared to LDVs
Much higher PM10 EFs have been reported in case of studded tyres
In general emission factors of single sources for LD close to the Euro 4/5 mass standard
* Friction tyres

## Slide 4
World Health Organization: Health effects of particulate matter (2013)
The health effects of inhalable PM are well documented.
  respiratory and cardiovascular morbidity, mortality from cardiovascular and respiratory diseases and from lung cancer.
There is good evidence of the effects of short-term exposure to PM10 on respiratory health, but for mortality, and especially as a consequence of long-term exposure, PM2.5 is a stronger risk factor than the particles in the 2.5–10 μm range.
At present, at the population level, there is not enough evidence to identify differences in the effects of particles with different chemical compositions or emanating from various sources. It should be noted, however, that the evidence for the hazardous nature of combustion-related PM (from both mobile and stationary sources) is more consistent than that for PM from other sources.
Health effects of PM10 and PM2.5

## Slide 5
US EPA: Integrated Science Assessment for Particulate Matter (2009)
Health effects of PM10 and PM2.5
 | Causality determination |  |  |  |  | 
 | PM2.5 |  | PM(10-2.5) |  | UFP (<100 nm) | 
Outcome | Short term exposure | Long term exposure | Short term exposure | Long term exposure | Short term exposure | Long term exposure
Cardiovascular effects | Causal | Causal | Suggestive | Inadequate | Suggestive | Inadequate
Respiratory effects | Likely to be causal | Likely to be causal | Suggestive | Inadequate | Suggestive | Inadequate
Mortality | Causal | Causal | Suggestive | Inadequate | Inadequate | Inadequate
Reproductive and Developmental |  | Suggestive |  | Inadequate | Inadequate | Inadequate
Cancer, Mutagenicity, and Genotoxicity |  | Suggestive |  | Inadequate | Inadequate | Inadequate

## Slide 6
US EPA: Integrated Science Assessment for Particulate Matter (2009)
PM Sources and Constituents Linked to Health Effect
There is some evidence for trends and patterns that link particular ambient PM constituents or sources with specific health outcomes, but there is insufficient evidence to determine whether these patterns are consistent or robust.
For cardiovascular effects, multiple outcomes have been linked to a PM2.5 crustal/soil/road dust source.
There is less consistent evidence for associations between PM sources and respiratory health effects, which may be partially due to the fact that fewer source apportionment studies have been conducted that examined respiratory-related outcomes.
Overall, the results indicate that many constituents of PM can be linked with differing health effects and the evidence is not yet sufficient to allow differentiation of those constituents or sources that are more closely related to specific health outcomes
Health effects of PM10 and PM2.5

## Slide 7
Non-exhaust traffic related PM emissions significantly contribute to ambient PM10 and PM2.5
Several studies carried out on animals or in-vitro cells with sometimes contradictory results (different techniques and methodologies used) – Difficulties in extrapolating the results to humans
Fate of non-exhaust particles: Residence time? Dispersion? Exposure?
Soil and water contamination? (Not considered in the JRC literature study)
Health effects of non-exhaust particles

## Slide 8
Mass? The focus would be on large particles
Number? The focus would be on ultrafine particles
Both? Wide range of size to deal with
Physical properties or chemical composition of particles?
Chemical composition of brakes and tyres?
  Are particle generation mechanisms and influencing factors sufficiently known?
  Only in the case of brakes the source is linked exclusively to the vehicle
Sampling and measurement procedures:
  Representativeness of “real-world” emissions - Definition of “normal driving conditions”
What should we look at?

## Slide 9
Minimizing particle generation by changing chemical composition/physical properties of brakes and tyres?
Traffic and/or driving behaviour control measures? (e.g. speed limits, Low Traffic Zones, congestion charges,…)
Road conditions/characteristics? (e.g. road material, road maintenance, wetting/cleaning,…)
Cost/effectiveness?
What abatement measures?

## Slide 10
US EPA: Integrated Science Assessment for Particulate Matter (2009)
CAUSAL RELATIONSHIP
Evidence is sufficient to conclude that there is a causal relationship with relevant pollutant exposures.
LIKELY TO BE A CAUSAL RELATIONSHIP
Evidence is sufficient to conclude that a causal relationship is likely to exist with relevant pollutant exposures, but important uncertainties remain.
SUGGESTIVE OF A CAUSAL RELATIONSHIP
Evidence is suggestive of a causal relationship with relevant pollutant exposures, but is limited because chance, bias and confounding cannot be ruled out. For example, at least one high-quality epidemiologic study shows an association with a given health outcome but the results of other studies are inconsistent.
INADEQUATE TO INFER A CAUSAL RELATIONSHIP
Evidence is inadequate to determine that a causal relationship exists with relevant pollutant exposures. The available studies are of insufficient quantity, quality, consistency or statistical power to permit a conclusion regarding the presence or absence of an effect.
Health effects of PM10 and PM2.5

## Slide 11
US EPA: Integrated Science Assessment for Particulate Matter (2009)
Exposures to artificially generated particles may provide important information on the health effects of PM, but are not truly representative of ambient air pollution particles. The direct exposure of humans to ambient air pollution particles may be complicated by factors that cannot be controlled such as coexposures to other air pollutants (e.g., O3, SO2, and NO2). In concentrating ambient particles, gaseous copollutants are not proportionately concentrated and interactions between PM and the copollutant cannot be investigated unless the latter are re-introduced. These limitations as well as daily variability in concentration and composition can make it difficult to compare the results from controlled human exposure studies employing particles from different sources.
Animal toxicological studies explore the effects of pollutants on human health, especially through the study of model systems in other species. These studies evaluate the effects of exposures to a variety of pollutants in a highly controlled laboratory setting, and allow exploration of mechanisms by which a pollutant may cause effects. There are, however, uncertainties associated with quantitative extrapolations between laboratory animals and humans on the pathophysiological effects of any pollutant. The differences between humans and rodents with regard to pollutant absorption and distribution profiles based on breathing pattern, exposure dose, and differences in lung structure and anatomy all have to be taken into consideration.
Health effects of PM10 and PM2.5