## Slide 1: Japan position for EVE reference guide

## Slide 2
1 Introduction
1.1 Overview of EVE IWG
 | EVE reference guide recommendation | Japan positions (draft)
1.1 Overview of EVE IWG |  | Insert the text before the paragraph 1.1.1. as follows: When a recommendation of future GTR is proposed by the EVE IWG, it could be considered among the group of experts such as existing WLTP IWG under WP29 /GRPE, etc., whether it is feasible to develop a gtr for the recommended item.

## Slide 3
5.1 Vehicle Range & Energy Consumption Testing
 | EVE reference guide recommendation | Japan positions (draft)
5.1 Vehicle Range & Energy Consumption Testing | Heating be set to achieve (as quickly as possible) and subsequently maintain a specified, standard cabin temperature | Even though these equipment have more impact on the electrified vehicles than conventional vehicles, fuel consumption as well as range and energy consumption shall be measured under the same test protocol for all types of vehicles. WLTP IWG could take responsibility for these requirements including taking into account its necessity.
 | Requirements flexible enough to accommodate both resistive heating element and heat pump systems | 
 | Requirements flexible and extensible enough to accommodate future radiant heating solutions such as infra-red panels and foot wells | 
 | Requirements flexible enough to factor in additional luxury features that accomplish passenger heating – heated seats, heated steering wheel | 

## Slide 4
5.1 Vehicle Range & Energy Consumption Testing
 | EVE reference guide recommendation | Japan positions (draft)
5.1 Vehicle Range & Energy Consumption Testing | Air conditioning be set to achieve (as quickly as possible) and subsequently maintain a specified, standard cabin temperature | Currently independent IWG(MACTP) is active for this requirement. There is a possibility that this activity would be inserted to future WLTP gtr amendment. Therefore, WLTP IWG could take responsibility for these requirements including taking into account its necessity.
 | Requirements flexible enough to accommodate both electric air-conditioner systems as well as heat pumps | 
 | Requirements flexible and extensible enough to accommodate future cooling systems such as cooled seats. | It's not right timing to discuss these items at this moment because technologies are not mature.
 | Requirements flexible and extensible enough to accommodate future advanced solutions featuring smart materials | 
 | Requirements flexible enough to accommodate potential future active catalyst pre-heating systems for PHEVs | Current WLTP gtr draft already has similar requirement and shall be measured under the same test protocol for all types of vehicles.
 | In conjunction with the development of appropriate test procedures or gtr, consideration of additional research to quantify the impact of climate and auxiliary system operation on range and energy efficiency is recommended. | Current WLTP gtr draft already has similar requirement and shall be measured under the same test protocol for all types of vehicles.

## Slide 5
5.2 Method for Energy Conversion Formula
5.2 Method for Energy Conversion Formula | A standardized formula for calculating and stating energy consumption for electrified vehicles is therefore recommended for consideration. | It is necessary to clarify whether these items are within the mandate of WP29. Japan believes this item is out of scope of WP29. Japan suggests this item could be dealt with in other specialist body such as IEA.
 | EVE reference guide recommendation | Japan positions (draft)

## Slide 6
5.3 Battery Performance & Durability | Based on this mixed state of voluntary standards, it is recommended that a uniform propulsion battery test procedure be considered. | Gtr should focus on the vehicle base performance requirements, not parts level. In that sense, Japan suggests that the battery durability could be discussed in WLTP in relation to the emission deterioration, energy consumption and driving range in vehicle base. But, it might be huge challenge to develop the common test procedure.
 | It is recommended that the development of future test protocol or GTR attempt to capture this deterioration in performance at key points during the battery life-cycle. | 
 | It is further recommended that the outcome from any such deterioration testing be used to influence the reporting of vehicle range and energy efficiency. | 
5.3 Battery Performance & Durability
 | EVE reference guide recommendation | Japan position

## Slide 7
5.4 Battery Recycling | Pursuit of a GTR is therefore not recommended at this time. What is recommended is that resources be allocated to evaluate the value of developing manufacturing-for-recyclability requirements. | The word of “manufacturing-for-recyclability requirements” shall be defined.
5.4 Battery Recycling
 | EVE reference guide recommendation | Japan positions (draft)