## Slide 1
Mar,1,2022
Introduction of e-Call EMC in China

## Slide 2
Standard situation
In China, the National Technical Committee of Auto Standardization is in the process of applying for the establishment of the E-call standard, so Technical content is not clear yet.
There is no uniformly released and publicly available E-call EMC standard.
Some of tests are currently mostly R&D tests by OEMs.
Notes: （ISO号）

## Slide 3
Test situation
test set-up
Place the communication antenna diagonally behind the field generating device.
Simulate a 2G cellular network communication connection using a wideband radio communication tester, and play music.
test severity levels
100kHz-2GHz：70V/m @ CW，70V/m @ AM/PM.
Note: Skip the working frequency band of e-Call.
failure criteria/acceptance criteria
judging whether the music received is abnormal, such as volume and noise.
Notes: （ISO号）