## Slide 1: Proposal for ESA type approval
February 2022 (V1)

## Slide 2: Motivation
Clarification for REESS charging cables necessary
ESA test applicability flow chart can lead to misinterpretation: simplification needed

## Slide 3: Mobile charging cables
ESA test not applicable for mobile REESS charging cables
  A test setup for charging cables is defined neither in CISPR 25 nor in ISO 11452-2
  However, IEC 61851-21-2 provides a proper setup as it is intended to cover the designated use case of a vehicle charging cable connected to the power grid
Power grid
Mode 2 cable (ICCPD)
vehicle
Mode 3 wallbox
vehicle
Power grid
Devices attached to the power grid usually require a (national) type approval, e.g. CE within the EU.
For the purpose of type approval, testing acc. to international standards or national equivalents is required.
As the mode 2 cable is attached to the power grid, compliance with IEC standards or national equivalents (e.g. ENs or EN IECs) is already required.
The mode 2 cable shall not be considered to be an ESA to avoid double certification.
Clarification and update of flow chart is necessary!
The mode 3 wallbox is not considered to be an ESA; it is only tested according to IEC standards

## Slide 4: Conclusion (1)
Mode 1:
  If the cable is fixed at the vehicle: type approval with vehicle (this is clear because no other cable can be used)
  Mobile cable  normally passive cable  ESA test not applicable
Mode 2:
  IEC 61851-21-2:2018 covers ESA test from R10.06 in most cases
  IEC radiated emission method is different with other, yet stricter limits; wider frequency range depending on the highest internal frequency; measurement distance of 3m reasonable for foreseeable use case of charging in residential environment for the protection of off-board receivers; 1m in CISPR 25 refers to the protection of on-board receivers which is in the responsibility of the VM.
  IEC radiated immunity test does not cover ESA immunity test, but
      based on vehicle failure criteria in R10.06:
      - vehicle sets in motion
      - unexpected release of the parking brake
      - loss of Parking position for automatic transmission,
      Mode 2 cable can not technically cause any of the failures above. Testing in mode 3 allows the same disturbance to be coupled to the vehicle.
      ESA test not applicable: testing the mode 2 charging cable according to IEC 61851-21-2 or national equivalent is sufficient. ESA type approval or type approval of every kind of VM mode 2 charging cable in combination with the vehicle does not provide added value. By changing the mindset regarding the mode 2 interface regulatory burden will be reduced (see TF-EMC-25-03e).

## Slide 5: Conclusion (2)
Mode 3:
  Mobile cable: normally passive cable: ESA test not applicable
  Wallbox: usually requires (national) type approval due to the direct connection to the power grid
    E.g. for the purpose of CE marking, the European equivalent of IEC 61851-21-2, EN IEC 61851-21-2, is used
Mode 4:
  Cable is fixed at charging station: normally passive cable: ESA test not applicable
  DC charging station: usually requires (national) type approval due to the direct connection to the power grid
    E.g. for the purpose of CE marking, the European equivalent of IEC 61851-21-2, EN IEC 61851-21-2, is used

## Slide 6: Update of paragraph 7.1.3
The charging harness delivered by the manufacturer should be used preferably, but it is not necessary to type approve a mobile (not fixed at vehicle) charging harness with the vehicle:
„a“

## Slide 7: Update of flow chart 3.2.1
Electrical/electronic sub assembly (ESA) classification
ESA for fitment into vehicles and mechanically fastened* or connected to the vehicle wiring harness?
Passive ESA or system?
Use restricted by technical means to immobilized vehicle?
Application of Regulation No. 10
No application of Regulation No. 10
Yes
No (e.g. detachable REESS charging cable, remote key, USB powered portable equipment or connected to the cigarette lighter interface)
Yes (e.g. lifting platform)
No
Yes (e.g. broadcast receivers, ambient lights, protection against vermins)
No
After market equipment without immunity related functions?
Yes (e.g. spark plugs, cables, passive antenna)
No
*mechanically fastened = with the use of tools for (de-)installation or provided clips intended to fasten the component

## Slide 8: Additional Information
The next slides show a simplified comparison for the mode 2 charging cable:
IEC 61851-21-2 vs. ESA type approval according R10.06.

## Slide 9: Simplified Comparison: Immunity (1)
Port | Immunity Mode 2 Charging Cable | IEC 61851-21-2 (AC charging immunity requirements – Environments other than residential) | R10.06 ESA Type Approval | Comment
Enclosure | ESD | ±4 kV contact, ±8 kV air | Not available | 
 | Radiated Immunity | 80 to 1000 MHz: 10 V/m 1,4 to 2,7 GHz: 3 V/m | 800 mm Stripline, TEM Cell, BCI, ALSE; ALSE: 20 to 2000 MHz: 30 V/m | To be discussed
 | Magnetic Fields | 50; 60 Hz 30 A/m (for systems ≤ 32 A) 100 A/m (for systems > 32 A) | Not available | 
AC Input | Burst | ±4 kV | ±2 kV | 
 | Surge | Line to earth ±4 kV Line to Line ±2 kV | Line to earth ±2 kV Line to Line ±1 kV | 
 | Conducted RF Fields | 0,15 to 80 MHz: 10 V | Not available | 
 | Voltage Dips and interruptions | 40 % residual voltage 70 % residual voltage 0 % residual voltage 0 % residual Voltage | Not available | 

## Slide 10: Simplified Comparison: Immunity (2)
Port | Immunity Mode 2 Charging Cable | IEC 61851-21-2 (AC charging immunity requirements – Environments other than residential) | R10.06 ESA Type Approval | Comment
Wired network and signal control | Burst | ±2 kV | Not available | 
 | Surge | ±1 kV | Not available | 
 | Conducted RF Fields | 0,15 to 80 MHz: 10 V | Not available | 
CPT | Burst | ±2 kV | Not available | 
 | Surge | ±1 kV | Not available | 
 | Conducted RF Fields | 0,15 to 80 MHz: 10 V | Not available | 

## Slide 11: Simplified Comparison: Emission
Port | Emission Mode 2 Charging Cable | IEC 61851-21-2 (Class B equipment) | R10.06 ESA Type Approval | Comment
Enclosure | Radiated disturbances (above 30 MHz) | Limits from IEC 61000-6-3 * QP and AV at 3 and 10 m distance; 30 MHz to 6 GHz depending on highest internal frequency | Measurement distance 1 m (CISPR 25): ESA Broadband limit (QP) [dBµV/m]: 30-75 MHz: 62 - 25.13 log(f/30) 75-400 MHz: 52 + 15.13 log(f/75) 400-1000 MHz: 63 ESA Narrowband limit (AV) [dBµV/m]: 30-75 MHz: 52 - 25.13 log(f/30) 75-400 MHz: 42 + 15.13 log(f/75) 400-1000 MHz: 53 | Stricter limits in IEC standard
 | Radiated disturbances (2 kHz to 185 kHz) | Only DC charging equipment | Not available | Only DC charging equipment
AC Input | Harmonic currents | IEC 61000-3-2:2014 (≤ 16 A/phase) IEC 61000-3-12:2011 (> 16 A, ≤ 75 A/phase) | IEC 61000-3-2:2014 (≤ 16 A/phase) IEC 61000-3-12:2011 (> 16 A, ≤ 75 A/phase) | 
 | Voltage fluctuations and flicker | IEC 61000-3-3:2013 (≤ 16 A/phase) IEC 61000-3-11:2017 (> 16 A, ≤ 75 A/phase) | IEC 61000-3-3:2013 (≤ 16 A/phase) IEC 61000-3-11:2017 (> 16 A, ≤ 75 A/phase) | 
 | Conducted disturbances (150 kHz to 30 MHz) | Limits from IEC 61000-6-3 QP and AV | Limits from IEC 61000-6-3* QP and AV | 
Wired network and signal control | Conducted disturbances (150 kHz to 30 MHz) | Limits from IEC 61000-6-3* QP and AV | Limits from IEC 61000-6-3* QP and AV | 
CPT | Conducted disturbances (150 kHz to 30 MHz) | Limits from IEC 61000-6-3* QP and AV | Limits from IEC 61000-6-3* QP and AV | 
 | Transient emissions | Only DC charging equipment | N/A | Only DC charging equipment
*generic emission standard for residential environment