## Slide 1: OICA Input to SIG-05
Restructuring of the Japanese Proposal
March 2022

## Slide 2: OICA Proposal to SIG-05
OICA Approach
OICA has tried to group the lamps used outside of the normal condition of use. In this way performance requirements can be assigned to lamp groups/use cases.
The terms proposed by OICA Temporary [usage] lamp, task lamp etc.. are certainly not 100% fixed. They helped us to group the lamps but can be improved for greater understanding by all parties.
A lamp check (test) and operation indicator are new additions that were not covered in the Japanese proposal.
The paragraph numbering within the OICA proposal is also open for re-arranging in case certain sections would be better placed elsewhere.

## Slide 3: OICA Proposal to SIG-05
OICA Approach
Temporary Usage lamps - shall not exceed an intensity of [700]cd, except driving beam headlamps where the maximum luminous intensity is restricted to [3,500]cd.
    - Approved lamps may be switched ON as lamps as defined in §2.7.8. provided the maximum luminous intensity is in compliance with the technical provisions for the lamp concerned. This is not permitted for Reverse lamps, DRLs above [700]cd and driving beam above [3,500]cd.
- However, Manually controlled lamp checks may be performed in any condition.
The temporary [usage] lamp may operate to indicate ongoing processes for as long as they apply. If the underlying condition for activation ceases to exist, they must be switched OFF.
Operation Indicator - The duration of the operation indicator shall not exceed 3 seconds for status changes.