## Slide 1: Working Paper No. WLTP-05-12
1
Item 5, Overview of key issues of WLTP Phase 1B
Cycle/Process:
Downscaling/Gearshifting
Proposal by H. Steven
04.01.2014

## Slide 2: Downscaling, current status
2
The downscaling procedure is specified in paragraph 7 of annex 1.
The method as such is agreed, but paragraph 7.3 “Determination of the downscaling factor” needs to be amended.
  India requests modifications of the calculation parameter/coefficients r0, a1 and b1 and made already a proposal for amendments (see WLTP-DHC-18-05). This issue is related to # 5 of WLTP-05-04.
  Calculation parameter/coefficients for torque meter method should be added (see # 4 of WLTP-05-04).

## Slide 3: Downscaling, current status
3
Another point that needs clarification is related to paragraph 7.4 of annex 1 “Additional requirements”.
The text, that specifies the drive instructions in case the vehicle cannot follow the trace of the downscaled cycle does not exclude the activation of a “kick-down” for automatic transmission vehicles.
In addition to that an error in formula 6 of paragraph 7.2.2 of annex 1 needs to be corrected.
It should read “with i = 1520 to 1724” instead of “with i = 1520 to 1725”.

## Slide 4: Downscaling, next steps
4
# 5 of WLTP-05-04 (modifications of r0, a1 and b1):
  HS will perform calculations based on the Indian amendment proposal, analyse the results and discuss possible compromise proposals with the Indian colleagues (February – March 2014).
  Validation/verification tests should be performed by India (March - April 2014).
  After these tests HS will draft an amended text for paragraph 7.3 of annex 1 (May 2014).
  The possible activation of a “kick-down” for automatic transmission vehicles in case the vehicle cannot follow the trace of the downscaled cycle will be discussed with interested parties.

## Slide 5: Downscaling, next steps
5
# 4 of WLTP-05-04 (Calculation parameter/coefficients for torque meter method):
  HS will develop the necessary formulae, discuss them with Japan and deliver an amended text by May 2014.

## Slide 6: Gearshifting, current status
6
The gearshift prescriptions for manual transmission vehicles are specified in annex 2 of the GTR.
The following issues are listed in WLTP-05-04 for further amendments:
  Special gearboxes or auxiliary gearboxes (e.g. exclusion of “crawler” gears), see # 6 in WLTP-05-04.
  Addition of formulas based on the torque meter method, see # 7 in WLTP-05-04.
  Skipping of gears, see # 8 in WLTP-05-04.
To point 3 the skipping of the 3 s rule for acceleration phases, the modification of the safety margin for the full load power curve etc. (sailing?) should be added.

## Slide 7: Gearshifting, current status
7
In addition to that a further point is listed in WLTP-05-04, which should be added to the gearshift prescriptions:
  Development of gear shift family criteria, see # 9 in WLTP-05-04.
The application of regional temperatures should be considered for this point.

## Slide 8: Gearshifting, next steps
8
# 6 of WLTP-05-04 (special gearboxes or auxiliary gearboxes):
  HS will perform calculations based on input from the task force to be established, analyse the results and discuss possible proposals with the TF (February – April 2014).
  The specifications of ECE R 83 (annex 4, paragraph 6.1.3) will be considered.
  Amended text for annex 2 (May 2014).
  This time schedule needs to be extended, if validation tests will be necessary.

## Slide 9: Gearshifting, next steps
9
# 7 of WLTP-05-04 (Addition of formulas based on the torque meter method):
  HS will develop the necessary formulae, discuss them with the TF and deliver an amended text by July 2014.
# 8 of WLTP-05-04 (Skipping of gears etc.):
  HS will perform calculations based on input from the TF, analyse the results and discuss possible solutions/proposals with the TF (– May 2014).
  Validation tests (– August 2014).
  Amended text for annex 2 (September 2014).

## Slide 10: Gearshifting, next steps
10
# 9 of WLTP-05-04 (Development of gear shift family criteria):
  The necessary steps for this issue will be drafted after preparatory discussions with Japan.