## Slide 1: Temperature Correction of Tyres
Special Case in UN-Regulation No. 51.03
Paragraph 3.3.4 in Annex 3, Appendix 2

## Slide 2: Temperature Correction of Tyres Special Case
Source: simulation of Ulrich Messer

## Slide 3: Temperature Correction of Tyres Special Case
The problem occurs mainly with BEVs due to the minimal powertrain sound component
Problem:
  Tyre rolling sound @ cruising is higher than the overall sound level @ acceleration
  Powertrain sound component can’t get negative and is set to 1% of overall level
  Recompositing of Lurban based on Tyre Rolling sound @ cruising leads to higher values due to the overestimation of tyre component
Reason:
  simplification of the temperature model uses tyre rolling sound @cruising adjusted to averaged speed between PP’ and BB’ for recompositing Lwot, ref
  if the maximum sound level is before PP’ the situation gets worst
Measures in this special case
  New definition of tyre rolling sound @ acceleration (two approaches)
A: Accelerated Tyre rolling sound set to vref and ref (no speed correction) based on cruising condition

## Slide 4: Temperature Correction of Tyres Special Case
B: Accelerated tyre rolling sound adjusted to a virtual speed lower than vTR,ref

## Slide 5: Temperature Correction of Tyres Special Case
C1: Reported Lurban is set to Lcrs
Justification:
  that means Lcrs>Lwot.
  In this case only Lcrs should be used final sound level as Lurban for Annex 3. Otherwise Lurban is less than Lcrs.
  lower sound level than Lcrs as final value in Annex 3 does not makes sense for regulation
C2: Reported Lurban is set to Lcrs