## Slide 1: 30th Session User working stream
Paris / Hybrid Conference
19 - 21 July 2022

## Slide 2: Status
 | Safety Requirements for ‘The ADS shall interact safely with the authorized user in the vehicle’
9 | User interaction with and the interface of ADS (features) shall have a high-level commonality of design
10 | The ADS HMI shall provide clear and unambiguous information to the user
11 | The ADS shall be designed to prevent misuse and errors in operation
12 | The ADS shall be designed to assure a safe ADS feature activation
13 | An ADS which permits or can request a user intervention shall be designed to assure a safe Transition of Control
14 | The ADS which permits a transition of control shall be designed to assure a safe user initiated take over.
15 | The use of the ADS shall be supported by documentation and tools to facilitate the authorized user in understanding the functionality and operation of the system
16 | The integration of an ADS which permits a transition of control with the entire vehicle HMI shall be assured

## Slide 3: Status
10 | The ADS HMI shall provide clear and unambiguous information to the user | The vehicle shall indicate its ADS capabilities in terms of their automated [features] and their ODD. The ADS shall inform the user on the current conditions: ADS status information The availability of automated features User Role Responsibility Permitted NDRA Potential roles to activate “Standard” information Vehicle speed, range and Time to Fuel ADS failure information The ADS shall inform the user on the upcoming conditions: ODD boundaries Upcoming actions or change in roles Oncoming decisions/manoeuvers Estimated time until take over in normal conditions Transition related communication. The ADS shall ensure that safety related information is prioritised and presented in a clear and unambiguous manner.

## Slide 4: Status
take over; activation; unplanned and planned ToC
activation; take over; planned ToC
activation; take over
SR 9 - 16
SR 9 - 16
SR 9, 10, 11, 12, 14, 15
An ADS which permits or can request a user to intervene in the DDT
An ADS which does not permit or will not request a user to intervene in the DDT
SR 10; Safety stop
‘activation’

## Slide 5: Status
Goods
Shared vehicle
Private vehicle
Interface to operator; Interface for maintainance; Interface remote control
FRAV: some SRs
E.g., maintainance: some provisions of SR #9, #10, #11, #12, #15.
Interface to passenger; Interface to operator; Interface for maintainance; Interface remote control
FRAV: some SRs
Interface to ADS user; Interface for maintainance; Interface remote control
FRAV: some SRs
An ADS which does not permit or will not request a user to intervene

## Slide 6: Status
 |  | VMAD pillars | Requirement needs | Remarks
User interaction with and the interface of ADS (features) shall have a high-level commonality of design. | · The ADS should be designed to foster a level of trust that is aligned with its capabilities and limitations to ensure proper use of the system. | Audit | There is currently no general specification to be able to check whether there is a high level of commonality. If such a commonality exists then a checklist would suffice. | 
 | · The operation of the interaction shall have in common: |  |  | 
 | o [use of common sequence of states in the transition/activation/overriding/…] |  |  | 
 | · The interaction should be simplified: |  |  | 
 | o [Limit the number of roles] |  |  | 
 | o [Limit the number of potential transitions] |  |  | 
 | o [Limit the number of settings] |  |  | 
 | o [Limit the number of different interaction modes] |  |  | 
The ADS HMI shall provide clear and unambiguous information to the user. | · The vehicle shall indicate its ADS capabilities in terms of their automated [features] and their ODD. | Audit; test track or real world with a wide diversity of typical drivers (this is an extensive test); human out of the loop simulation. | For the audit it should be ensured that a user centred design process in the development of an ADS is implemented and followed. Such a user centred design process should be developed. Some of the detailed provisions can be checked through a checklist; Standardisation on icons/earcons is needed (relates to commonality). | Whether the information is indeed clear and unambiguous should also be checked through driving on test track or real world with a wide diversity of naive drivers (this is quite an extensive test). The correct functioning of the HMI can be tested through human out of the loop simulation.
 | · The ADS shall inform the user on the current conditions: |  |  | 
 | o ADS status information |  |  | 
 | o The availability of ADS features |  |  | 
 | o User Role |  |  | 
 | o Responsibility |  |  | 
 | o Permitted NDRA |  |  | 
 | o Potential roles to activate |  |  | 
 | o “Standard” information: |  |  | 
 | § Vehicle speed, range and Time to Fuel |  |  | 
 | o ADS failure information |  |  | 
 | · The ADS shall inform the user on the upcoming conditions: |  |  | 
 | o ODD boundaries |  |  | 
 | o Upcoming actions or change in roles |  |  | 
 | o Oncoming decisions/manoeuvers |  |  | 
 | o Estimated time until take over in normal conditions |  |  | 
 | o Transition related communication. |  |  | 
 | · The ADS shall ensure that safety related information is prioritized and presented in a clear and unambiguous manner. |  |  | 
The ADS shall be designed to prevent misuse and errors in operation. | · The ADS shall be designed to prevent inadvertent activation or deactivation. | Audit | A user centred design process should be developed. | This could be part of the common specification
 | · The controls dedicated to the ADS shall be clearly distinguishable from other controls. |  |  | 
 | · The ADS shall provide feedback when the user attempts to enable unavailable functions. |  |  | 

## Slide 7: Till 2023 Users
Work on the level of detail below the provisions
  Since technology is not matured, research is necessary to evaluate the best solutions for standards
    Commonality is not there yet
    Research is needed which is not done within FRAV
  To develop and gain experience in the success of different HM Interaction solutions the guidelines need to be clear enough to give direction and do give a certainty for future development (avoid depreciation through regulation)
Standards & recommendations on HMI (e.g., symbols, tale-tales)

## Slide 8: Till 2023 Users
Work on the state diagram for activation, de-activation (take-over), and transfer of control
    Outcome could be a 0.0 version
  Commonality related to this topic
  High level assessment
  Some functional tests
Interface with VMAD
  Verifiable criteria will be difficult in this stage
  Items to be assessed are feasible
  Recommendations are more related to assessment than fixed test methods
Interface with TF ADAS

## Slide 9: Till 2023 Users
User roles
  a lot of light between driver and user
There are many different users with different skills
  averages won’t work!
Driver readiness
Merge all into doc 5