## Slide 1: An Approach to DCAS Validation: Implementation of the NATM Techniques
Submitted by the TF on ADAS Co-Chair
ADAS 14-08

## Slide 2: Background
Documentation:
  Draft DCAS UN Regulation (Master Document) (ADAS-14-02)
  ADAS use case compilation document (ADAS-08-04)
  NATM Second Iteration & Guidelines (ECE/TRANS/WP.29/2022/57 & …/58)
Reasons:
  Although DCAS is intended to assist the driver, DCAS is a (set of) partial automation system(s)
  Similarly to validating of ADS, validating of DCAS looks more complex rather than validating of single ACSF per UN R 79. At least, a comprehensive audit of manufacturer’s documentation is needed

## Slide 3
1958 Agreement Compliance Assessment Chart
 | Approval |  |  |  |  |  |  | Post- Approval | 
Traditional compliance assessment | Analysis of the manufacturer’s documentation | Product identification | Physical tests/checks (may be substituted by simulation) |  |  | COP assessment |  | COP Inspection | 
NATM | Audit of the manufacturer’s documentation | Product identification | Scenario-based: |  |  | COP assessment |  | COP Inspection | In-service monitoring & reporting
 |  |  | Virtual tests | Track tests | Road tests |  |  |  | 
The width of the cells is not time-scaled.
The NATM elements are more comprehensive compare to those of traditional compliance assessment.

## Slide 4: Validation of DCAS: Audit of the manufacturer’s documentation
The draft DCAS UN Regulation (Master Document) already many times set the provisions requesting the manufacturers to provide to the approval authority the comprehensive documented evidence of compliance, so that for the DCAS compliance assessment, the audit of the manufacturers’ documentation based on the NATM techniques should be carried out.

## Slide 5: Validation of DCAS: Track Testing
Track testing should be the basic part of physical checks of DCAS performance, therefore for the DCAS compliance assessment the track testing pillar of the NATM should definitely be involved.

## Slide 6: Validation of DCAS: Road Testing
Road testing supplements track testing.
Road testing is needed to assess DCAS capabilities in real conditions according to the declared capabilities. In particular, the interaction between DCAS and the driver and between the DCAS vehicle with other vehicles should be verified.
As some real-world driving situations cannot be simulated on the test track, for the compliance assessment of DCAS, such situations should be identified and verified through road testing.

## Slide 7: Validation of DCAS: Virtual Testing / Simulation
Simulation supplements and partly substitutes the physical testing.
Simulation allows to assess DCAS performance under wide diverse conditions within DCAS operational boundaries provided that the simulation model is validated and verified.
Simulation can cover safety-critical conditions that would be difficult and/or unsafe to reproduce on test tracks or public roads.
Thus, simulation allows to save time and reduce expenses and risks associated with physical tests, so that simulation is a relevant pillar of the NATM that should be used for the compliance assessment of DCAS.

## Slide 8: Validation of DCAS: Scenarios
According to the NATM, a scenario is a description of one or more real-world driving situations that may occur during a given trip.
So, scenarios refer to the conditions, under which virtual and physical tests are carried out.
In the DCAS UN Regulation, scenarios should represent the following conditions:
  DCAS normal operation;
  DCAS failure (and involvement of the driver);
  Driver’s failure (detection of the driver’s disengagement).
In the DCAS UN Regulation, scenarios do not need to be detailed as described in the NATM. The meaning of “scenario” is “the set of conditions” for a specific virtual or physical test of DCAS. But scenarios are understood similarly as they are understood in the NATM.

## Slide 9: Validation of DCAS: In-service Monitoring and Reporting
Similarly to ADS, DCAS should be assessed regarding the in-service safety after market introduction.
As DCAS interacts with a driver, it is important to monitor the concerns arising from such interaction to identify the driver’s misuse, overreliance, confusion, etc.
In the DCAS UN Regulation, in-service monitoring should address e.g.:
  DCAS failures
  Driver’s failures (detection of the driver’s disengagement)
  Road accidents.
Thus, in-service monitoring and reporting pillar of the NATM should be applied also for the purpose of compliance assessment in the DCAS UN Regulation.

## Slide 10: Conclusion
The validation of DCAS similarly to the validation of ADS should comprise the pillars and techniques introduced in the NATM.

## Slide 11: Question to the ADAS TF
Would the ADAS TF support the approach to the compliance assessment of DCAS by implementing the techniques introduced by the NATM?

## Slide 12: Thank you for your attention!