## Slide 1: Luc Goubert, Belgian Road Research Centre 21st meeting of the IWG Measurement Uncertainty hybrid meeting
The STEER uncertainty analysison the EU Tyre (Noise) Label

## Slide 2: Regulation No 117 of the Economic Commission for Europe of the United Nations (UNECE)

## Slide 3: Regulation No 117 of the Economic Commission for Europe of the United Nations (UNECE)
Regulation No 117 (UNECE):
Controlled Coast By-method
(smooth) ISO 10844 test track
Test vehicle equipped with 4 tyres to be tested
Two sided measurements
At least 16 runs

## Slide 4: Uncertainty analysis
Category name | Category #
Equipment | 1
Experimental set up | 2
Measurement conditions | 3
Measurement | 4
Test vehicle | 5
Test track | 6
Test tyres | 7
Calculation | 8
41 “sources of uncertainty” identified in whole procedure, classified in 8 categories
Analysis complying with GUM*
*ISO/IEC Guide 98-3:2008 (E) Uncertainty of measurementPart 3: Guide to the expression of uncertainty in measurement (GUM: 1995)

## Slide 5: Uncertainty contribution from the test track
ETRTO1: 0,92 dB
M+P: “old” RRT of 20052: max-min difference about 4 dB
Recent Swiss study3: 1,3 dB
Expert vision within consortium: about 1 dB
1ETRTO, 2019. Tyre noise uncertainties in UN Regulation No. 117,
Presentation at 2nd Meeting of GRBP Task Force, Brussels, 28-29 November 2019.
2Van Blokland, G., Peeters, B., 2006. Comparison of surface properties of ISO 10844 test tracks.
3Bühlmann, E., Schlatter, F., Sandberg, U., 2021.
Temperature influence on tire/road noise measurements:
Recently collected data and discussion of various issues related to standard testing procedures.
Proc. INTER-NOISE 2021 - 2021 Int. Congr. Expo. Noise Control Eng. https://doi.org/10.3397/IN-2021-1830

## Slide 6: Uncertainty contribution from the test tyres
Sample to sample variations: 0,26 dB1 up to 0,42 dB2
“Tyre family” effect: 0,59 dB up to 1,1 dB3
1ETRTO, 2019. Tyre noise uncertainties in UN Regulation No. 117,
Presentation at 2nd Meeting of GRBP Task Force, Brussels, 28-29 November 2019.
2STEER analysis from the data base from a tyre manufacturer
3Swedish-Polish study carried out in the margin of STEER project (see § 4,2,5 of STEER Final Report)

## Slide 7: Uncertainty contribution from the test vehicle
ETRTO1: 0,51 dB
STEER analysis2: 0,60 dB
1ETRTO, 2019. Tyre noise uncertainties in UN Regulation No. 117,
Presentation at 2nd Meeting of GRBP Task Force, Brussels, 28-29 November 2019.
2extracted from the data base from a tyre manufacturer

## Slide 8: Uncertainty contribution from the measurement conditions
Main uncertainty contribution is from the temperature correction: 0,59 dB1
1 § 3.3.7 of STEER Final Report

## Slide 9: Uncertainty analysis: results
Chart: Uncertainty contribution per uncertainty group (C1 tyres)
| equipment | experimental set up | meas. conditions | measurement | test vehicle | test track | test tyres | calculation | overall
min | 0.15478 | 0.02 | 0.59331 | 0.15115 | 0.55073 | 0.9 | 0.64475 | 0.26 | 1.4127
max | 0.15478 | 0.02 | 0.59331 | 0.15115 | 0.63498 | 1.24 | 1.1775 | 0.26 | 1.9478

## Slide 10: Detailed STEER MU analysis: see Annex 1 of STEER Final Report

## Slide 11: ETRTO uncertainty analysis (received from Truls on 15-09-2022)

## Slide 12: ETRTO uncertainty analysis (with my comments/questions)

## Slide 13: Senior research scientist Belgian Road Research Centre
Luc Goubert
0474/508356
l.goubert@brrc.be
www.brrc.be