## Slide 1: Summary of the STEER – ETRTO meeting on 9 March 2023
IWGMU-23-03, Agenda item 6.1
Washington, 22 March 2023
Report by Truls Berge, SINTEF
IWGMU-23-03

## Slide 2: Participants:
From STEER:
Ulf Sandberg, Luc Goubert, Erik Bühlmann, Truls Berge
From ETRTO: Michael Steffan, Marco Tosca, Nicola Pieroni, Thijs Weegerink, Anna Malosio, Hannu Onnela (also partner in STEER), Per-Uno Sturk (OICA)
Agenda items:
Measurement uncertainties for Reg.117
Temperature corrections – proposal from ETRTO

## Slide 3: 1. Measurement uncertainties for Reg117:
Luc Goubert made a short presentation of the STEER work on MU, the same given by him at the IWG MU meeting in Paris in November 2022 (IWGMU-21-06). Based on this work, Luc presented a revised table of the expected uncertainties, using the same approach as for ECE Reg.51.03 and ISO 362. This table will be revised by ETRTO before developing an Informal Document to the next GRBP meeting.
Then followed a discussion on the different quantities, especially related to test vehicle and tyre influence to the uncertainty budget. Input from came from Marco Tosca, referring to the MU table presented by ETRTO at the 2nd meeting of IWG MU (TFMU-02-02 Rev.1), where the tyre standard uncertainty was calculated to ± 0,5 dB (including 95% confid.) and the vehicle influence to ± 1,0 dB. This is then in agreement with the table given in TFMU-02-02 Rev.1

## Slide 4: MU - continued
It was agreed that it is difficult to put values on the different test vehicle design features to the variation in pass-by levels, such as underbody clearance, wheel house design and weight influence. Then, it was agreed that this variation can be up to ± 2,0 dB, giving a standard deviation (uncertainty contribution of 0,5 dB. This gives a contribution of ± 1,0 dB with 95 % confidence interv, (k=2).
For the tyre influence, it was agreed to set this value to 1 dB p-p. (tyre variations of the sane type, not "family" variations). This gives a standard deviation (uncertainty contribution) of 0,25 dB. In the STEER Final Report, the tyre contribution was estimated to be in the range of 0,26 to 0,42, so the value chosen is in agreement with STEER, but in the lower range.
No further disagreement on other quantities were found between STEER and ETRTO

## Slide 5: 2. Temperature corrections – proposal by ETRTO
Michael Steffan gave the same presentation as given to GRBP in February (GRBP-77-12) explaining the reason behind the revised procedure for road surface temperature corrections for C1 (normal and 3PMSF tyres).
After some discussion about the approach and methods used for developing the correction procedure, it was a general agreement from both parties that a correction based on road surface temperature would be preferable, as the relationship between tyre temperature and pass-by noise clearly is a non-linear process. However, measurements of the tyre temperature is not a straightforward process.
Steffan expressed his concern about using a linear process (as proposed by ISO) to correct for a non-linear process.
Ulf Sandberg pointed out that it is not only the non-linear glass transition process that influence the pass-by noise, but also damping, stick-slip and stick-snap.

## Slide 6: Temp. corr. - continued
Both parties agreed on that for future research a combination of air and road surface temperature, can be a better solution.
An investigation of the relationship between air and road surface temperature on ISO tracks in different climatic zones should be promoted.
Erik Bühlmann, as convener of ISO WG27 (temperature influence) invited Michael Steffan to make he same presentation for this group. Steffan will certainly do this at the next WG27 meeting (not yet scheduled.

## Slide 7: Thank you!