## Slide 1
OIL#12 | coast down procedure (Annex 4)
Discussion points | gtr description : Selection of reference speeds for road load curve determination Coast down method : on the truck4.3.1.1. , on the dyno. 8.1.3.2. Torque meter method : on the truck4.4.2., on the dyno. 8.2.2. <concerns> With the current description the following example would be possible and could depending on the curve and the properties of the vehicle - create an error. How should someone (Technical Service, NGO, …) know what speed-points were taken for the measurement? Coast Down: 20-40-60-80-100-115-130 km/h and Dyno: 20-30-50-70- 90-110-130 km/h <<counter-proposal>> fix the speed points at 20-40-60-80-100-115-130 km/h with the 15 km/h-steps at higher speeds because a better accuracy at higher speeds (resulting in higher energies) yields more accurate overall cycle energy.
Proposal | keep current gtr description.
Justification | Error possibility and amount of error does NOT depend on set reference speeds. Dyno. set curve is checked within tolerance anyway. Record keeping needs to be defined in other sections. On the other hands, “fixed reference speed” or “same reference speed for on the truck and on the dyno.” create negative impact on testing practicability. e.g. “fixed” : reference speed may differ depend on truck configuration “same” : difficult to truck the reference speed in different laboratories.
WLTP-06-05e by Japan