## Slide 1: Working Paper No. WLTP-06-10-rev1e
1
Agenda item 5: Status report on
Downscaling / Gearshifting (OIL #4-9)
by H. Steven
26.03.2014
6th WLTP IWG meeting, 26.-28. March 2014

## Slide 2: Downscaling, issues to be treated
2
The downscaling procedure is specified in paragraph 7 of annex 1.
The method as such is agreed, but paragraph 7.3 “Determination of the downscaling factor” needs to be amended.
  India requests modifications of the calculation parameter/coefficients r0, a1 and b1 and made already a proposal for amendments (see WLTP-DHC-18-05). This issue is related to # 5 of WLTP-05-04.
  Calculation parameter/coefficients for torque meter method should be added (see # 4 of WLTP-05-04).

## Slide 3: Downscaling, issues to be treated
3
Another point that needs clarification is related to paragraph 7.4 of annex 1 “Additional requirements”.
The text, that specifies the drive instructions in case the vehicle cannot follow the trace of the downscaled cycle does not exclude the activation of a “kick-down” for automatic transmission vehicles.
In addition to that an error in formula 6 of paragraph 7.2.2 of annex 1 needs to be corrected.
It should read “with i = 1520 to 1724” instead of “with i = 1520 to 1725”.

## Slide 4: Downscaling, current status, next steps
4
OIL # 5 of WLTP-05-04 (modifications of r0, a1 and b1):
  Calculations based on the Indian amendment proposal were performed. The analysis is still ongoing, because there was some delay in the data exchange between India and HS.
  A compromise proposal can be expected till 11.04.2014), followed by validation/verification tests by India (execution and dates to be confirmed).
  After these tests HS will draft an amended text for paragraph 7.3 of annex 1 (May 2014).

## Slide 5: Downscaling, current status, next steps
5
    The possible activation of a “kick-down” for automatic transmission vehicles in case the vehicle cannot follow the trace. It is proposed to discuss this issue within the gearshift prescriptions TF.
# 4 of WLTP-05-04 (Calculation parameter/coefficients for torque meter method):
  The problem was clarified between Japan and HS (coast down method delivers f0, f1 and f2, torque meter method delivers C0, C1 and C2).
  For the solution of this problem the results from OIL #14 and OIL #15 are required.
  As soon as these are available, an amended text for paragraph 7.3 of annex 1 will be drafted.

## Slide 6: Gearshifting, current status
6
The gearshift prescriptions for manual transmission vehicles are specified in annex 2 of the GTR.
The following issues are listed in WLTP-05-04 for further amendments:
  Special gearboxes or auxiliary gearboxes (e.g. exclusion of “crawler” gears), see OIL # 6 in WLTP-05-04.
  Addition of formulas based on the torque meter method, see OIL # 7 in WLTP-05-04.
  Skipping of gears, see OIL # 8 in WLTP-05-04.
To point 3 the skipping of the 3 s rule for acceleration phases, the modification of the safety margin for the full load power curve etc. (sailing?) should be added.

## Slide 7: Gearshifting, current status
7
A gearshift prescription task force was established meanwhile, consisting of the following persons:
  Annette Feucht, Audi,
  Takahiro Haniu, JARI,
  Christophe Griard, PSA,
  Nick Arden, Ford,
  Jos van de Venne, Ford,
  Henrik Malberg, Volvo cars,
  Christoph Lueginger, BMW,
  Peter Gaertner, Volkswagen,
  Heinz Steven, DAC (TF leader)

## Slide 8: Gearshifting, current status
8
The issue list, which built the basis for the discussions, contains the following points:
  Corrections in the current text (paragraph 3.2),
    n_max (should be 90% for all gears except highest gear instead of 120%),
    Correction of requirements for n_min for 2. gear, (the current text is insufficient),
  Specification of rated engine speed in case of a Prated plateau,
  Review 3 s rule for acceleration phases,
  Review gear use at a transition from an acceleration phase to a cruise phase,

## Slide 9: Gearshifting, current status, next steps
9
Continuation of the actual issue list:
  Additional speed depending safety margin (decreasing with increasing engine speed, optional or mandatory or depending on technology?),
  Assess the possibility of skipping of gears during acceleration phases,
  Assess the exclusion of auxiliary gears (crawler gears) in the gearshift prescriptions,
  Implementation of a sailing option, in case this measure will be agreed for the GTR,
  Add calculation formulas based on road load values from the torque meter method,

## Slide 10: Gearshifting, current status, next steps
10
A first web/telco took place at 20.03.2014, a face to face meeting (with web/telco possibilities) is planned for April.
The following text reflects the minutes of this web/telco:

## Slide 11: Gearshifting, current status, next steps
11
Corrections in the current text (paragraph 3.2 of annex 2 of the GTR)
There are two points in the current text, that need to be corrected and/or further specified, namely n_max and n_min_2.
In addition to that, the additional requirements for corrections and/or modifications of gear use (see paragraph 4 of annex 2 of the GTR) need to be specified more precisely and the rank order of these requirements needs to be checked.

## Slide 12: Gearshifting, current status, next steps
12
Specification of rated engine speed in case of a Prated plateau
The chairman explained the issue and presented his proposal for a solution.
From the following discussion can be concluded, that this is a good starting point but that it needs to be reconsidered more thoroughly.
This issue is mainly related to the specification of n_min_drive. Some members of the group expressed the request, that the determination formula for n_min_drive needs to be reconsidered in order to take into account differences in the available power at low engine speeds between different engine configurations (Diesel/Petrol, turbocharged/naturally aspirated).

## Slide 13: Gearshifting, current status, next steps
13
Review 3 s rule for acceleration phases
The chairman introduced this issue and presented the results of gearshift calculations with and without this rule for a variety of vehicle configurations.
Skipping the 3 s rule has a high influence (reduction) on the maximum engine speed in 1. gear, but this influence decrease significantly for higher gears. The average engine speed is not influenced much.
A colleague from Ford showed results for in-use driving behaviour data analysis, that supports the skipping.
The Japanese colleagues reminded the group, that the 3 s rule was originally introduced by them, expressed some concerns to skip it and requested more time for consideration.

## Slide 14: Gearshifting, current status, next steps
14
Review gear use at a transition from an acceleration phase to a cruise phase
Annette Feucht pointed out that it should be possible to allow upshifts by two gears at the transition from an acceleration phase to a cruise phase, if the available power would be high enough to ensure driveability, because this would be in line with practical use for today’s vehicles. This argument was supported by the European members of the group.
In order to implement this requirement into the GTR, it would be necessary to define boundary conditions for acceleration, cruise and deceleration phases.
The Japanese colleagues expressed scrutiny reservations.

## Slide 15: Gearshifting, current status, next steps
15
Additional speed depending safety margin (decreasing with increasing engine speed, optional or mandatory or depending on technology?)
This request was raised by vehicle manufacturers from India and Europe with regard to downsized, high pressure turbocharged engines.
In the current tool such measure is already foreseen with the additional margin fully applied at idling speed and linearly reduced to 0 at rated (reference) speed.
The discussion resulted in the need for differences between different engine configurations (Diesel/Petrol, turbocharged/naturally aspirated)
Christophe Griard and Henrik Malberg promised to prepare proposals for the further discussion.

## Slide 16: Gearshifting, current status, next steps
16
Assess the possibility of skipping of gears during acceleration phases
Although there seemed to be some reservation within the group to support such a possibility, Christoph Lueginger argued that this possibility could gain more reasoning, if the 3 s rule would be skipped. The group agreed on further consideration of this issue.

## Slide 17: Gearshifting, current status, next steps
17
Assess the exclusion of auxiliary gears (crawler gears) in the gearshift prescriptions
The chairman pointed out that this is a justified request but one would need robust technical, not design related delimitation criteria. It should be proven, that the crawler gear(s) have significant higher ratios than and that the ratio of the next higher gear corresponds to a “normal” 1. gear.
Nick Arden mentioned that this request came from Ford and showed a short presentation with justifications and a proposal for delimitation criteria.
It was agreed that this presentation should be distributed to the group for further consideration.

## Slide 18: Gearshifting, current status, next steps
18
Implementation of a sailing option, in case this measure will be agreed for the GTR
The chairman pointed out that another TF of the WLTP IG is dedicated to the “sailing” option for deceleration phases (see OIL # 31). If it will be agreed to implement this option into the GTR, the gearshift prescriptions (annex 2) need to be amended accordingly.
No further discussion took place in the group.

## Slide 19: Gearshifting, current status, next steps
19
Add calculation formulas based on road load values from the torque meter method
The chairman pointed out that discussions with the TF’s working on annex 4 are necessary before this task can be performed, in order to clarify the problem and work on solution proposals.
This statement was supported by Annette Feucht and Christoph Lueginger. Annette Feucht gave further explanations of the problem. Both promised to work on proposals to solve the problem.

## Slide 20: Gearshifting, current status, next steps
20
It is planned to deliver results for WLTP-07, but this is very much depending, whether validation tests will be required.
  For point 8 the results from OIL #31are required.
  For point 9 the results from OIL #14 and OIL #15 are required.
  As soon as these are available, an amended text for the corresponding sections of annex 2 will be drafted.

## Slide 21: Gearshifting, current status, next steps
21
Time schedule:
  Necessary calculations based on input from the TF, the analysis of the results and the discussion/development of possible solutions/proposals shall be finished in May 2014).
  Validation tests, if necessary till end of August 2014,
  Amended text for annex 2 till end of September 2014.

## Slide 22: Gear shift family criteria
22
In addition to that a further point is listed in WLTP-05-04, which should be added to the gearshift prescriptions:
  Development of gear shift family criteria, see OIL # 9 in WLTP-05-04.
The application of regional temperatures should be considered for this point.
For this point the GP TF will be co chaired by Japan and HS.
The necessary steps for this issue will be drafted after preparatory discussions with Japan.