|  | United Nations | ECE/TRANS/WP.29/GRSG/2014/XX |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 10 March 2014 Original: English |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

Working Party on General Safety Provisions

107th session

Geneva, 30 September–03 October 2014

Item XX of the provisional agenda

Regulation No. 125 (Forward field of vision of drivers)

Proposal for amendments to Regulation No. 125 (Forward field of vision of drivers)

Submitted by the expert from OICA

The text reproduced below was prepared by the expert from the International Organization of Motor Vehicle Manufacturers OICA *and is supported by the GRSG Informal Working Group Camera Monitor Systems.

Regulation No. 125 exempts rear-view mirrors from the requirement on obstructions within the forward field of vision of drivers.

Clarification is needed on how to treat devices for indirect vision (e.g. camera monitor device) that are intended to replace rear-view mirrors.

The additions to the current text of the Regulation are marked in red bold.

I.	Proposal

Paragraph 5.1.3. amend to read:

5.1.3.

Except as provided in 5.1.3.1 or 5.1.3.2., other than the obstructions created by

the A pillars, the fixed or movable vent or side window division bars, outside radio

aerials, rear-view mirrors devices for indirect vision 5) and windscreen wipers, there should be no obstruction in the driver’s 180° forward direct field of vision below a horizontal plane passing

through V1, and above three planes through V2, one being perpendicular to the

plane X-Z and declining forward 4° below the horizontal, and the other two being

perpendicular to the plane Y-Z and declining 4° below the horizontal (see Annex

4, appendix, figure 4).

The following are not considered to be obstructions to the field of vision:

(a) 	Embedded or printed “radio aerial” conductors, no wider than the following:

(i) Embedded conductors: 0.5 mm,

(ii) Printed conductors: 1.0 mm. These “radio aerial” conductors shall not cross zone A 4). However, three “radio aerial” conductors may cross zone A if their width does not exceed 0.5 mm.

(b) 	Within zone A located “defrosting/demisting” normally in “zigzag” or sinusoidal form having the following dimensions:

(i) Maximum visible width: 0.030 mm,

(ii) Maximum conductor density:

a. If the conductors are vertical: 8/cm,

b. If the conductors are horizontal: 5/cm.

4) As defined in Annex 18, paragraph 2.2. of Regulation No. 43 concerning the approval of safety glazing and glazing material.

5) In case of camera monitor device, the exemptions of 5.1.3. apply to cameras including their holders which are mounted to the vehicle exterior. The camera monitor system replacing a rear view Class I mirror only shall have the same exemption.

II.	Justification

Rear-view mirrors (inside and outside) are exempted from UN-Regulation No. 125. Reason: To comply with the field of vision required by UN-Regulation No. 46, both rearview mirrors and cameras must be mounted in a specific position.

The obstruction of the direct vision by an outside mounted camera compared to an outside mirror will significantly improve and in some cases the need for a specific position remains. Therefore, this exemption shall be extended to the outside mounted cameras and its holders.

It shall be allowed to position the monitor which displays the required field of vision of inside mirrors at the same location as today’s inside mirrors (this position is typically at the upper windshield area):

The traditional location of the interior rear view mirror is the best place to prevent from glare and reflection issues. In addition, all drivers are trained and used to get the information of rear vision at that place. Consequently, the monitor for indirect vision of Class I needs the same exemption as the interior rear view mirror.

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2010–2014 (ECE/TRANS/208, para. 106 and ECE/TRANS/2010/8, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.