## Slide 1: Annex 12 #2.6.4 Camera Monitor arrangement
IGCMS-II-03-12

## Slide 2: First proposal for location of the different display areas
  “The arrangement of the monitor(s) inside the vehicle shall be in such a way as expected by a driver.
  This means, that the image of the right side field of view shall be presented to the right of the longitudinal vertical plane passing through the ocular reference point, defined in paragraph 12.1. The image of the left side field of view shall be presented to the left of the longitudinal vertical plane passing through the ocular reference point.
  If the CMS shows more than one FOV on one display, non-continuous images shall be clearly separated from each other.”

## Slide 3
Left
Right
Monitor Arrangement
Situation with mirrors
Right FOV
Left FOV
Central FOV

## Slide 4
Left
Right
Monitor Arrangement
ALLOWED with CMS
Right FOV
Left FOV
Central FOV

## Slide 5
Left
Right
Monitor Arrangement
Right FOV
Left FOV
Central FOV
ALLOWED
Not recommanded
« What is in front of the driver should be dedicated to forward driving informations »

## Slide 6
Left
Right
Monitor Arrangement
Right FOV
Left FOV
Central FOV
ALLOWED
Not recommanded
« What is in front of the driver should be dedicated to forward driving informations »

## Slide 7
Left
Right
Monitor Arrangement
Right FOV
Left FOV
Central FOV
ALLOWED
Not recommanded
« What is in front of the driver should be dedicated to forward driving informations »

## Slide 8
Left
Right
Monitor Arrangement
Right FOV
Left FOV
Central FOV
FORBIDDEN
This is an issue for OICA

## Slide 9
Left
Right
Monitor Arrangement
Right FOV
Left FOV
Central FOV
FORBIDDEN
This is an issue for OICA

## Slide 10: OICA new proposal
  “The arrangement of the monitor(s) inside the vehicle shall be in such a way as expected by a driver.
  This means, for a left hand drive vehicle, that the image of the right side field of view shall be presented to the right of the longitudinal vertical plane passing through the ocular reference point, defined in paragraph 12.1. The image of the left side field of view shall be presented to the left of the longitudinal vertical plane passing through the ocular reference point.
  Notwithstanding the above requirements, in case where the left and right fields of view are shown on one display, the central axis of the display may be located between the longitudinal vertical plane passing through the ocular reference point and the median longitudinal plane of the vehicle.
  If the CMS shows more than one FOV on one display, non-continuous images shall be clearly separated from each other.”

## Slide 11
Left
Right
Monitor Arrangement
Right FOV
Left FOV
Central FOV
ALLOWED
With OICA proposal

## Slide 12
Left
Right
Monitor Arrangement
ALLOWED
With OICA proposal
Right FOV
Left FOV
Central FOV

## Slide 13
Left
Right
Monitor Arrangement
ALLOWED
With OICA proposal
Right FOV
Left FOV
Central FOV

## Slide 14
Left
Right
Monitor Arrangement
FORBIDDEN
Agreed
Right FOV
Left FOV
Central FOV