## Slide 1
5th session of TF-QRTV
MU improvement by multi-microphone
2023/2/6-7
JAPAN AUTOMOBILE STANDARDS INTERNATIONALIZATION CENTER
TF-QRTV-05-02

## Slide 2
<Background>
ISO WG42 has undertaken a systematic analysis of measurement uncertainty of ISO 16254 according to the principles of the GRBP TF MU. As one of the uncertainty reduction, it is proposed to use 5 microphones in the height between 0,6 m … 1,6 m height instead of one mic in the height of 1.2m. To confirm the appropriate microphone numbers and locations, experimental verification was carried out by Japan.
<Result>
Adding microphones in the vertical direction is effective for reducing Measurement Uncertainty.
From this test result, about 5 microphones seems to be appropriate number.
Summary
Current
1.2ｍ
1.2ｍ
2.0ｍ
2.0ｍ
ISO proposal
2.0ｍ
2.0ｍ
0.8ｍ
0.8ｍ~1.6ｍ
0.2ｍ interval (5 mic)
Fig1. Microphone location (current)
Fig2. Microphone location (ISO proposal)
TF-QRTV-05-02

## Slide 3
Measurement condition
Sound source:
・Single speaker with white noise (Considered not to be affected by vehicle reflections)
・Longitudinal/Vertical directions: almost the same position as the actual mounting position
・Lateral direction: vehicle CTR(①)
Number of measurement points: 220 points
・Vertical: 22 points × longitudinal:５ points × lateral(LH/RH): 2 points × 1 speaker locations
Location:
・Indoor (free sound field space that satisfies ISO26101)
2500mm
<Side view>
<Plan view>
FR
CTR
LH
RH
Speaker height: 700mm
Speaker①
Mic Position II is shifted 50mm from Mic Position I.
Measured at each position and acquired data of 22 points at 50mm intervals.
Mic Position II
Mic Position I
TF-QRTV-05-02

## Slide 4
Result: location① CTR
White noise: LH side microphone result (difference among frequency, microphone location and height）
White noise: RH side microphone result (difference among frequency, microphone location and height）
White noise
White noise
RH
LH
H mm
H mm
Adding microphones in the vertical direction is effective for reducing Measurement uncertainty.
From this test result, about 5 microphones seems to be appropriate number.
big
low
〇dB
〇dB
TF-QRTV-05-02