## Slide 1: Automated and connected road transport France’s views on the use of scenarios
Submitted by the expert from France VMAD-28-05
Website : https://www.ecologie.gouv.fr/en/automated-vehicles

## Slide 2
Outline
Scenario-based approach
  Roots in VMAD recommendations
  Rationale of French approach
  Status of work
  Ideas for next steps

## Slide 3: FR scenario approach rooted in ECE/TRANS/WP.29/2022/57
Main recommandations made by VMAD | 
Coverage principle | Holistic and dense coverage of traffic situations
Scenario catalogue | VMAD will establish a catalogue of scenarios […]
Edge scenarios | Adequate coverage of relevant, critical, and complex scenarios Identifying unexpected scenarios Unsafe behaviours of other road users —if reasonably foreseeable—should be included in the scenario catalogue
Link with ODD | catalogue of scenarios […] relevant to the ODD (using standardised ODD taxonomy)
Common descriptors | Standardized and structured language for describing scenarios…
Combinations | …combining a number of relevant elements

## Slide 4: Scenarios : main rationale underlying the FR approach
  1. Support completeness of foreseeable traffic hazards’ analysis
  Ease scenario generation towards completeness, through
    Data-based & Evidence-based
    +
    Specific work on descriptors
      Fine decomposition of descriptors’ axis
      Multiple combination of descriptors
      Extension of descriptors’ axis and descriptors’ values
        Including according to data and evidence-bases
      Encompass regulatory scenarios
        e.g.: Highway code; injunctions from law enforcement; priority vehicles

## Slide 5: Scenarios: main rationale underlying the FR approach (cont’ed)
  2. Proportionate safety demonstration via scenarios :
  2.1 According to criticality
        low criticality = e.g. self declared consideration  very critical = e.g. mandatory test
        mandatory pre-defined scenarios ↔ random approach
    2.2. Articulating generic scenarios versus ODD-specific scenarios
    Articulate scenarios to be scrutinized
      at vehicle level
        at system level (cf. remote capabilities)
        on a specific route or zone
  3. Support traceability, transparency & explicability
  Address possible societal coverage issues
    (e.g. scenarios with disabled).

## Slide 6: Scenario descriptors: FR doctrine
  Macro-axes (functional layers)
  Static traffic environment
    geometric configuration of the infrastructure +
    static signalling and traffic rules (speed, restricted areas)
  Nominal manœuvre (« intended manœuvre »)
  Hazards
    collision precursor event (“targets”)
    technical failures of the system
    (NB : visibility impairments are described in axis 5 below)
  System response
  Hazards affecting response
    unexpected masks
    visibility and adhesion conditions
    system failures
    adaptive behaviour of other collision precursors
OE
D
R

## Slide 7: Iterative process for scenario generation
Accident data bases
Real world data
Descriptors’ axis
Analytical hasard-based
Concept based
Knowledge based
Data based
Axis combination
Scenario library (descriptors, values)
Combinatory
Extended scenario library (descriptors, values)

## Slide 8: Iterative process for scenario generation linked to NATM pillars
Scenario generation,
feeding and enrichment
Concept based
Knowledge based
Data based
Scenario library (descriptors, values)
Combinatory
Extended scenario library (descriptors, values)
NATM pillar 1:
Simulations / virtual testing
NATM pillar 2:
Track testing
NATM pillar 3:
Real-world testing
NATM pillar 5: in service monitoring
NATM pillar 4: Audit

## Slide 9: Iterative process of scenario generation & use
Lists (descriptors, attributes, scenarios)
Combinatory
Scenario databases or sources
Nominal scenarios
from design activities, induced by intended use (ODD, OEDR, route, …)
Accident scenarios
accidentology (representative of the intended use)
Scenarios from risk analysis
related to functional insufficiencies
related to failures
Scenarios based on driving
during system development
during “in-service monitoring”
Scenario generation & classification
NATM pillar 1:
Simulations / virtual testing
NATM pillar 2:
Track testing
NATM pillar 3:
Real-world testing
NATM pillar 5: in service monitoring
NATM pillar 4: Audit
Assessing the completeness of scenarios addressed by the system
White run on route

## Slide 10
  Static traffic environment
  Nominal driving manoeuvre
  Hazards
    Collision precursor events
    Technical system failure
  System response
  Hazards affecting system response
                Visibility
    Other road user behaviors
    Failures
Link between ODD definition and scenarios
Complete ODD
“nominal” ODD
“nominal environmental conditions” ODD
“nominal addressable events” ODD

## Slide 11: French views on the follow-up in VMAD
VMAD should provide a methodology to generate scenarios for all use cases, including highway chauffeur but also urban situations and freight
  This methodology should make it possible to standardize layers of description and descriptors
  This methodology should be linked with ODD description
  NB : completeness of the scenario catalogue may depend more on layers, descriptors and attributes than on building functional scenarios based on collected data or hazards
  This methodology should highlight the iterative substance of scenario generation
VMAD should elaborate guidance on the minimum set of scenarios appropriate to (to be defined) macro-use cases (= scenario catalogue(s))
VMAD should issue a guidance on the updating process to the scenario catalogue and its lists of descriptors/attributes

## Slide 12: French views on the follow-up in VMAD
The “reasonably foreseeable” is one of the most important principle to achieve systems’ safety demonstration and validation
“Foreseeability” shouldn’t solely rely on collected (field-based ou system-based) scenarios but also on a sound (desk-top) process to conceive all possible scenarios with which the system could be confronted
This process could be based on de-composing and combining scenarios’ axis and set as an additional pillar of the scenario approach
Accident data bases
Real world data
Descriptors’ axis
Analytical hasard-based
Concept based
Knowledge based
Data based
Axis combination

## Slide 13: French views on the follow-up in VMAD
Generating reasonably foreseeable scenarios should combine or encompass :
  Nominal and failure scenarios
  Traffic hazards and failure scenarios
  Conceivable edge or critical
  Situations with several alter road users outside the ego vehicle (e.g. masking the scene)
  Driving behaviours offending traffic rules
  « Fuzzy » scenarios in terms of respecting driving rules (e.g. right to cross horizontal signage in order to overtake a vehicle encroaching the lane)
  Foreseeable situations though individual road users behaviours might not be foreseeable (e.g. restless crowded spots)
  Reasonably Foreseeable must tent towards Reasonably Conceivable

## Slide 14: Thank you for your attention – more details available on https://www.ecologie.gouv.fr/en/automated-vehicles

## Slide 15: Annex 1 French library on scenario-based approach and principles
Methodological documents available at:
https://www.ecologie.gouv.fr/en/automated-vehicles
https://www.ecologie.gouv.fr/sites/default/files/DGITM_Approche-par-scenarios-fevrier-2022-EN.pdf
https://www.ecologie.gouv.fr/sites/default/files/DGITM-L1-septembre_2022-EN.pdf
https://www.ecologie.gouv.fr/sites/default/files/DGITM_Approche-par-scenarios-fevrier-2022-EN.pdf
https://www.ecologie.gouv.fr/sites/default/files/DGITM-ODD_dezscriptors-juin_2022-EN.pdf
Guideline documents available at:
http://www.strmtg.developpement-durable.gouv.fr/
Scenario database (MOSAR) = application of methodological and technical principles
& national closed-access reference documents = scenario requirements

## Slide 16: Annex 3: Safety reference documents for automated transport systems 1/3
Theme / title | Document | State | Remarks (EN versions for recent methodological documents)
Horizontal regulation - use case approach | Methodological document DGITM | Published 2017 | https://www.ecologie.gouv.fr/sites/default/files/DGITM_Automated-vehicle-horizontal-regulation-2017-EN.pdf EN version
New safety validation methods | Methodological document DGITM-PFA | Published2020 | https://www.ecologie.gouv.fr/sites/default/files/DGITM_Nouvelle-approche-validation-systemes-avril-2019-EN.pdf FR version only
Human/system articulation: manoeuvre approach | Methodological document DGITM | Published 2020 | https://www.ecologie.gouv.fr/sites/default/files/DGITM_AD-articulation-roles-systemes-octobre-2020-EN.pdf FR version only
Characterisation of the routes: division into sections | Research report UGE-STRMTG | Published 2021 | https://www.ecologie.gouv.fr/sites/default/files/DGITM_STPA-analyse-securite-parcours-mars-2021-EN.pdf FR vesrion only
Application of the GAME approach | Implementation Guide STRMTG | Published 2021 | https://www.ecologie.gouv.fr/sites/default/files/DGITM_Guide-application-STRA-principe-GAME-EN.pdf FR version only
Scenario-based validation approach | Methodological document DGITM | Published 2022 | https://www.ecologie.gouv.fr/sites/default/files/DGITM_Approche-par-scenarios-fevrier-2022-EN.pdf EN version

## Slide 17: Safety reference documents for automated transport 2/3
Theme / title | Document | Deadline | Remarks
Scenario validation: interactions with law enforcement and priority vehicles | Methodological framework document DGITM | Published 2022 | https://www.ecologie.gouv.fr/sites/default/files/DGITM_Approche-par-scenarios-fevrier-2022-EN.pdf EN version
Accidentology references for safety objectives | Research report DGITM | Published 2022 | https://www.ecologie.gouv.fr/sites/default/files/DGITM-Rapport_accidentalite-juillet_2022-EN.pdf EN version
ODD definition | Methodological framework document DGITM | Published 2022 | https://www.ecologie.gouv.fr/sites/default/files/DGITM-ODD_dezscriptors-juin_2022-EN.pdf EN version
Route characterisation | Methodological framework document DGITM | Q3 2022 | Will incorporate elements from the ODD document and the "route cutting" study report. To be integrated into the STRMTG GAME safety demonstration guide (see below)
Characterisation of remote intervention functions | Methodological framework document DGITM | Q3 2022 | To be integrated into the STRMTG GAME safety demonstration guide (see below)
Scenario generation | Methodological framework document DGITM-SystemX | Published 2022 | https://www.ecologie.gouv.fr/sites/default/files/DGITM-L1-septembre_2022-EN.pdf EN version
Scenario rating |  | Q3 2022 | To be included in the STRMTG GAME safety demonstration guide (see below)
Use of scenarios in the safety demonstration |  | Q4 2022 | 

## Slide 18: Safety standards for automated transport systems 3/3
Theme / title | Document | Deadline | Remarks
GAME safety demonstration Definitions from the glossary Safety demonstration method, including: Pathway decomposition Functional decomposition Hazards and high level requirements | Implementation Guide STRMTG | Published | https://www.ecologie.gouv.fr/sites/default/files/DGITM-GuideD%C3%A9monstration_GAME_STRA_v1_31aout2022-EN.pdf FR version only
Additions to be considered in the short term: Use of scenarios and safety analysis of routes | STRMTG | 2023 | 
RETEX - Handling of events | Implementation Guide STRMTG | 2023 | 
Cyber requirements | Implementation Guide STRMTG | Q4 2022 | NB: The STRMTG is aiming for a 'martyr' version of this guide by Q3 2022
Missions of the accredited qualified bodies | Implementation Guide STRMTG | Q3 2022 | 

## Slide 19
Traffic hazard
Ego manoeuvre
Static configuration
Annex 2: Scenario descriptors, layers and sub-layers (example)
Macro-layer
Descriptors
Hazard affecting response
Response
1
2
3
4
5
Geometric caracteristic (infra)
Static signage
Infrastructure lisibility
Attributs
Traffic regime
Priority regime
Lane marking
Traffic signs
Bitters and beacons
One way
Bidirectional
Separate lane
With variable channel allocation
…
Elevation change
Road surface
Longitudinal profile
Plan view
Lane width
Intersection type
Longitudinal variation of the longitudinal profile
Adjacent area of the lane
Number of lanes
Traffic light

## Slide 20
Traffic hazard
Ego manoeuvre
Static configuration
Scenario descriptors: layers and sub-layers (example)
Macro-layer
Descriptors
Hazard affecting response
Response
1
2
3
4
5
Rolling in current section
Intersections and crossings
Parking
Insertions and exits
Rolling / Tracking
Intersection crossing
Entry from insertion lane
Exit from exit lane
Level crossing
Turn left
Turn right
U-turn
Roundabout crossing
Overtaking
Lane change
Crossing
Insertion of a private road
Attributs

## Slide 21
Traffic hazard
Ego manoeuvre
Static configuration
Scenario descriptors: layers and sub-layers (example)
Macro-layer
Descriptors
Hazard affecting response
Response
1
2
3
4
5
Rolling in current section
Intersections and crossings
Parking
Insertions and exits
Attributs
Input / output TC channel
Public transport exit notch to public road
Stop on track
Post-stop departure on track
Notch along the lane
Online parking
Spurred parking
Entrance and stop notch for public transport
Manoeuvring public road parking / exit
Stop on lane
Loading / unloading for delivery
In double file
Reserved area
In pedestrian areas

## Slide 22
Traffic hazard
Ego manoeuvre
Static configuration
Scenario descriptors: layers and sub-layers (example)
Macro-layer
Descriptors
Hazard affecting response
Response
1
2
3
4
5
Type / Nature
Manoeuvre
Hazard area descriptors
Contextual element as a presumption of attitudes
Attributs
Type of third party
Guided transport
Specialised self-propelled vehicles
Extraordinary convoys
Vulnerable road users (pedestrians, cyclists)
Animal
Object
Road vehicle (car, motorized 2-wheelers, truck)
Distances
Vehicle category
International (M, N, O)
National (navurb)
With respect to the vehicle
Size
Location with respect to the ego
Number / density / weight
Third way or location in relation to the ego
(x, y, z)
In relation to the road
In relation to the carriageway

## Slide 23
Traffic hazard
Ego manoeuvre
Static configuration
Scenario descriptors: layers and sub-layers (example)
Macro-layer
Descriptors
Hazard affecting response
Response
1
2
3
4
5
Type / Nature
Manoeuvre
Hazard area descriptors
Contextual element as a presumption of attitudes
Attributs
Type of manoeuvring intention
Speed
Ancillary objects
Feet on carriageway
Open door
Person around vehicle
(motorised) personal transport device (MPTD) on pavement
Safety distances
Intersecting road features
Movement characteristics
Public institution
Hospital
School
Size
Location with respect to the ego
Angle
Characteristics of adjacent generator areas
Acceleration
Erratic movements
Passenger in vehicle
(M)PTD at an intersection