## Slide 1
Task Force 3: Electrolyte leakage
Last update- 12/05/2014

## Slide 2
Organization of Task force
Issues raised during last EVS meeting
Present requirement and purpose
Approach of Task Force
Issues related to Electrolytes
Proposal : Aqueous Electrolytes
Conclusion and future work
Content:

## Slide 3
Scope:
  Issues related to electrolyte leakage (except venting)
Objective :
  Reply all the queries on this issue , provide justification for the requirements in GTR draft and if required propose test procedure.
Organization of Task force: Scope & Objective

## Slide 4
China (CATARC) :
European union (JRC):
USA (NHTSA) :
South Korea ( KATRI):
France (UTAC):
OICA (Alliance, Daimler, JLR, PSA, GM, Toyota, Nissan, JAMA, VW, Scania, SK Continental , Volvo, Renault)
Organization of Task force: Members
Contributions
Research data /analysis: JRC
Comments: JRC, NHTSA, KATRI, CATARC , OICA

## Slide 5
End of January 2014: Initial comments on the issue by exchange of emails
28th February 2014: 1st meeting with co-sponsors on progress of task force
11th March 2014: 1st audio meeting of TF to discuss the initial proposals
21st March 2014: 1st face to face meeting in Paris
11th April 2014: 2nd audio meeting of TF to finalize the task force conclusion on aqueous electrolyte REESS
25th April 2014: 2nd meeting with co-sponsors on progress of task force
8th of May 2014: Comments on the ‘status report’ by exchange of emails
12th May 2014: 2nd face to face meeting in Washington (validation of conclusion)
13th May 2014: Presentation of task force progress report in the 5th GTR-EVS meeting
Organization of Task force: Work plan

## Slide 6
Electrolyte Leakage: Issues raised during last EVS meeting
Three category of questions
Leakage detection:
  How to distinguish leakage?
  What is an appropriate coating?
Leakage (spillage) amount measurement :
  How is leakage measured?
  How to quantify electrolyte leakage amount (7 % volume or 5 litters)?
  How to differentiate ‘electrolyte leakage’ from ‘coolant’?
  How to measure the electrolyte vapor (in case required to)?
  Electrolyte leakage currently defined as liquid leakage. This poses possible difficulty for batteries using volatile electrolytes (e.g. Li-ion). How is liquid electrolyte leakage measured and distinguished from electrolyte lost due to vapors or evaporation of spilled electrolyte?
Venting gas:
  How to differentiate smoke from combustion with electrolyte vapors at venting, for example in the thermal cycling test?

## Slide 7
Test items | Purpose of the test | Present Requirements
Vibration | -The user is supposed to continue to use the vehicle after the event. -In this case, stringent requirements should be applied | -No evidence of electrolyte leakage
Thermal shock and cycling |  | 
External short circuit protection | -The proposed test procedure is to confirm the operation of protective function. -In this case, stringent requirements should be applied | 
Overcharge protection |  | 
Over-discharge protection |  | 
Over-temperature protection |  | 
Mechanical integrity | -Same as vehicle post-crash | -No evidence of electrolyte leakage
Mechanical shock |  | 
REESS requirements for whole vehicle post-crash | -The user is supposed to stop using the vehicle until certain repair/maintenance is conducted once subject to the event, presuming the battery would not be re-used for any other purpose than vehicle propulsion. -In this case, the requirement relevant to the accident situation, in order to avoid additional risk to the occupants and the surrounding people, should be applied. | -Until 30 min after the impact, there shall be no electrolyte leakage from the REESS into the passenger compartment -no more than 7 % by volume of the REESS electrolyte capacity spilled from the REESS to the outside of the passenger compartment.
Electrolyte Leakage: Present requirement & Purpose
In-use
Post-crash

## Slide 8
  Complete list of risk associated with all type of electrolytes and situation in the GTR are analyzed
  TF members agreed to distinguish the REESS in to two categories based on the types of electrolytes
    Aqueous electrolyte
    Non-aqueous electrolyte
  TF member agreed to distinguish in-use and post-crash requirements
  The discussions will be in two steps:
    first complete the discussion on REESS based on aqueous electrolytes (by end March) => discussion completed
    and then discuss the particularities of REESS with non-aqueous electrolytes . => still under discussion, need further time
Approach :

## Slide 9
 | Issue | Potential Risk | Proposed Solution
1 | Leakage/spillage in liquid form | Irritant, Corrosive Large amounts, order of liters, expected | No evidence of electrolyte leakage/spillage Well understood and documented, e.g. FMVSS 305, UNECE R100.02, UNECE R94/95/12, IEEE 1578 Visual inspection as described in the current GTR text may be used for electrolyte leakage/spillage detection
2 | Vapor from leakage/spillage | No significant amount expected | No action needed (low volatility of water)
3 | Volatile gas | Expected in normal operation Flammable gas (e.g.H2) | Well understood and documented (e.g. UNECER100.02, EN62485-3, SAEJ1718) Venting (proposal from Japan)
4 | Leakage/spillage in liquid form | Irritant, Corrosive Large amounts, order of liters, expected | Until 30 min after the impact, there shall be no electrolyte leakage from the REESS into the passenger compartment No more than 7 % by volume of the REESS electrolyte capacity spilled from the REESS to the outside of the passenger compartment. Visual inspection may be used for electrolyte leakage/spillage detection
5 | Vapor from leakage/spillage | No significant amount expected | No action needed (low volatility of water)
Issues related to Electrolyte : Aqueous Electrolytes
In-use
Post-crash
TF3 experts agrees that proposed solution is adequate for issues related to Aqueous Electrolytes

## Slide 10
Add the following clarification on the leakage detection: [Based on FMVSS 305]
Good engineering judgment should be used to fulfil the requirement of an appropriate coating. One of the possible solutions might be an absorbent paper which surrounds the REESS casing. If in this case an electrolyte leakage occurs, the absorbent paper would get stains and wetted. The electrolyte leakage would be simple to recognize by visible inspection.
Add the following clarification on spillage/leakage measurement: [Based on FMVSS 305]
The spilled amount of electrolyte can be measured by usual techniques of determination of liquid volumes after collecting the spillage. For containers containing both Stoddard (colored coolant) and electrolyte, the fluids shall be allowed to separate by specific gravity then measured.
Proposal : Final text will be proposed in the next GTR-EVS meeting
Final text will be proposed in the next GTR-EVS meeting

## Slide 11
 | Issue | Potential Risk | Proposed Solution
1 | Leakage/spillage in liquid form | Flammable, Toxic, Corrosive Small amounts, order of millilitres, expected | Under discussion
2 | Vapor from leakage/spillage | Toxic / flammable gas | Under discussion
3 | Volatile gas | Not expected in normal operation | Under discussion
4 | Leakage/spillage in liquid form | Flammable, Toxic, Corrosive Small amounts, order of millilitres, expected | Under discussion
5 | Vapor from leakage/spillage | Toxic / flammable gas | Under discussion
Issues related to Electrolyte : Non-Aqueous Electrolytes
In-use
Post-crash
Still under discussion

## Slide 12
  Aqueous electrolyte
  Non-aqueous electrolyte
  Leakage
  Spillage
  …
Definitions :
These definitions are still under discussion

## Slide 13
Conclusion and future work
Completed :
  List of issues related to electrolytes and associated potential risks
  Discussions on aqueous electrolyte : Leakage detection and measurement techniques are clarified
Future work :
  Discussions on risk associated with non-aqueous electrolytes
  Propose final text for agreed topics
  Required time: Till next GTR-EVS meeting (October)

## Slide 14
Annex