Draft of a new 07 series of amendments to UN Regulation No. 10

IWG-EMC-31-02e (Sec) Updated draft of ECE R10 07.docx

extends frequency range, but some Annexes are not changed.

- paragraph 6.4 which includes freq. range extension refers to:

Annex 6

4.	Test requirements

4.1.	Frequency range, dwell times, polarization.

The vehicle shall be exposed to electromagnetic radiation in the 20 to 2,000 MHz frequency ranges in vertical polarization.

The test signal modulation shall be:

(a)	AM (amplitude modulation), with 1 kHz modulation and 80 per cent modulation depth in the 20 to 800 MHz frequency range; and

(b)	PM (pulse modulation), Ton 577 µs, period 4,600 µs in the 800 to 2,000 MHz frequency range.

If not otherwise agreed between Technical Service and vehicle manufacturer.

Frequency step size and dwell time shall be chosen according to
ISO 11451-1.

4.1.1.	The Technical Service shall perform the test at the intervals specified in ISO 11451-1 throughout the frequency range 20 to 2,000 MHz.

- paragraph 6.8 which includes freq. range extension refers to:

Annex 9

3.	General test requirements

3.1.	Frequency range, dwell times

Measurements shall be made in the 20 to 2,000 MHz frequency range with frequency steps according to ISO 11452-1.

The test signal modulation shall be:

(a)	AM (amplitude modulation), with 1 kHz modulation and 80 per cent modulation depth in the 20 to 800 MHz frequency range; and

(b)	PM (pulse modulation), Ton 577 µs, period 4,600 µs in the 800 to 2,000 MHz frequency range.

If not otherwise agreed between Technical Service and ESA manufacturer.

Frequency step size and dwell time shall be chosen according to
ISO 11452-1.

3.2.	The Technical Service shall perform the test at the intervals specified in 
ISO 11452-1, throughout the frequency range 20 to 2,000 MHz.