## Slide 1
Contracting Party
Reporter
Concept
Status
Timeline
(Adoption of CP options, Partial Adoption, Deviations from GTR, etc.)
Remarks
(Planned changes of national regulatory instruments to accommodate GTR20.)
Revision of KMVSS in harmony with GTR20 (Phase 1)
Moon, Bohyun (KATRI)
The safety of REESS of KMVSS was harmonized with GTR20
Korea
Revised KMVSS(GTR20 + WI) mandatory for New Types
The safety of REESS in KMVSS is harmonized with GTR 20 phase 1.
The water immersion test remains in revised KMVSS.
The revised KMVSS became mandatory from July 1, 2021, and vehicles that have already been certified will be exempted from the revised KMVSS until June 30, 2023.
The new KMVSS regulation for electric motorcycles, which adds the water immersion test and the GTR20’s test condition to UN R136, became mandatory from DEC 25, 2022.
Currently, the manufacturer can choose the 4.9m drop test instead of a mechanical impact test.
The KMVSS is considering revising the mechanical impact test as a mandatory test, and requiring an additional drop test for vehicles whose batteries are exposed in the lower part of the vehicle.
KMVSS does not have any TP regulations. It will be revised once the test procedure is agreed.
Revised KMVSS(GTR20 + WI) mandatory for New Registrations
New KMVSS for Electric motorcycle mandatory for All models
Transposition of GTR20 (Phase 1) to National Regulation - Progress Report - 26th EVS-GTR IWG (Apr. 2023)