## Slide 1: Proposal of EC JRC for R10
Testing all intended normal operation modes of a vehicle

## Slide 2: Amendment background and rational
As JRC research showed 2 out of 5 tested vehicles may have issues in other intended (not transient) normal conditions of use. The basic problem is that some propulsion engine operation modes are not tested because of the possible interpretation inconsistency between 6.1.2 and 7.1.2 of R10 and CISPR 12.
This proposal is not so much about amending the existing requirements rather than clarifying them in the context of the technological developments.
Later we can define testing procedures if we have time, i.e. ANNEX 4-5 and 7.

## Slide 3: Proposed supplement to 6.2.1
Before testing, the Technical Service has to prepare a test plan in conjunction with the manufacturer, which contains at least mode of operation, stimulated function(s), monitored function(s), pass/fail criterion(criteria) and intended emissions. The test plan shall take into account all normal intended operating conditions of the propulsion, charging and auxiliary systems including but not restricted to multiple (if more than one) engine operation strategies, recuperation modes and different configurations (selectable by the driver or by the control system). Manufacturer shall assess the intended electromagnetic disturbance generated by all elements in the test plan by means of calculations, test reports etc.
The test plan and the assessment of the intended electromagnetic disturbances shall be attached to the type approval documentation in Annex II a and b, and shall cover:
- Number and types of propulsion and auxiliary engines
- Different modes of operations (selectable by the driver or the system) and their characteristics (e.g. power, current, charging, discharging etc.)
- Schema (e.g. flow chart or table) of the engines operation control strategy and their dependence on the driving or other selectable conditions (charge of the battery, speed, power, etc.)
- Characteristic frequency ranges of the disturbances in all normal intended modes of operation
- Intended emission (measured or estimated/simulated by the manufacturer)

## Slide 4: Proposed supplement to 7.1.2
Before testing the Technical Service has to prepare a test plan in conjunction with the manufacturer, for the configuration "REESS charging mode coupled to the power grid" configuration which contains at least mode of operation, stimulated function(s), monitored function(s), pass/fail criterion (criteria) and intended emissions. The test plan shall take into account all normal intended operating conditions of the "REESS charging mode coupled to the power grid", charging and auxiliary systems including but not restricted to heating and cooling sub-systems different configurations (selectable by the driver or by the control system). Manufacturer shall assess the intended electromagnetic disturbance generated by all elements in the test plan by means of calculations, test reports, measurements etc.
The test plan and the assessment of the intended electromagnetic disturbances shall be attached to the type approval documentation in Annex II a and b, and shall cover:
- Number and types of charging and auxiliary subsystems
- Different modes of operations (selectable by the driver or the system) and their characteristics (e.g. power, current, charging power, heating cooling power etc.)
- Schema (e.g. flow chart or table) of the control strategy and their dependencies on the charging or other selectable conditions (state of charge of the battery, ambient and battery temperature, power, etc.)
- Characteristic frequency ranges of the disturbances in all normal intended modes of operation during charging
- Intended emission (measured or estimated/simulated by the manufacturer)

## Slide 5: Annex 2a
74. Number and types of propulsion and auxiliary engines related to charging and driving modes
75. Different modes of operations of the propulsion and charging subsystems (selectable by the driver or the system) and their characteristics (e.g. power, current, charging, discharging etc.)
76. Schema (e.g. flow chart or table) of the engines operation control strategy and their dependence on the driving or other selectable conditions (charge of the battery, speed, power, etc.)

## Slide 6: Keep in touch
EU Spotify
ec.europa.eu/
europa.eu/
@EU_Commission
@EuropeanCommission
European Commission
europeancommission
@EuropeanCommission
EUTube
Notes: Delete/update as appropriate

## Slide 7: Thank you
© European Union 2020
Unless otherwise noted the reuse of this presentation is authorised under the CC BY 4.0 license. For any use or reproduction of elements that are not owned by the EU, permission may need to be sought directly from the respective right holders.
Slide xx: element concerned, source: e.g. Fotolia.com; Slide xx: element concerned, source: e.g. iStock.com
Notes: Update/add/delete parts of the copy right notice where appropriate.
More information: https://myintracomm.ec.europa.eu/corp/intellectual-property/Documents/2019_Reuse-guidelines%28CC-BY%29.pdf