## Slide 1: Industry input for ACPE-02 meeting Issue of overlapping between ACPE and low speed emergency systems
May 15-16-17, 2023

## Slide 2
Overriding of AEBS operation
Extract from R131-02 (same principles in R152)
Introduction
During any action taken by the system (the warning and emergency braking phases), the driver can, at any time through a conscious action like an accelerator kick-down or a swerving action that results in enough change of direction not to hit the target, take control and override the system.
5.3. Interruption by the Driver
5.3.1. The AEBS shall provide appropriate and robust means for the driver to interrupt the collision warning and the emergency braking.
5.3.2. In both cases above, this interruption may be initiated by any positive action (e.g. kick-down or a swerving action that results in enough change of direction to not hit the target) that indicates that the driver is aware of the emergency situation. The vehicle manufacturer shall provide a list of these positive actions to the technical service at the time of type approval, and it shall be annexed to the test report.
Kick-down is given as an example of how to override AEBS intervention.
Kick-down is indeed often used on vehicles, for more than 10 years.
Drivers are used to this logic, thus changing this logic may have a negative effect for driver.

## Slide 3
stationary
Accelerator pedal
Kick-down
Case 1
ACPE – AEBS overlapping
No ACPE intervention
 OK
AEBS intervenes
(by braking and cutting acceleration)

## Slide 4
Accelerator pedal
Kick-down
AEBS intervenes
(by braking and cutting acceleration)
AEBS enables acceleration and stops braking
“potential pedal error is detected”  ACPE inhibits acceleration (and may brake)
ACPE – AEBS overlapping
 NOK
Case 2
stationary
What shall the vehicle do:
Obey ACPE regulation ?
Or
Obey AEBS regulation ?
Conclusion: velocity could be a perfect parameter to separate regulatory scope and avoid contradictions

## Slide 5
ACPE – ABLS overlapping
ABLS = Automatic Braking Low Speed maneuvering (parking in/out…)
  ISO 4273 is not yet published (Draft DIS)
  The group should analyze the potential contradiction between ISO 4273 and ACPE
New ISO work item on ACPE
  ISO 19486 = ACPE standard on pedal mix up, to mitigate collision with obstacles, covering performance and test procedure
  The work on test procedure will start with standstill.
Conclusion
  ISO work is just being initiated on ACPE, the recommendation is to focus on standstill operation in the IWG.

## Slide 6
Conclusion
Overlapping of requirements between ACPE and ‘low speed emergency systems’ must me avoided.
(There must be a gap between ACPE and e.g. AEBS requirements).
Standstill vehicle-to-vehicle operation is the only feature considered today in J-NCAP, where industry have sufficient experience.
The recommendation is to limit ACPE to standstill vehicle-to-vehicle operation.