## Slide 1: TP-TF report for 27th IWG meeting
2023.6
EVS-GTR

## Slide 2: Outline
01 Recent work & meeting
02 Discussion in TP-TF
03 Next-step work

## Slide 3: 01 Recent work & meeting
Apr, 2023——26th IWG meeting
  TP-TF report
  Remaining issues
    IWG meeting-test/documentation approach harmonization
    TP-TF-Technical topics
    Test family
    Round robin test
Jun 8, 2023 ——TP-TF meeting
  Discussion on technical topics determined in the 26th IWG meeting

## Slide 4: 02 Discussion in TP-TF A. Initiation method
Background
In the current regulation draft, localized rapid external heating from ISO 6469-1 AMD1:2022 is the only mentioned initiation method
Alternative initiation method
  Technology neutrality and feasibility
  Equivalency of main and alternative methods: Whether TR initiated successfully?

## Slide 5: 02 Discussion in TP-TF A. Initiation method
Discussion Summary
China suggest that Localized rapid external heating could be regard as main method, but alternative initiation methods are also necessary, such as nail penetration and internal heating in the ISO 6469-1 AMD:2022. Different kinds of initiation methods are suitable for different cell and Every initiation method has limitations.
Japan showed a presentation emphasizing that nail penetration initiation method should be kept from a technology neutral perspective. Nail method could initiate single cell TR successfully and is feasible for vehicle test. Sidewall rupture is observed in nail and heater initiation.
Canada noted that a proposal text on nail penetration initiation method is important for each CP to evaluate it.

## Slide 6: 02 Discussion in TP-TF A. Initiation method
Discussion Summary
OICA emphasized that alternative method would be beneficial and equivalency has widely influence factors.
EU expressed technical concern about nail penetration method, such as insufficient information on how it compares to other initiation methods, extensive modification not intended by design and Geometric dependence combined with high precision required for nail positioning. As a result, they proposed to focus on localized rapid external heating in Phase 2
Korea noted that the main initiation method is localized rapid external heating, and other initiation methods in ISO can only be used as alternative methods when the main initiation method fails. Methods not found in ISO are proposed for discussion in Phase 3.
*EU and Korea provide their feedback after the meeting

## Slide 7: 02 Discussion in TP-TF B. Criteria of thermal runaway
Background
In the regulation draft from EU/JRC, the criteria of thermal runaway is as follows and OICA also provided a proposal based on ISO 6469-1 AMD: 2022
Main criteria
Thermal runaway can be detected by the following conditions:
(i) The measured voltage of the initiation cell drops, and the drop value exceeds 25% of the initial voltage;
(ii) The measured temperature of the initiation cell exceeds the maximum operating temperature defined by the manufacturer;
(iii) dT/dt ≥ 1 °C/s of the measured temperature of the initiation cell for at least 3s.
Supplementary criteria
The following indicators can be considered as supportive evidence of occurrence for thermal runaway:
— dP/dt ≥ 0.01 bar/s of the measured pressure in the pack for at least 3s;
— smoke release;
— occurrence of ejected solid material;
— failure of the BMS or signal faults (if the BMS is still active). Logged faults in the BMS shall be analysed. Thermal runaway indicators shall be specified and documented if required.
The following indicators are post-analysis criteria as evidence of whether a thermal runaway has occurred in the initiation cell and whether this has resulted in thermal propagation in the REESS or REESS subsystem:
— mass loss greater than its electrolyte mass of the initiation cell;
— REESS or cell rupture;
— REESS deformation;
— material formation indicating high temperatures (e.g. molten and re-solidified aluminium or copper);
— specific reaction products such as e.g. metallic nickel or cobalt, lithium-aluminium oxide;
— current collector foil absence (partial or total);
— thermal decomposition of polymer materials, e.g. separator, isolation material.
Thermal runaway can be judged when:
(a) Both (i) and (iii) are detected;
(b) Both (ii) and (iii) are detected; or
(c) At least two supplementary criteria and (iii) are detected.

## Slide 8: 02 Discussion in TP-TF B. Criteria of thermal runaway
Preliminary conclusion
Post-analysis, which provide further evidence and help ascertain the occurrence of TR, could be moved to Rationale part.
Discussion Summary
China suggest to continue discussing it based on JRC’s proposal, which is referred to several regulation and standards and has been discussed for several meeting. For the new parameter proposed, it could be added into criteria after agreement in IWG.
OICA emphasized that the printed version of ISO 6469-1 AMD:2022 should be a reference, in which TR detection criteria is divided into 2 parts according to energy density of cell.

## Slide 9: 02 Discussion in TP-TF C. Test level
Background
In the current regulation draft, only vehicle level test is proposed
Component level is necessary:
  Low cost and easy to implement
  Vehicle level TP test is challenging for heavy-duty vehicle
Component level isn’t necessary:
  Equivalency between component and vehicle level should be confirmed

## Slide 10: 02 Discussion in TP-TF C. Test level
Preliminary conclusion
Continue to discuss based on China’s proposal? (need confirmation in IWG, especially for some points beyond technical issues, such as CP option)
China’s proposal
Considering test efficiency, cost and enforceability,
For all vehicles of Category 1-1 and vehicles of Categories 1-2 and 2 with GVM of 4,536 kg or less: Vehicle level, REESS level could be alternative choice depending on CP option.
For vehicles of Category 1-2 and Category 2 with GVM exceeding 3,500 kg: Vehicle level or REESS level, Manufacturers choose the test level to be conducted.

## Slide 11: 02 Discussion in TP-TF C. Test level
Discussion Summary
Japan shared a presentation to clarify that difference of severity between vehicle level test and pack level test is not observed and occupant safety are explained by documentation and/or supplemental component level test. As a result, Japan noted that component level test should be kept in GTR.
Canada generally agree with China’s proposal but they noted that further discussion is necessary on pass/fail criteria and hazardous condition in component level.
OICA emphasized that the situation of HDV is different with passenger vehicle so that HDV and passenger vehicle should be discussed separately.
EU/JRC acknowledged that different safety risks may need to be considered for heavy-duty vehicles. JRC also acknowledge testing limitations associated with vehicle-level tests for heavy-duty vehicles. JRC recognize the need for further discussion on these aspects.
Korea noted that an agreement is needed on how to avoid regulations regarding the intrusion of toxic gases into the vehicle compartment.
*EU and Korea provide their feedback after the meeting

## Slide 12: 02 Discussion in TP-TF D. Target cell selection
Preliminary conclusion
Background
Canada provide a proposal on target cell selection, including the installation shall minimize modifications to thermal insulators and structure and cell shall be selected represents the worst case conditions for thermal propagation.
Continue discussing with the basis of Canada proposal.

## Slide 13: 02 Discussion in TP-TF D. Target cell selection
Background
China generally agree the cell selection principle in Canada’s proposal and further comments will be provided later.
OICA suggest to consider “severe” condition rather than “worst” case.
US questioned whether different test agencies select cell independently, Canada answered that different test labs would choose the same target cell in principle, but further research is needed.
JP considered that disabled cooling system represent worse scenario and should be allowed.
EU/JRC will provide feedback on Canada’s proposal for the selection of the initiation cell at the next IWG meeting after reviewing the proposal.
Korea agree with CA proposal but they noted that additional sentences below are required.
Note. If the heating element is inserted between two cells, then thermal runaway may be initiated in two cells simultaneously unless sufficient thermal insulation or barriers are added that does not impede natural RESS functionality.
Discussion Summary
*EU and Korea provide their feedback after the meeting

## Slide 14: 02 Discussion in TP-TF E. Hazardous situation clarification
Preliminary conclusion
Background
Hazardous situation should be clarified.
According to the previous discussion, external fire, explosion and smoke in the cabin are regard as temporary hazardous situation in the test approach
Discussion on OICA’s proposal in IWG meeting

## Slide 15: 02 Discussion in TP-TF E. Hazardous situation clarification
Discussion summary
OICA noted that the definition of hazardous situation is essential(reflected in their proposal in IWG meeting).
Canada agree with the importance of the definition of hazardous situation and suggest to discuss it as a independent item in the upcoming IWG meeting.
EU/JRC noted that they do not see the need to make the regulation more lenient. At the moment setting up quantitative requirements for exposure is not feasible for various reasons, including the lack of sufficiently selective and robust verification methods.
China suggest to maintain the temporary hazardous situation criteria until new consensus achieved in the IWG.
Korea noted that Verification of Hazardous condition can only rely on visual inspection and gas detectors. In the case of vehicle-level testing, it can be challenging due to the larger test space compared to battery testing. Additionally, confirming whether explosions or other incidents occurred after testing becomes difficult if a fire spreads throughout the entire vehicle. To ensure accurate verification of criteria, it is believed that a DTC (Diagnostic Trouble Code) for TR or TP warning signals would be necessary.
*EU and Korea provide their feedback after the meeting

## Slide 16: 02 Discussion in TP-TF F. Clarification Warning indication to allow egress or 5 minutes”
Preliminary conclusion
OICA proposal in last IWG meeting
List all possible scenarios and discuss the corresponding judgment

## Slide 17: 02 Discussion in TP-TF F. Clarification Warning indication to allow egress or 5 minutes”
Discussion summary
OICA suggested to divided the column of hazardous situation into “fire, explosion” and “smoke”, because they require different consideration.
Item | Situations |  |  |  |  |  |  |  | 
 | TR of cell | TP of system | Hazardous situation occurs | Warning signal needed |  |  |  |  | 
 |  |  |  | China | Japan | EU | German | Korea | Canada
1 | No | No | No | No | No | No | No | No | No
2 | Yes | No | No | Yes | No | No | Yes | Yes | Maybe No
3 |  |  | Yes | Yes | Yes | Yes | Yes | Yes | Yes
4 |  | Yes | No | Yes | field data needed | Yes | Yes | Yes | Yes
5 |  |  | Yes | Yes | Yes | Yes | Yes | Yes | Yes
The warning signal based on （TR？TP？Hazardous situation occurs？） |  |  |  |  |  |  |  |  | 

## Slide 18: 03 Next-step work
Next TP-TF meeting will be held between 27th and 28th IWG meeting (meeting date is still need to be discussed between TF-leaders).

## Slide 19: Thanks