## Slide 1: OICA proposal on family concept for thermal propagation certification EVS #27 meeting 2023
UNECE EVS-IWG

## Slide 2
Add this new paragraph in part C Technical background 3 Thermal propagation
XX. To support this verification process, whilst minimising the burden of increased testing for manufacturers, two family concepts were developed within the GTR for thermal propagation testing: a REESS family and a vehicle family. This is likely to reduce the need for additional testing where multiple REESS and vehicles may have the same characteristics with respect to verification of the thermal propagation protection. In addition, the thermal propagation verification for the REESS/vehicles in the same REESS/vehicle family may be combined between different regions with the agreement of all Contracting Parties involved. This contributes not only to minimise the testing burden but also to increase the verification robustness.
family concept for thermal propagation certification

## Slide 3
family concept for thermal propagation certification
Add this new paragraph before Documentation approach and Thermal propagation test
Definitions of Families
  Vehicles/REESS having the same characteristics with respect to their evaluation on the criteria below may be grouped into vehicle/REESS families for the purpose of compliance verification of the thermal propagation protection.
  Families with the same characteristics with respect to compliance verification shall be defined as follows:
REESS family criteria for thermal propagation certification
  REESSs that are substantially similar with respect to the following elements may consist of the same REESS family:
  (a) The chemistry, capacity and physical dimensions of its cells;
  (b) REESS design influencing the thermal propagation protection;
  (c) Battery Management System (BMS) (with regards to thermal propagation protection);
  (d) Operation strategy of all components influencing the thermal propagation protection;
    (e) Venting strategy
  At the request of the manufacturer, with appropriate technical justification, and, with the approval of the technical service, if applicable, the manufacturer may deviate from the above criteria for families.
This concept apply to both documentation and testing

## Slide 4
Add this new paragraph before Documentation approach and Thermal propagation test
Vehicle family criteria for Light Duty vehicle thermal propagation certification
Light Duty Vehicles that are substantially similar with respect to the following elements may consist of the same LDV family:
  (a) Underbody layout;
  (b) REESS venting strategy;
  (c) REESS clearance with vehicle body and floor;
  (d) REESS family
  At the request of the manufacturer, with appropriate technical justification, and, with the approval of the technical service, if applicable, the manufacturer may deviate from the above criteria for families.
family concept for thermal propagation certification