## Slide 1: OICA Presentation on IWG-EMC-36-03 background changes
May 2023
IWG-EMC-36-04

## Slide 2: Context: OICA proposal for R10.07
OICA has issued a proposal for R10.07 concerning the following topics:
Addition of flowchart for charging mode to be tested in each concerned annex
Suppression of Annex 14 and 20 (and all associated wording)
Wording and all set-up for vehicle in charging mode updated for consistency on Z-folding with last agreed decisions in CISPR and ISO (concerns Annex 4 and Annex 6)
Precision on preferred configuration when using reverberation chamber method for ESA immunity test in Annex 9
Addition of a definition of “Auxiliary equipment (AE)” and use auxiliary equipment for consistency in all the document (instead of associated equipment
Addition of AAN in 7.1.4.
Confirmation of 10 V/m as test level for immunity between 2 and 6 GHz.
Editorial updates in Appendix 8
This document includes background information on these proposed changes

## Slide 3: Addition of flowchart for charging mode to be tested in each concerned annex
Background
For each concerned annex the existing wording of previous draft R10.07 has been replaced by a dedicated flow-chart to precise which charging modes have to be tested depending on available charging modes in the vehicle
The proposal is based document “IWG-EMC-34-02-Rev.1 (OICA) REESS_Flowcharts Annexes” already discussed in IWG
Concerned part in the OICA draft proposal
  Annex 4 clause 2.2.
  Annex 6 clause 2.2.1.1.
  Annex 11 clause 2.1.
  Annex 12 clause 2.1.
  Annex 13 clause 2.1.
  Annex 15 clause 2.
  Annex 16 clause 2.

## Slide 4: Suppression of Annex 14 and 20 (and all associated wording)
Background
During the presentation of “IWG-EMC-34-02-Rev.1 (OICA) REESS_Flowcharts Annexes” in previous IWG meeting most of the participants (CPs, OICA, ..) agreed that Annex 14 test could be suppressed (no test performed up to now by any technical service) and consequently annex 20 (ESA)
Concerned part in the OICA draft proposal
  Clauses 7.6.
  Clauses 7.20.1. to 7.20.3. (exemptions concerning only annex 14)
  All Annex 14
  Clauses 7.14.
  All Annex 20

## Slide 5: Wording and all set-up for vehicle in charging mode updated for consistency on Z-folding with last agreed decisions in CISPR and ISO (concerns Annex 4 and Annex 6)
Background
In recent discussions for revision of CISPR 12 (in CISPR/D/WG1) and for publication of ISO 11451-5 and revision of ISO 11451-2 (in ISO/TC22/SC32/WG3) it was agreed to improve the vehicle test set-up concerning the charging cable Z-folding part (for consideration of large section cables):
  Allow a larger dimension for the projected width (up to 1 m instead of up to 0,5 m)
  Not allow overlaps or contact between windings
The proposal is that for consistency these last agreed changes at international standardization level shall be considered for R10.07
Concerned part in the OICA draft proposal
  Annex 4 clause 2.3.3.
  Annex 4 vehicle in charging mode figures
  Annex 6 clause 2.3.3.
  Annex 6 vehicle in charging mode figures

## Slide 6: Precision on preferred configuration when using reverberation chamber method for ESA immunity test in Annex 9
Background
In ISO 11452-11 published standard for component test in reverberating chamber, test set-up to be used can be with or without ground plane
The proposal is to fix in R10.07 which set-up to be used (the one with ground plane) to ensure better repeatability.
Concerned part in the OICA draft proposal
  Annex 9 clause 4.5.2.

## Slide 7: Addition of a definition of “Auxiliary equipment (AE)” and use auxiliary equipment for consistency in all the document (instead of associated equipment)
Background
It have been noticed by OICA EMC TF members that in different part of R10.06 different wording (“associated equipment”, “auxiliary equipment”, “ancillary equipment”) were used to describe the same device.
The proposal is to:
  use in each concerned part a consistent wording “Auxiliary equipment (AE)”
  add a definition “Auxiliary equipment (AE)”
Concerned part in the OICA draft proposal
  New definition 2.32.
  Appendix 8 clause 5.1.
  Appendix 4 clause 2.4.3.
  Appendix 6 clause 2.4.3.

## Slide 8: Addition of AAN in Paragraph 7.1.4.
Background
It have been noticed by OICA EMC TF that some wording concerning AAN were not in line with last agreed wording in CISPR 12 and CISPR 25 (in CISPR/D/WG1) and in revision of ISO 11451-1 and ISO 11452-1 (in ISO/TC22/SC32/WG3).
The proposal is that for consistency these last agreed changes concerning AAN at international standardization level shall be considered for R10.07
Concerned part in the OICA draft proposal
  Clause 7.1.4.
  Appendix 8 clause 5.

## Slide 9: Confirmation of 10 V/m as test level for immunity between 2 and 6 GHz
Background
Extension of vehicle immunity testing and ESA immunity testing up to 6 GHz has been agreed in IWG. The test level between 2 GHz and 6 GHz is still under discussion
The proposal is that in consistency with IEC 61000-6-1 and 61000-6-2 in which test levels between 2 and 6 GHz are around a third of test levels below 2 GHz. For consistency in terms of ratio OICA proposal for R10.07 is to use a test of 10 V/m above 2 GHz
Concerned part in the OICA draft proposal
  Clause 6.4.2.1.
  Clause 6.8.2.1.
  Clause 7.7.2.1.
  Clause 7.18.2.1.

## Slide 10: Editorial updates in Appendix 8
Background
R10.06 in appendix 8 is not fully consistent (editorial changes) with last agreed wording in CISPR 12 and CISPR 25 (in CISPR/D/WG1) and in revision of ISO 11451-1 and ISO 11452-1 (in ISO/TC22/SC32/WG3).
The proposal is that for consistency these last agreed changes at international standardization level shall be considered for R10.07 Appendix 8
Concerned part in the OICA draft proposal
  Clause 6.4.2.1.
  Clause 6.8.2.1.
  Clause 7.7.2.1.
  Clause 7.18.2.1.