## Slide 1: Draft UN Regulation addressing DCAS – Outline
Submitted by the TF Leadership
ADAS 21-04

## Slide 2
means hardware and software collectively capable of assisting a driver in controlling the longitudinal and lateral motion of the vehicle on a sustained basis containing at least one feature, which is specified under section 6 in this Regulation and which requires the driver to be engaged and to monitor the environment, and vehicle/system performance, permanently.
DCAS
DCAS System
Basis lateral & longitudinal control
Feature 2
(e.g. system-initiated LC)
Feature 3
(e.g. Adv Driver-Initiated LC)
Etc.
Emergency Safety (e.g. RMF)
Failure Detection & Response
Driver Monitoring Strategy
Active
Stand-by
Off
Driver Information Materials
DCAS Operation Monitoring
Controllability
E.g. Camera
Steering
DCAS approved as a L2 system comprised of features
Speed Limit Compliance Assistance
Safe Headway Assistance
System Boundaries

## Slide 3
DCAS General & Specific Features
General Requirements
Lane Keeping
Longitudinal control
System Boundaries
Lane Changes
Driver Unavailability Response
Specific Feature Requirements
System-initiated maneuvers
Lane Changes
[Hands-off]
Other System-Initiated Manoeuvres
Other advanced driver-initiated manoeuvres
Advanced driver-initiated lane change
Advanced driver initiated manoeuvres
Controllability
Failure Detection & Response
Operation Modes & HMI
Driver Monitoring

## Slide 4
Substantive changes reflecting TF guidance &
previous comments
Mandatory equipment of emergency systems and RMF capability
Detailed failure detection and notification requirements
Extension of mode of operation & HMI (messages and signals) requirements to address confusion and/or overreliance
  Mandatory warning of upcoming system-initiated manoeuvres
  Notice to check indirect vision devices
Speed limit compliance and headway distance obligations
Overhaul of driver monitoring underway (specific visual attentiveness & physical attentiveness requirements)
Extensive driver information materials obligations & declaration of driver information strategy (Annex 3)
Mandatory controllability
Other ADAS systems cannot be active during DCAS operation. Emergency safety systems can activate
Extension of requirements for system-initiated manoeuvres coupled with extensive declaration obligations

## Slide 5
Section 5 – 5.1 General Requirements
Driver must remain engaged
Manufacturer shall implement strategies to ensure mode awareness and avoid driver overreliance
Manufacturer shall take effective measures to guard against reasonably foreseeable misuse by the driver
Driver must be able to override or deactivate at any time
Must be equipped with emergency safety systems (UN Regulation Nos. 131, 152, 179 and 130)
Section 5 – 5.2 DCAS interaction with other vehicle assistance systems
DCAS operation shall not suppress or deactivate other emergency assistance systems
Transitions between DCAS and other assistance or automation systems, prioritization, suppression and deactivation to ensure nominal and safe operation shall be described to the AA.

## Slide 6
Section 5 – 5.3 Functional Requirements
Detailed manufacturer description of detection capabilities and system boundaries of system and features, as well as other equipped systems
Assess and respond to surroundings as required to implement intended functionality
Adapt behaviour to surrounding traffic conditions by avoiding disruption of the flow of traffic
Use longitudinal and lateral motion to maintain appropriate distances from other road users
Other relevant vehicle systems may be activated (e.g. wipers, heating, indicators)
Control strategy shall aim to reduce risk of collision and ensure controllability (per 5.3.6)
Section 5 – 5.3.5 Response to system boundaries
Detected boundaries when switched on
Detailed description of system boundary conditions for each system and feature (considering Annex 3 Appendix 3)
Describe behaviour and impact on system performance when beyond boundaries
Declare means of identification of system boundaries
Notify driver when system boundary is exceeded and terminate assistance in predictable and controlled way. Strategy described.
Warning when approaching of a system boundary

## Slide 7
Section 5 – 5.3.6 Controllability
System shall aim to ensure that control actions by the system including, but not limited to those resulting from failures and/or reaching system boundaries remain controllable. This must take into account the driver’s potential reaction time.
System shall implement strategies relevant to the system’s intended operational design, within defined system boundaries to be assessed by the AA, e.g.
  Limiting system steering output
  Adjusting position in the lane of travel
  Road type and attribute determination (etc)
Section 5 – 5.3.7.1 Lane keeping
Shall keep a stable position in its lane of travel within its boundary conditions. Lateral acceleration values to be specified by the manufacturer.
Only permitted higher lateral acceleration than 3.0 m/s² provided
  the system provides visual information to the driver on the upcoming driving situation/manoeuvre which may induce higher values
  System adapts vehicle speed to upcoming changes in road curvature
  System ensures driver is engaged confirming visual attention
Leaving the lane to form an access corridor for emergency and enforcement vehicles allowed
  If system only leaves its current lane of travel when this is required and allowed according to national traffic rules
  System to ensure sufficient lateral and longitudinal distance to road boundaries, vehicles and other road users
  Return completely to original lane of travel once situation requiring intervention transpired

## Slide 8
Section 5 – 5.3.7.2 Lane Change
Sufficient notice to be provided to the driver. Compliance with requirements in 6.1.1 and 6.2.2 mandated.
Lane change requirements largely aligned with recent approaches in R79
Section 5 – 5.3.7.3 Driver Unavailability Response Lane keeping
When driver is determined to be unavailable following an engagement warning cascade, slow down and aim to remain in the lane of travel. Avoid deceleration of greater than 4.0 m/s² until coming to a stop. Hazard lights activated
Manufacturer to implement strategies to draw external attention to the emergency situation (e.g. emergency call, horn use)
Higher deceleration values are permitted for very short durations, e.g. as haptic warning
If equipped with a lane change system, aim to perform lane changes towards a slower or emergency lane if capable of doing so, accounting for surrounding traffic and road infrastructure.
Alternatively, compliance with RMF or additional response strategies can be evidenced.

## Slide 9
Section 5 – 5.3.8.1 Deceleration and Acceleration
System acceleration or deceleration shall remain controllable for surrounding traffic, unless increased levels of deceleration are required to ensure safety of the vehicle and/or surrounding road users. To be declared.
Section 5 – 5.3.8.2 Speed Limit Compliance Assistance
Aim to detect the applicable speed limit in current lane of travel
Continuously display system-determined speed limit
Aim to follow the system-determined speed limit or driver-speed limit, whichever is lower
Control not to exceed the speed limit, provide a means to override
Any assisted deceleration should be controllable
When the driver overrides and exceeds a system-determined speed limit, provide optical and acoustic/haptic warning
When override ends, system resumes control based on last system-determined speed limit or driver-set speed.
Alternatively, evidence compliance with national regulations for speed limit control systems. To be declared.

## Slide 10
Section 5 – 5.3.8.3 Safe Headway Assistance
System aims to make driver comply regulatorily defined headway according to national traffic rules
For M1 & N1, requirement fulfilled if either:
  A visual warning is provided upon first activation during a run cycle that the headway configuration is set to <[2]s
  Visual warning is provided when system detects that the headway to the road user ahead is too short/shorter than necessary for safe operation
Section 5 – 5.4 System safety response to detected failures
Detection of electrical and non-electrical failure conditions affecting safe operation
If a failure affects safe operation of a system/feature, control assistance of given system/feature to be terminated in safe manner according to safety concept
Manufacturer to take measures to ensure failures must remain controllable for the driver
System to switch “off” if failure affects the entire system upon termination of assistance, coupled with optical and audible failure warning signal. Gradually reduce control assistance if capable of doing so and inform the driver.
If failure affects specific features, system operation is permitted to continue if remaining features are unaffected
Notice to driver when a system or feature affected by a failure is attempted to be switched “on” or “activated” by driver.

## Slide 11
“Off” to “On” only upon a deliberate action by the driver
“Active” only if:
  Driver’s in the seat and safety belt is fastened
  System is able to monitor driver’s engagement with the driving task
  No failure affecting the safe operation of the system has been detected
  System has not detected to be outside of system boundaries
  Other safety systems are operational
Section 5 – 5.5. Modes of operation
Section 5 – 5.5.3.2 Activation
System can be switched off at any time. When switched off, system to go “off”
If preconditions for activation are no longer met, the system or features shall no longer generate control output by transitioning to “stand-by” or “off”
Automatic deactivation upon a standstill following an emergency intervention.
Section 5 – 5.5.3.3 Deactivation

## Slide 12
Inform the driver on system status, request of the driver to perform a specific action, system boundaries, detected failures, intended driver-confirmed or system-initiated manoeuvres (or sequence)
Signals to be clear, timely and noticeable. Not lead to confusion.
Use combination of visual, audio and/or haptic feedback
Messages and signals should be prioritized if offered in parallel. Safety-relevant messages and signals to be prioritized. Explained by manufacturer
Messages and signals to encourage driver understanding of intended system control outputs
System messages to be unambiguously distinguishable from messages by other assistance or automation systems equipped on the vehicle
Aim to visually communicate deactivation reason
Inform driver on availability of features, and inability to activate a given feature.
[May take into account potential impairments of users]
Section 5 – 5.5.3.4 Driver Override
Section 5 – 5.5.4.1 System Messages and Signals
May remain “active” when a driver overrides provided priority is given to the driver’s input
Input to the brakin control higher than system-generated deceleraton or by maintaining the vehicle in standstill, to override longitudinal control function
Accelerator input shall temporarily revert longitudinal control assistance to “stand-by” until end of override
Steering input shall override the steering action. Effort necessary shall not exceed 50 N. May allow minor lateral corrections.

## Slide 13
System to visually inform the driver about upcoming manoeuvres [at least 3 seconds] ahead of their initiation. System to
  Inform driver ahead of time about the sequence of manoeuvres that are upcoming
  Inform the driver of system intent at a given point in time (e.g. notice that system is changing speeds to perform a lane change)
Any notice to clear and easy to understand
Messages and signals aim to avoid driver complacency and misuse
System to be equipped with the means to detect driver disengagement depending on the assistance provided, driving and environmental conditions
Monitor at least physical or visual disengagement using appropriate criteria
If driver detected to be disengaged, warning to be provided
Warning shall guide driver about the required actions to resume appropriate engagement
If the driver continues to be disengaged, he warning shall be escalated. Remains on as long as driver is disengaged or until system deactivation
Continued disengagement triggers unavailability response
Repeated or prolonged driver disengagement may lead to inability to reactivate the system for the start/run cycle
Further requirements under development
Section 5 – 5.5.3.4.1.11 System messages and signals for system-initiated manoeuvres
Section 5 – 5.5.4.2 [Driver Engagement]

## Slide 14
Main requirements maintained (e.g. detailed information materials through documentation, video, website materials), complementing owner’s manual.
Documentation and educational materials not to describe system in a manner that would mislead customer about the capabilities/limits
If system dsigned to assist lane changes on roads where there is no physical separation, system shall implement strategies to ensure that lane change procedure is only performed where there is no oncoming traffic in the target lane
Only permitted to perform lane changes on roads with pedestrians and cyclists if the system is able to reduce the risk of a collision with any vulnerable road user
Time between initiation of the lane change procedure and start of the lane change is only permitted to be extended beyond [7s] where this is not in violation of national traffic rules, and there is engagement of the driver with the ongoing lane change by looking at the relevant areas of road ahead, to the side, or looking to the vehicle’s mirrors.
Section 5 – 5.5.5 Driver Information Materials
Section 6 – 6.1.1 Advanced Driver-initiated lane change

## Slide 15
Relevant to manoeuvres where the vehicle selects a lane, enters into or takes a roundabout exit, leads vehicle to leave its lane of travel when this is no a lane change, leads the vehicle to take a turn, leads the vehicle to depart or arrive at a parked position, other
System and signals for system-initiated manoeuvres applies. System to ensure driver has sufficient time to confirm.
Request to be indicated through a visual and audible signal
Cannot proceed if request is not confirmed. If so, continue on lane of travel or request resumption of control
Aim to respond to vehicles, road users, infrastructure and a blocked path ahead within or to be in planned trajectory
Aim to respond to traffic lights, stop signs, right-of-way infrastructure and restricted lanes.
Aim to safely and cautiously navigate hillcrests where relevant for the manoeuvre
Aim to respond appropriately to road users and infrastructure where VRUs cross the lane of travel
Detailed activation requirements
Further review through master document
Section 5 – 6.1.2 Other driver-initiated manoeuvres

## Slide 16
Text adjusted from ALKS
Consideration of adjusted parameters for the assessment of the target lane for a regular lane change, in consideration of different lane characteristics in e.g. urban environments. To be declared by the manufacturer
Section 5 – 6.2.2 System-initiated lane changes
Similarity to driver-initiated manoeuvres
More extensive, stringent national traffic rule compliance obligations
More extensive detect and response requirements
Any manoeuvre to be indicated to other traffic
System cannot be initiated if manoeuvre would cause other road users to unreasonable decelerate/evade
Further review through master document
Section 5 – 6.2.3 Other System-initiated Manoeuvres

## Slide 17
DCAS Multi-Pillar Assessment – In-Service
Monitoring
Periodic Reporting to the Approval Authority
Occurrence | Periodic Reporting [1 Year]
1.a. Safety-critical occurrences known to the DCAS manufacturer | X
1.b. Aggregated distance driven with Paragraph 6 features switched on or active | X
2.a. Detection of prolonged driver disengagement, resulting in a warning cascade | X
2.b. Activation of an emergency system, such as a Risk Mitigation Function, due to the continuous driver disengagement | X
3.a Detected system-level failures resulting in the unavailability of DCAS | X
3.b Detected DCAS-deactivations without prior warning to the driver | X
3.c Detected driver response to system deactivation | X
Example List of ccurrences, list to be agreed with authority
Manufacturer must maintain processes to monitor safety-critical occurrences resulting from DCAS operation
Manufacturer must notify Authority without undue delay of any severe accidents where DCAS was on, or active [3] seconds before accident, resulting in:
  Deployment of airbags and/or restraints
  Activation of emergency systems
Any safety-critical occurence within system boundaries which may impact the broader safe use of DCAS, must be investigated and notified to the Authority (incl. applicable remediations)
Approval Authority shall have authority to request investigation results from the manufacturer [within 6 months of the occurence or accident] subject to national rules

## Slide 18
New: System Information Data (Section 9) & Declaration of system capability (Annex 3, Appendix 4)
New obligation, in addition to CEL Audit, for manufacturer to declare in detail the system and features permitting detailed assessment/verification. (May be restructured)
Section 9: Aimed to outline system characteristics
Specific features on the system according to paragraph 6
Conditions for activation & System boundaries
DCAS interaction with other vehicle systems
Means for activation, deactivation and override
Criteria monitored and means to determine sufficient driver engagement
Annex 3, Appendix 4: Aimed to outline system/feature performance to support testing
Operating Ranges of each feature
Operating Domain of each feature
System capability to respond to other road users
System capability to follow the course of the lane
System’s ability to ensure safe operation when assisting lane changes
System’s ability to operate in accordance to traffic rules for a certain manoeuvre

## Slide 19
Section 10 – Requirements for Software Identification and Cyber Security
RXSWIN may be implemented, if so must comply with UN Regulation No. 156 (based on RE.3)
System compliance with UN Regulation No.156 to be evidenced

## Slide 20
Main Open decision points for TF ADAS consideration reflecting conflicting proposals
5.3.8.2 Speed Limit Compliance Assistance:
Is the driver allowed to set a system speed limit above the system-determined speed limit?
Option 1 – SDG preferred: [Allow driver to set a system maximum speed at any time (e.g. in the context of system misidentified speed-limit]
Option 2 – ETSC preferred: [System shall not allow the driver to set a maximum speed above the system-determined speed limit]
5.4 Failure Indication: Should a failure affecting a feature be indicated constantly during DCAS operation, or when system is switched on?
Option 1 - Industry preferred: [Notice of failure is provided when system is switched on. Failure/inavailability notice is provided when driver attempts to activate a feature]
Option 2: [Notice of failure is consistently provided upon system being switched on]