## Slide 1: SLR – Stage 2 – Step 2
Achieve technology-neutrality for light sources
as far as possible/reasonable (ref. SLR-52-03/Rev.8)
Philipp Plathner (IEC), Walter Schlager (IEC)
9-August 2023
SLR-63-04
Revision of SLR-62-07/Rev.1

## Slide 2: Introduction
Light Source related changes enforced in R148-01 and R149-01
  All technologies (even unknown) are allowed in all functions, mixing possible
  All concepts (replaceable UN-approved light sources, light source modules, non-replaceable light sources) are allowed in all functions, mixing possible
  Number per function is not limited
  Technology-dependency is kept only where necessary, e.g. for testing
Current installation regulations contain specific requirements related to light source technologies (filaments, LEDs, …)
  Remove/improve these parts – where possible – with the target to have it consistent with R148-01 and R149-01
  Start with R48, use 08 series

## Slide 3: List of topics under consideration (1/3)
topic | example | comment | Proposed solution
Filament (general) | Defined under 2.9.1.4. | Keep definition | -
Gas-discharge (general) | Defined under 2.9.1.5. | Keep definition | -
LED module (general) | Definition under 2.9.1.7. | Keep definition | Consider to rearrange paragraphs  “LED module” as sub-paragraph of “light source module”
Gas-discharge (ballast) | 2.9.2.1. | Technology-dependency needed | -
LED module (objective luminous flux) | 2.10.1. (b) … | The value of the objective luminous flux is relevant for all kind of modules | Replace LED module by light source module. Rename (a) to “UN approved …” and introduce case (c) for non-replaceable LS.
LED module (replaceability) | 5.29. LED modules are not required to be replaceable | Technology-dependency based on typical lifetime. Remark: Consider to allow only replaceable light source modules, as non-replaceable ones could be considered as non-replaceable light sources. | “Light source modules need to be replaceable; however LED modules do not need to be replaceable, if so stated in the communication sheet of the component type approval.”

## Slide 4: List of topics under consideration (2/3)
topic | example | comment | Proposed solution
LED module | 5.31. … | In a listing of “light source modules, LED modules and …” it is needless to mention LED modules, as they are covered by light source modules | Delete “LED modules”. Note: is the second sentence in 5.31. meaningful and needed?
Gas-discharge (switching) | 6.2.7.3. and 6.22.7.2. (c) | Technology-dependency needed | -
LED module + number of additional light sources | 6.2.7.4. | Make consistent with R149-01 | Allow more than one light source and replace LED module by light source module
LED module / tell-tale mandatory | 6.2.8.2. | Make consistent with R149-01 | Replace LED module by light source module and introduce light source option.
Headlamp cleaning | 6.2.9.2. … | Still technology-dependent | Replace “LED module(s)” by “light source module(s)”. Add plural to “light source(s)”.

## Slide 5: List of topics under consideration (3/3)
topic | example | comment | Proposed solution
Levelling (manual vs. automatic) | 6.2.9.3. … | Up to 08-series there is discrimination of light source technology/performance | Replace “LED module(s)” by “light source module(s)”. Add plural to “light source(s)”. Note: Recently, GRE adopted 09-series with technology-neutral levelling requirement.
Filament “lamps” (test voltages) | 6.2.9.3. | Today it covers H9 and L1, but it should become future-proof | Make it technology-neutral for all “UN approved light sources”
Filament light sources (specific flashing cond.) | 6.23.7.1.1., 6.23.9.1. and 6.25.7.1.1. | Technology-dependency needed | -